## Slide 1: Final Exam Review
Haonan Wang
CMPE 200 Computer Architecture & Design

## Slide 2: Final Exam Composition
Multiple-choice Single-answer: 3 points * 10 = 30
Multiple-choice Multiple-answer: 4 points (wrong option -4, missing option -2) * 5 = 20
True or False: 2 points * 9 = 18
Questions & Answers: 8 points (steps 6 + answer 2) * 4 = 32
Bonus question: 10 points * 2 = 20
Total = 30 + 20 + 18 + 32 + 20 = 100 + 20
  If you get more than 100 points, the excessive points will be used to improved your overall grade.
Exam settings:
  Time: Thursday, Dec. 8th, 12:15 - 14:30 @ CLARK 222 with LockDown Browser
  Closed book (but you can print out the MIPS data card and use it if needed)
  Cheat sheet (handwritten): A4 paper * 2 allowed, pictures of all sides must be submitted before the exam
  Use of calculator and scratch paper allowed
  Double-check your laptop and turn off your cellphone before the exam
  Submit your answers on time (otherwise score will not be counted)!

## Slide 3: Processor Interface Mechanisms
Two ways for processors to access peripheral devices:
  Port-mapped I/O (PMIO): isolated I/O, special I/O instructions, separate address spaces
  Memory-mapped I/O (MMIO): one address space
MIPS processors use memory-mapped I/O
  Use load and store instructions to communicate with peripheral devices
  For a MIPS processor that only supports lw and sw, all data transfer will be 32 bits

## Slide 4: Processor Interface Mechanisms
Two ways to communicate with CPU:
  Polling: The CPU polls the device periodically
  Interrupt: The I/O device calls the CPU actively
Two ways for data transfer between the memory and I/O:
  CPU controlled
  Direct Memory Access (DMA)

## Slide 5: Why?
Two Types of Locality:
  Temporal Locality (Locality in Time): If an address is referenced, it tends to be referenced again (e.g., loops, reuse)
  Spatial Locality (Locality in Space): If an address is referenced, neighboring addresses tend to be referenced (e.g., array, stack, etc.)
On-chip
Off-chip

## Slide 6: Cache Hit and Miss
Hit: Data appears in some block of the cache
  Hit Rate: # hits / total accesses on the cache
  Hit Time: Time to access the cache
Miss: Data needs to be retrieved from the lower level (and stored in cache)
  Miss Rate: 1 - (Hit Rate)
  Miss Penalty: Average delay in the processor caused by each miss
Lower Level Memory
(cache/main memory)
Cache
To Processor
From Processor
data block X
data block Y
Can’t find!
Miss
Hit
Hit
read
read

## Slide 7: Reducing Penalty: Multi-Level Cache
AMAT in multi-level cache organization
  = Thit(L1) + Miss_rate(L1) x
  [ Thit(L2) + Miss_rate(L2) x
  { Thit(L3) + Miss_rate(L3) x T(memory) } ]
Example:
  Miss rate of L1, L2, L3 = 10%, 5%, 1%, respectively
  AMAT = 1 + 0.1 x [ 10 + 0.05 x { 20 + 0.01 x 300 } ] = 2.115 cycles
Second
Level
Cache
Third
Level
Cache
300 cycles
20 cycles
10 cycles
On Processor Die
L1
L2
L3
First-level
Cache
Hit Time
1 cycle
Vs. 31 cycles
14.7x speedup!
Main
Memory
(DRAM)
Off-Chip

## Slide 8: Measuring Performance with Caches
Note: this is miss ratio with regard to all instructions
= read ratio * cache miss rate
Assuming cache hit costs are included as part of the normal CPU execution cycle, then
  CPU time = IC × CPI × CP
  = IC × (CPIideal + Memory-stall cycles) × CP
CPIstall
Memory-stall cycles come from cache misses (a sum of read-stalls and write-stalls)
  Read-stall cycles = read miss ratio × read miss penalty
  Write-stall cycles = write miss ratio × write miss penalty + write buffer stalls
For write-through caches, we can simplify this to
  Memory-stall cycles = miss ratio × miss penalty

## Slide 9: Impacts of Cache Performance
Relative cache penalty increases as processor performance improves (faster clock rate and/or lower CPI)
  The memory speed is unlikely to improve as fast as processor cycle time. When calculating CPIstall, the cache miss penalty is measured in processor clock cycles needed to handle a miss
  The lower the CPIideal, the higher the impact of stalls
Example: A processor with a CPIideal of 2, a 100 cycle miss penalty, 36% load/store instructions, and 2% I$ and 4% D$ miss rates
  Memory-stall cycles = 2% × 100 + 36% × 4% × 100 = 3.44
  CPIstalls = 2 + 3.44 = 5.44
What if the CPIideal is reduced to 1? Or the processor clock rate is doubled (doubling the miss penalty)?

## Slide 10: Cache Types
N-way Set-Associative: Number of ways > 1 & Number of sets > 1
  Slightly complex searching mechanism
Direct Mapped: Number of ways = 1
  Fast indexing mechanism
Fully-Associative: Number of sets = 1
  Extensive hardware resources required to search
Block offset
Byte offset
Index
Tag
Decreasing associativity
Fully associative (only one set)
Direct mapped (only one way)
Increasing associativity
Selects the set
Used for tag compare
Selects the word in the block
Assuming fixed sized cache:
Way 0
Way 1
Set 0
Set 1
block 0
block 1
block 2
block 3
…
…

## Slide 11: Four-Way Set Associative Cache
31 30 . . . 11 10 9 . . . 2 1 0
Byte offset
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Index
Data
Tag
V
0
1
2
.
.
.
253
254
255
8
Index
22
Tag
Hit
Data
32
4x1 select

## Slide 12: Cache Miss Classification: The 3 C’s
Compulsory (cold) Misses
  On the 1st reference to a block
  Related to # blocks accessed by a code, not related to the configuration of a cache
Capacity Misses
  The program’s working set size exceeds the cache capacity
Conflict Misses
  Multiple memory blocks map to the same set in set-associative caches

## Slide 13: Cache Policies: Cases - Revisit
Allocation policy: do we allocate a block in cache for the missed data?
Read policies:
  Read Hit: this is what we want. Only one data read from the cache.
  Read Miss: needs to fetch from lower level, but just write to the register once after that
    read-allocate (with replacement policy) vs. no-read-allocate (i.e., cache bypassing)
Write policies (only for the data cache): consistency & performance tradeoffs
  Write Hit: behavior and number of writes depends on write policy
    Write-through vs. write-back vs. write-evict
  Write Miss: needs to first read from lower level, then apply write policies
    Write-allocate (with replacement policy): Write-through vs. Write-back
    No-write-allocate (bypassing): Write-evict
What else must be considered?
+ write policy of evicted data
+ write policy of evicted data

## Slide 14: Cache Miss Behavior Analysis
Read miss:
  +Write-through: evict victim block + fetch block from lower level
  +Write-back: evict victim block + write back evicted block if dirty + fetch block from lower level
  +No-write: find victim block + fetch block from lower level
Write miss:
  Write-allocate:
    +Write-through: evict victim block + fetch block from lower level + store word to block + store word to lower level
    +Write-back: evict victim block + write back evicted block if dirty + fetch block from lower level + store word to block
  No-write-allocate: +Write-evict: store word to lower level directly

## Slide 15: Reduce Miss Rate (1): Code Optimization
Misses occur if sequentially accessed array elements come from different cache blocks
Code optimizations  No hardware change
  Rely on programmers or compilers
Examples:
  Loop interchange: In nested loops, outer loop becomes inner loop and vice versa
  Loop blocking: partition large array into smaller blocks, thus fitting the accessed array elements into cache size

## Slide 16: Reduce Miss Rate (2): Reduce the 3 C’s
Increase Cache Size
  Reduce miss for: capacity miss, conflict miss
  But has many limitations
Increase Associativity
  Reduce miss for: conflict miss
  But may increase access latency
Increase Cache Block Size
  Reduce miss for: compulsory
  But may increase miss penalty (more data will be evicted and fetched)
  Very large blocks could increase miss rate

## Slide 17: Reduce Miss Rate (4): Multi-level Caches
Having a unified L2 cache (i.e., it holds both instructions and data) and in some cases even a unified L3 cache
L1 cache should focus on minimizing hit time in support of a shorter clock cycle
Secondary cache(s) should focus on reducing miss rate to reduce the penalty of long main memory access times

## Slide 18: DRAM Subsystem Organization
  Dram: Dynamic RAM
DRAM Organization:
Channel
DIMM
Rank
Chip
Bank
Row/Column
Channel: Independent memory subsystem
  E.g., 2 independent Channels:

## Slide 19: DRAM Design 2: Synchronous DRAMs
Like page mode DRAMs, synchronous DRAMs (SDRAMs) can transfer a burst of data from a series of sequential addresses in the same row
For words in the same burst, don’t have to provide the complete (row and column) addresses
  The entire row is loaded into a row buffer (SRAM).
  Specify the starting (row+column) address and the burst length (burst must be in the same row).
  Data words in the burst are then accessed from that SRAM under control of a clock signal.

## Slide 20
DDR (Double Data Rate) SDRAMs
DDR1 VS DDR1+:
DDR2 vs. QDR

## Slide 21
Row Buffer
(Row 0, Column 0)
Row decoder
Column mux
Row address 0
Column address 0
Data
Row 0
Empty
(Row 0, Column 1)
Column address 1
(Row 1, Column 0)
HIT
Row address 1
Row 1
Column address 0
CONFLICT !
Columns
Rows
Access Address: Row Operation:
R0
R0
R1
Activation
Restore, Precharge, Activation
No operation
RBL=2
RBL=1
Credit: Onur Mutlu.
Row Operations & Row Buffer Locality
Improving Row Buffer Locality (RBL) is the key to improve DRAM efficiency

## Slide 22
……
Activation Counter:
R1: Activation = 1
R5: Activation = 2
R1: Activation = 3
R5: Activation = 4
R5: Activation = 4
Avg RBL = 5 / 4 = 1.25
……
requests currently
in the pending queue
oldest
request
R1
R5
R1
R5
future
requests
R2
R4
R3
In-order scheduling
(FIFO):
Request Stream
R5
……
Activation Counter:
R1: Activation = 1
R1: Activation = 1
R5: Activation = 2
R5: Activation = 2
R5: Activation = 2
Avg RBL = 5 / 2 = 2.5
……
requests currently
in the pending queue
oldest
request
R1
R5
R1
R5
future
requests
R2
R4
R3
Out-of-order scheduling
(FR-FCFS):
Request Stream
R5
Visible to the memory scheduler
Same
activation
Same
activation
Same
activation
RBL & Memory Scheduling Schemes

## Slide 23
  Rotational latency: wait for the desired sector to rotate under the head
    ½ of 1/RPM converted to ms: 0.5R/5400RPM = 5.6ms to 0.5R/15000RPM = 2.0ms
  Transfer time: transfer a block of bits (one or more sectors) under the head to the disk controller’s cache (70 to 125 MB/s are typical disk transfer rates)
    the disk controller’s “cache” takes advantage of spatial locality in disk accesses
    cache transfer rates are much faster (e.g., 375 MB/s)
  Controller time: the overhead the disk controller imposes in performing a disk I/O access (typically < 0.2 ms)
Sector
Track
Cylinder
Head
Platter
Controller
+
Cache
Magnetic Disk Characteristic
  Seek time: position the head over the proper track
    3 to 12/15 ms on average
    Due to locality of disk references, the actual average seek time may be only 25% to 33% of the advertised number

## Slide 24: Typical Disk Access Time
  If the measured average seek time is 25% of the advertised average seek time, then
Avg disk read/write
= 4.0 ms + 0.5/(15,000RPM/(60sec/min)) + 0.5KB/(100MB/sec) + 0.2 ms
= 4.0 + 2.0 + 0.005 + 0.2 = 6.2 ms
Avg disk read/write = 1.0 + 2.0 + 0.005 + 0.2 = 3.2 ms
The average time to read or write a 512B sector for a disk rotating at 15,000 RPM with average seek time of 4 ms, a 100MB/sec transfer rate, and a 0.2 ms controller overhead

## Slide 25: Address Translation Mechanisms
Physical page
base addr
Main memory
Disk storage
Virtual page #
V
1
1
1
1
1
1
0
1
0
1
0
Page Table (in main memory)
Offset
Physical page #
Offset
Page table register
virtual address
physical address
Page walk: Search (walk) the page table
Page fault: a DRAM miss for the page
 Page in disk

## Slide 26: A TLB in the Memory Hierarchy
A TLB miss – is it a page fault or merely a TLB miss?
  If the page is loaded into main memory, then the TLB miss can be handled by loading the translation information from the page table into the TLB (10’s of cycles )
  If the page is not in main memory, then it’s a true page fault (1,000,000’s)
TLB misses are much more frequent than true page faults
CPU
TLB
Lookup
Cache
Main
Memory
VA
PA
miss
hit
data
Trans-
lation
hit
miss
¾ t
¼ t

## Slide 27: TLB Event Combinations
TLB | Page Table | Cache | Possible? Under what circumstances?
Hit | Hit | Hit | 
Hit | Hit | Miss | 
Miss | Hit | Hit | 
Miss | Hit | Miss | 
Miss | Miss | Miss | 
Hit | Miss | Miss/ Hit | 
Miss | Miss | Hit | 
Yes – this is what we want!
Yes – although the page table is not
checked after the TLB hits
Yes – TLB missed, but PA is in page table and data is in cache
Yes – TLB missed, but PA is in page table, data not in cache
Yes – page fault
No – TLB translation is not possible if the page is not present in main memory
No – data is not allowed in the cache if the
page is not in memory

## Slide 28: Memory Systems that Support Caches
The off-chip interconnect and memory architecture can affect overall system performance in dramatic ways
CPU
Cache
DRAM
Memory
bus
One word wide organization
(one word wide bus & memory)
32-bit data
&
32-bit addr
per cycle
on-chip
Assume:
1 memory bus clock cycle to send the address
15 memory bus clock cycles to get the 1st word in the block from DRAM (row cycle time), 5 memory bus clock cycles for 2nd, 3rd, 4th words (column access time)
1 memory bus clock cycle to return a word of data
Memory-Bus to Cache bandwidth
number of bytes accessed from memory and transferred to cache/CPU per memory bus clock cycle

## Slide 29
If the block size is one word, then for a cache miss, the pipeline will have to stall for:
  memory bus clock cycle to send address
  memory bus clock cycles to read DRAM
  memory bus clock cycle to return data
  total clock cycles miss penalty
Number of bytes transferred per clock cycle (bandwidth) for a single miss is
  bytes per memory bus clock cycle
  1
  15
  1
  17
  4 / 17 = 0.235
One Word Wide Bus, One Word Blocks
CPU
Cache
DRAM
Memory
bus
One word wide organization
(one word wide bus & memory)
32-bit data
&
32-bit addr
per cycle
on-chip

## Slide 30
What if the block size is four words and each word is in a different DRAM row?
  cycle to send 1st address
  cycles to read DRAM
  cycles to return last data word
  total clock cycles miss penalty
Number of bytes transferred per clock cycle (bandwidth) for a single miss is
  bytes per memory bus clock cycle
1
  4 x 15 = 60
  1
  62
  (4 x 4) / 62 = 0.258
One Word Wide Bus, Four Word Blocks
CPU
Cache
DRAM
Memory
bus
One word wide organization
(one word wide bus & memory)
32-bit data
&
32-bit addr
per cycle
on-chip

## Slide 31
What if the block size is four words and all words are in the same DRAM row?
  cycle to send 1st address
  cycles to read DRAM
  cycles to return last data word
  total clock cycles miss penalty
Number of bytes transferred per clock cycle (bandwidth) for a single miss is
  bytes per memory bus clock cycle
1
15 + 3 x 5 = 30
1
  32
  (4 x 4) / 32 = 0.5
CPU
Cache
DRAM
Memory
bus
One word wide organization
(one word wide bus & memory)
32-bit data
&
32-bit addr
per cycle
on-chip
One Word Wide Bus, Four Word Blocks

## Slide 32
For a block size of four words
  cycle to send 1st address
  cycles to read DRAM banks
  cycles to return last data word
  total clock cycles miss penalty
CPU
Cache
bus
on-chip
Number of bytes transferred per clock cycle (bandwidth) for a single miss is
  bytes per memory bus clock cycle
  (4 x 4) / 20 = 0.8
1
15
  4 x 1 = 4
  20
DRAM
Memory
bank 1
DRAM
Memory
bank 0
DRAM
Memory
bank 2
DRAM
Memory
bank 3
Interleaved Memory, One Word Wide Bus
  What about interleaving channels?

## Slide 33: Can We Do Better?
Latency vs. throughput
Levels of Parallelism:
  Instruction-level Parallelism (ILP)
    Executing independent instructions (in one thread) in parallel
  Data-level Parallelism (DLP)
    Executing the same instruction on different data subsets
  Thread-level Parallelism (or Task-level Parallelism, TLP)
    Executing independent computing tasks in parallel (on same or different data)

## Slide 34: Dynamic Pipeline Scheduling
Challenges
  All data hazards (memory and registers) must be resolved by hardware
Data Dependencies
  RAW (Read After Write) : True dependency
    Dynamic pipeline preserves only this dependency
  WAR (Write After Read) & WAW (Write After Write) : False dependencies
    Dynamic pipeline removes false dependencies by using register renaming

## Slide 35: Dependencies Among Instructions
lw $t0, 20($s2) addu $t1, $t0, $t2 sub $s2, $s4, $t3 slti $t0, $s2, 20
P2
P3
P3
P1
P1
P4
lw P1, 20($s2) addu P2, P1, $t2 sub P3, $s4, $t3 slti P4, P3, 20
Logical | initial | lw | addu | sub | slti
l1 | t0 | P1 | P1 | P1 | P4
l2 | t1 | t1 | P2 | P2 | P2
l3 | t2 | t2 | t2 | t2 | t2
l4 | t3 | t3 | t3 | t3 | t3
l5 | s2 | s2 | s2 | P3 | P3
l6 | s4 | s4 | s4 | s4 | s4
initial | lw | addu | sub | slti
P1 | P2 | P3 | P4 | P5
P2 | P3 | P4 | P5 | …
P3 | P4 | P5 | … | 
P4 | P5 | … |  | 
P5 | … |  |  | 
Mapping table status
Free list status

## Slide 36
Shared Memory multi-Processor (SMP)
  Single address space shared by all cores
  Cores coordinate/communicate through shared variables (via loads and stores)
    Need synchronization primitives (e.g., locks)
  Two styles
    Uniform memory access (UMA): easier for programming
    Non-uniform memory access (NUMA): more scalable & lower latency to local memory
Message Passing multi-Processors (MPP)
  Each core has its own private address space
    Cores share data by explicitly sending and receiving information (message passing)
  Coordination is built into MP primitives (message send & message receive)
How to Share Data?

## Slide 37: Cache Coherence Methods
Snooping-based protocol
  Each processor’s cache controller constantly snoops on the bus
  Processors observe other processors’ actions
    E.g., processor A makes “read-exclusive” request for A on bus, processor B sees this and invalidates its own copy of A
Interconnection Network
Memory
P
$
P
$
...
Snooper
P
$
P
$
Snooper
Snooper
Snooper
I’m going to modify block X
X
X
X
invalidate X
invalidate X

## Slide 38: Cache Coherence Methods
Directory-based protocol
  Directory tracks ownership (sharer set) for each block (who has what)
    A modified bit and multiple presence bits per cache block
  Directory coordinates invalidation appropriately
    E.g., processor A asks directory for “read-exclusive” copy, directory asks processor B to invalidate the requested copy, waits for ACK from processor B, then responds to processor A
Interconnection Network
Memory
P
$
P
$
P
$
P
$
...
Directory
Presence bits, one bit for each processor
Modified bit
X
X
X
I’m going to modify block X
Invalidate X
Done
Done
OK
0

## Slide 39
Load balancing is another important factor
  E.g., a single core with twice the load of the others cuts the speedup almost in half
S = serial part, W = parallel part, N cores
  Time on 1 processor is S + W
Suppose the workload is equally distributed and there is no extra overhead to accumulate partial results
  Time on N processors is S + W/N
Suppose the workload is almost equally distributed (and still no overhead)
  One core does 2(W/N), one does nothing, most do W/N
  Time is S + max(2(W/N), 0, W/N) = S + 2(W/N) = S + W/(N/2)
Load Balancing

## Slide 40: Multi-core CPUs, Multiprocessors, and GPUs
Multi-core CPUs, Multiprocessors
  Individual cores are fine-tuned for high ILP
  Good for Task-level parallelism (TLP)
  However, it is hard to employ hundreds of cores in one system
    Cache coherence, control, power, cost …
For specific tasks, Graphics Processing Unit (GPU) can be an alternative solution
  For tasks with high Data-Level parallelism
  E.g., particle simulation, image/video processing, games, machine learning …
  The usage of GPU is common now
Instruction & Data level parallelism combinations
  SISD: Classical Von Neumann machine
  MISD: NA
  SIMD: GPU
  MIMD: multi-core & multiprocessor

## Slide 41: Why is GPU so Efficient?
GPU is specialized for compute-intensive, highly data parallel computation (owing to its graphics rendering origin)
  More transistors can be devoted to data processing rather than caching and control
  At peak performance GPU uses order of magnitude less energy per operation than CPU
  Working with suitable applications: high arithmetic intensity (the ratio between arithmetic operations and memory operations), high DLP, not too sensitive to latency
Credit: Dan Negrut, ME964 UW-Madison

## Slide 42: Classical GPGPU Architecture (Nvidia)
Warp Scheduler
Threads
Interconnect
…
…
L1 Caches
SM/Core
L1 Caches
PE
PE
…
L2 Cache
DRAM
Module
Memory Controller
L2 Cache
Memory Controller
L2 Cache
Memory Controller
DRAM
Module
DRAM
Module
Register File
Register File
SM/Core
PE
PE
…
Memory
Partition
W
W
W
W
W
W
warps
Row open:
Activation
Row close:
Restore & Precharge
Memory Array
Row Buffer
Warp contains 32 threads that execute the same instruction with different data - SIMD

## Slide 43: Multicore Performance: Amdahl’s Law
Speedup due to enhancement E:
Speedup w/ E = ----------------------
Exec time w/o E
Exec time w/ E
ExTime w/ E = ExTime w/o E  ((1-F) + F/S)
Speedup w/ E = 1 / ((1-F) + F/S)
Suppose that enhancement E accelerates a fraction F (F <1) of the task by a factor S (S>1) and the remainder of the task is unaffected:

## Slide 44
Consider an enhancement that runs 20 times faster but is only usable 25% of the time
Speedup w/ E = 1/(.75 + .25/20) = 1.31
What if its usable only 15% of the time?
Speedup w/ E = 1/(.85 + .15/20) = 1.17
Amdahl’s Law tells us that to achieve linear speedup with 100 cores, none of the original computation can be scalar!
To get a speedup of 90 from 100 cores, the percentage of the original program that could be scalar would have to be 0.1% or less
  Speedup w/ E = 1/(.001 + .999/100) = 90.99
Example 1: Amdahl’s Law
Speedup w/ E = 1 / ((1-F) + F/S)

## Slide 45
Consider summing 10 scalar variables and two 10 by 10 matrices on 10 cores
Speedup w/ E = 1/(.091 + .909/10) = 1/0.1819 = 5.5
What if there are 100 cores?
Speedup w/ E = 1/(.091 + .909/100) = 1/0.10009 = 10.0
What if the matrices are 100 by 100 (or 10,010 adds in total) on 10 cores?
Speedup w/ E = 1/(.001 + .999/10) = 1/0.1009 = 9.9
What if there are 100 cores?
Speedup w/ E = 1/(.001 + .999/100) = 1/0.01099 = 91
Speedup w/ E = 1 / ((1-F) + F/S)
Example 2: Amdahl’s Law

## Slide 46: Other Important Points
Review the first half with midterm review slides and exam questions!
Processor review quiz
Extra review session (online): 15:00 – 16:15 PM, Sunday, Dec. 4th
  Check announcements on Canvas
Extra Office hour (online): 15:00 – 16:15 PM, Wednesday, Dec. 7th
  Check announcements on Canvas
You do not have to know everything in the textbook. However, any content covered in the lecture could appear in the exam. The review slides do not cover everything.
Do not leave it blank!

## Slide 47: Good Luck!
I will be available for questions via Email/Canvas/Slack/Zoom
Interested in GPUs?
  Spring 2023: CMPE214 GPU Architecture and Programming
Grader & Research opportunities
  Yes, you are readily prepared!
  Funded opportunity: RA position for outstanding students
  MS Thesis & MS projects
Course Evaluation: Please participate before Dec 7, 2022
  You should have received an E-mail, or you can find it on Canvas in the SOTE/SOLATE tab
  Feel free to send me feedback directly!
Thank you!