## Slide 1: Midterm Review (1)
Haonan Wang
CMPE 200 Computer Architecture & Design

## Slide 2: Midterm Exam Composition
Multiple-choice Single-answer: 4 points * 8 = 32
Multiple-choice Multiple-answer: 6 points (wrong or missing option -3) * 4 = 24
True or False: 3 points * 8 = 24
Questions & Answers: 10 points (steps 8 + answer 2) * 2 = 20
Bonus question: 10 points * 1 = 10
Total = 32 + 24 + 24 + 20 + 10 = 100 + 10
  If you get more than 100 points, the excessive points will be used to improved your overall grade.
Exam settings:
  Time: Monday, Oct 19, 15:00 - 16:15 @ Clark 222 with LockDown Browser
  Closed book (but you can print out the MIPS data card and use it if needed)
  Cheat sheet (handwritten): A4 paper * 1 allowed, pictures of both sides must be submitted before the exam
  Use of calculator and scratch paper allowed
  Double-check your laptop and turn off your cellphone before the exam

## Slide 3: Relative Performance
Define Performance = 1/Execution Time
“X is n times faster than Y”
Example: time taken to run a program -- 10s on a computer A, 15s on computer B
Execution TimeB / Execution TimeA = 15s / 10s = 1.5
A is 1.5 times faster than B.

## Slide 4: Example: Average CPI
Instruction Type | Integer | Floating point | Branch | Load/ Store
CPI for type | 1 | 2 | 4 | 3
Instruction Count in program A | 50 | 10 | 10 | 10
Instruction Count in program B | 20 | 0 | 10 | 10
Program A: Total Instructions = 80
Clock Cycles = 50×1 + 10×2 + 10×4 + 10x3 = 140
Avg. CPI = 140/80 = 1.75
CPU time (if Clock period = 100 ps)
  = 1.75 x 80 x 100ps = 14000 ps = 14ns
Program B: Total Instructions = 40
Clock Cycles = 20×1 + 10×4 + 10×3 = 90
Avg. CPI = 90/40 = 2.25
CPU time (if Clock period = 100 ps)
  = 2.25 x 40 x 100ps = 9000 ps = 9ns

## Slide 5: Throughput
Pipeline IPC | N / (N+K-1)
Let n → ∞ (n = infinity) | 1
Throughput (T) = # of instructions executed / time
IPC = Instruction Per Cycle = 1 / CPI
  For a large number of instructions, the IPC of a pipelined processor is 1 instruction per clock cycle
  Only when we keep the pipeline full of instructions
Assume we execute N instructions using a K stage datapath

## Slide 6: Byte-oriented vs. Word-oriented Memory
Most processors are byte-oriented
  Can access a word from any byte address
MIPS: Word-oriented
  Words must be aligned to multiples of 4
  Not word-addressable!
  Provides some simplicity in design
Logical views can be arranged in rows of 4-bytes for word-oriented memories
Proc
Mem
A
D
/
32
/
32
…
12
F3
3B
0x00002
0x00001
0x00000
Logical Byte-Oriented View of Mem
12
F3
3B
7C
47
13
00
8E
…
0x00008
0x00004
0x00000
Logical Word-Oriented View

## Slide 7: Tips to Remember Endianness
Looks normal (same as writing order) when address is from low to high
Looks strange here
But same as writing order when address is from high to low
word value:
Little-Endian
0 x 1 2 3 4 5 6 7 8
78
0x03
56
34
0x02
0x01
12
0x00
12
0x00
34
56
0x01
0x02
78
0x03
34
56
78
12
…
0x00004
0x00000
Logical Word-Oriented View

## Slide 8: Signed vs. Unsigned Instructions
Other instructions also have unsigned versions
  addu, addiu, subu, divu, multu, …
Example:
  Assume that $2 = 0xFFFFFFFF, $3 = 0x00000001, what is $1?
  slt $1, $2, $3 # signed set less than
  # -1 < +1  $1 = 1
  sltu $1, $2, $3 # unsigned set less than
  # +4,294,967,295 > +1  $1 = 0

## Slide 9: Instruction Formats
0
rs
rt
rd
shamt
funct
31:26
5:0
25:21
20:16
15:11
10:6
35 or 43
rs
rt
address
31:26
25:21
20:16
15:0
4
rs
rt
address
31:26
25:21
20:16
15:0
R-type
Load/ Store
(I-type)
Branch
(I-type)
opcode
always read
read, except for load
write for R-type and load
sign-extend and add
different ALU instructions

## Slide 10: Branch Target Addressing
Why branch’s next instruction should be considered?
  Because MIPS increments program counter (PC) by 4 before executing an instruction
  This already incremented PC value is used for branch target address calculation
Branch Target Address Calculation
  Target address = branch’s next instruction address + offset x 4
  bne $t0, $s5, Exit
    Exit (0x00080018) = addi address (0x00080010) + distance (2) x 4 byte/inst
  b Loop
    Loop (0x00080000) = Exit address (0x00080018) + distance (-6) x 4 byte/inst
80000 | Loop: sll $t1, $s3, 2
80004 | add $t1, $t1, $s6
80008 | lw $t0, 0($t1)
8000C | bne $t0, $s5, Exit
80010 | addi $s3, $s3, 1
80014 | b Loop
80018 | Exit: …

## Slide 11: Loading an Immediate
What if you want to load an immediate value to a register?
If immediate (constant) is 16 bits or less
  Use ori or addi instruction with $0 register
  Examples : You want to load value 1 to $2
    addi $2, $0, 1 // R[2] = 0 + 1 = 1
    ori $2, $0, 0x1 // R[2] = 0 | 1 = 1
If immediate is more than 16 bits
  Immediates limited to 16 bits so we must load constant with a 2-instruction sequence using the special LUI (Load Upper Immediate) instruction
  To load $2 with 0x12345678
    lui $2, 0x1234
    ori $2, $2, 0x5678
12340000
R[2]
12345678
R[2]
OR 00005678
LUI
ORI
LUI: the immediate value is loaded to the MSB 16 bits of the target register

## Slide 12: Jump Target Addressing
Jump instruction provides larger scale jump than branch
Target address = First 4 bits of jump’s next instruction address : Last 28 bits of (target x 4)
Example: j Loop (0x00080000)
  The first 4 bits of Exit = 0x0
  Last 28 bits of target x 4 = 0080000
  target = 0x0020000
00080000 | Loop: sll $t1, $s3, 2
00080004 | add $t1, $t1, $s6
00080008 | lw $t0, 0($t1)
0008000C | bne $t0, $s5, Exit
00080010 | addi $s3, $s3, 1
00080014 | j Loop
00080018 | Exit: …
00
Target
PC [31:28]
Target address of Jump
4-bits
26-bits
2-bits
32 bits

## Slide 13: Exercise
Translate the given high-level language code to MIPS assembly.
  Assume that the address of integer variable x and y are in $4 and $1 respectively.
lw $2, 0($4)
lw $3, 0($1)
slt $1, $3, $2
beq $1, $0, Else
add $2, $2, $3
b Next
addi $2, $0, 1
sw $2, 0($4)
if (x > y)
x = x + y; else x = 1;
MIPS
High-level language
Tasks to do:
Load x value to a register
Load y value to another register
Check if y is less than x
If true, run add operation
Else, store 1 to one register
Store the result value to a in memory
Else:
x > y
x <= y
Next:

## Slide 14: Exercise 2
Translate the given high-level language code to MIPS assembly
  Assume that the base address of a char array a is in register $s0
    base address of an array: the address of the first element of the array
  Assume that the value of i is in $t0.
a[i]--;
add $t2, $s0, $t0
lb $t3, 0($t2)
subi $t3, $t3, 1
sb $t3, 0($t2)
MIPS
High-level language
Now we know that the address of a[i] is $s0 + 1byte * i = $s0 + $t0
Is this a valid operation to get one byte from $s0 + $t0?
lb $t1, $t0($s0)
No, because offset should be an immediate value, not a register id
We should change the base address value, not offset value
i.e. new base: $t2 = $s0 + $t0
and then load one byte from 0($t2)

## Slide 15: Less Than Comparisons
To reduce the number of instructions, you can also use slti or sltui instead of slt
  Example: Add numbers from 0 to 9
int sum = 0;
int i;
for (i = 0; i < 10; i++)
{
sum = sum + i;
}
# $s0 = i, $s1 = sum
add $s0, $0, $0
add $s1, $0, $0
addi $t0, $0, 10
for: slt $t1, $s0, $t0
beq $t1, $0, done
add $s1, $s1, $s0
addi $s0, $s0, 1
j for
done:
MIPS
High-level language
# $s0 = i, $s1 = sum
add $s0, $0, $0
add $s1, $0, $0
for: slti $t1, $s0, 10
beq $t1, $0, done
add $s1, $s1, $s0
addi $s0, $s0, 1
j for
done:

## Slide 16: Example: Recursion for 3!
Compiled machine code
…
$sp
0x000000FC
0x000000F8
0x000000F4
0x000000F0
0x000000EC
0x000000E8
0x000000E4
0x000000E0
0x000000DC
…
$a0 (0x3)
$ra
$sp
$a0 (0x2)
$ra
$sp
$a0 (0x1)
$ra
factorial: addi $sp, $sp, -8 # make room
sw $a0, 4($sp) # store input (n)
sw $ra, 0($sp) # store return address
addi $t0, $0, 2 # $t0 = 2
slt $t0, $a0, $t0 # n <= 1?
beq $t0, $0, else # no: go to else (recursion)
addi $v0, $0, 1 # yes: return 1
addi $sp, $sp, 8 # restore $sp
jr $ra # return
else: addi $a0, $a0, -1 # n = n -1
jal factorial # recursive call
lw $ra, 0($sp) # restore return address
lw $a0, 4($sp) # restore input
addi $sp, $sp, 8 # restore $sp
mul $v0, $a0, $v0 # n * factorial(n-1)
jr $ra # return
$sp
$v0 = 1
$sp
$a0 = 2
$v0 = 2 x 1
$sp
$a0 = 3
$v0 = 3 x 2
$v0 = 6

## Slide 17: Single-Cycle CPU Performance Analysis
Critical path for LW = Tpcq_PC + Ti-mem + TRFread + TALU + Td-mem + TMUX + TRFwrite
= (30 + 250 + 150 + 200 + 250 + 25 + 20) ps
= 925 ps
Function Unit | Parameter | Delay (ps)
Register clock-to-Q | Tpcq_PC | 30
MUX | TMUX | 25
Sign-extend | Ts_ext | 25
ALU | TALU | 200
Mem read | Tmem | 250
Register file read | TRFread | 150
Register file write | TRFwrite | 20

## Slide 18: 5-Stage Pipelined CPU
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
IF/ID
ID/EX
EX/MEM
MEM/WB
0
1

## Slide 19: Pipelined Timing
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10 | CC11
LW | IF | ID | EXE | MEM | WB |  |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM | WB |  |  |  | 
SW |  |  |  | IF | ID | EXE | MEM | WB |  |  | 
AND |  |  |  |  | IF | ID | EXE | MEM | WB |  | 
OR |  |  |  |  |  | IF | ID | EXE | MEM | WB | 
XOR |  |  |  |  |  |  | IF | ID | EXE | MEM | WB
Suppose we execute N instructions using a K stage datapath
Total execution cycle: K+N-1 cycles
  K cycle for 1st inst + (N-1) cycles for remaining insts
  Assume we keep the pipeline full
7 Instrs. =
11 clocks (5 + 7 – 1)

## Slide 20: Data Hazards
Read-After-Write (RAW)
  A following instruction reads a result from a previous instruction
Write-After-Read (WAR)
Write-After-Write (WAW)
RAW Example
  LW $t1,4($s0)
  ADD $t5,$t1,$t4
Initial Conditions:
$s0 = 0x10010000
$t1 = 0x0
$t4 = 0x24
After execution values should be:
$t5 = 0x0
00000060
12345678
0x10010000
0x10010004
$s0 = 0x10010000
$t1 = 0x60
$t4 = 0x24
$t5 = 0x84

## Slide 21: Pipeline Latency with Forwarding/Stall
Number of cycles we must stall to execute a dependent instruction:
Instruction that is the dependency source | w/o Forwarding (cycles) | w/ Forwarding (cycles)
LW | 2 | 1
Other instructions that update register file | 2 | 0
Data Hazards Solutions:
  - Hardware: stalling & forwarding
  - Software: compiler -- code reordering

## Slide 22: Forwarding Path
ALU
Res.
D-Cache /
D-Mem
Addr.
Read Data
Write Data
I-Cache / I-MEM
Addr.
Data
PC
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
IF/ID
0
1
EX
M
WB
Control
M
WB
WB
0
1
0
1
2
0
1
2
Forwarding Logic
20:16
15:11
rtE
rdE
rf_waE
25:21
MEM/WB
EX/MEM
rsE
ForwardBE
ForwardAE
rf_waM
rf_waW
Note: Logics for sign extensions and next pc calculation are omitted for simplicity
Hazard detection unit
StallIF
en
StallID
FlushE
ID/EX

## Slide 23: Code Scheduling to Avoid Stalls
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
lw $t1, 0($t0)
lw $t2, 4($t0)
lw $t4, 8($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
stall
stall
5 cycles for the first inst +
6 cycles for the remaining insts +
2 x 1 stall cycles = 13 cycles
Total
execution time
5 cycles for the first inst +
6 cycles for the remaining insts +
0 stall cycles = 11 cycles
Compiler can reorder code to avoid the stalls
C code for A = B + E; C = B + F;

## Slide 24: Control Hazard
Branch outcomes: Taken (T) or Not-Taken (NT)
Not known until late in the pipeline
  Prevents us from fetching future instructions
  Rather than stall, we can predict the outcome and keep fetching
  We only need to correct the pipeline if we guess wrong
Static Predictions
  Predict Taken
  Predict Not Taken
--- beq L1 L2 --- --- --- --- beq L2 L1 ---
T
T
NT
NT

## Slide 25: Early Branch Determination
Target address can be calculated earlier by moving shift-left-2 and Adder
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
IF/ID
ID/EX
EX/MEM
MEM/WB
0
1
=

## Slide 26: Branch Delay Slot
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM | WB |  |  | 
BNE |  |  |  | IF | ID | EXE | MEM | WB |  | 
OR |  |  |  |  | IF | ID | EXE | MEM | WB | 
ADD |  |  |  |  |  | IF | ID | EXE | MEM | WB
SUB |  |  |  |  |  |  | IF | ID | EXE | MEM
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
BNE $a0,$s1,L2 (T)
OR $s0,$t6,$t7
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome
Instruction in the
target address (L2)
No Flush
& Better Performance

## Slide 27: Early Determination w/ Predict NT
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM | WB |  |  | 
OR |  |  |  | IF | ID | EXE | MEM | WB |  | 
BNE |  |  |  |  | IF | ID | EXE | MEM | WB | 
AND |  |  |  |  |  | IF |  |  |  | 
ADD |  |  |  |  |  |  | IF | ID | EXE | MEM
SUB |  |  |  |  |  |  |  | IF | ID | EXE
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $a0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome
Instruction in the
target address (L2)
nop
nop
T!
Flush
nop
nop

## Slide 28: Early Branch Determination: Issues
Target address can be calculated earlier by moving shift-left-2 and Adder
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
IF/ID
ID/EX
EX/MEM
MEM/WB
0
1
=
This may need extra data forwarding and stall
because now the operand value is needed in ID stage (not in EXE stage)

## Slide 29: Early Determination w/ Predict NT
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM | WB |  |  | 
OR |  |  |  | IF | ID | EXE | MEM | WB |  | 
BNE |  |  |  |  | IF | ID | ID | EXE | MEM | WB
AND |  |  |  |  |  | IF | IF |  |  | 
ADD |  |  |  |  |  |  |  | IF | ID | EXE
SUB |  |  |  |  |  |  |  |  | IF | ID
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $s0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome
Instruction in the
target address (L2)
nop
nop
nop
T!
If BNE has dependency with its preceding instruction, OR, one cycle stall is required to get the OR’s result value
 Still better than normal 3 cycle flushing

## Slide 30: Early Branch Determination
Forwarding logic for early branch determination
  ForwardAD = branchD and we_regM and (rsD ≠ 0) and (rf_waM == rsD)
  ForwardBD = branchD and we_regM and (rtD ≠ 0) and (rf_waM == rtD)

## Slide 31: 1-bit Predictor
Each entry of branch prediction buffer is 1-bit (1: Taken, 0: Not Taken)
  The entry value is the latest outcome of the branch
  Next outcome of the branch is predicted based on current value
  Example: Assume that the actual outcomes of the branches at 0xDC04, 0xDC08, and 0xDC20 are untaken, taken, and untaken, respectively
0xDC04 for(i=0;i<10000;i++)
{
0xDC08 if( ( i % 100) == 0 )
tick( );
0xDC20 if( (i % 2) == 0)
even();
}
prediction bit
0
1
0
..
predicted T
predicted NT
predicted NT
Actual result: NT
0
Actual result: NT
1
Actual result: T

## Slide 32: Is 1 bit Enough?
DC04: NNNNNNN ... NNNNNNNNNNT
10,000 iterations
Mis-predictions: 2 / 10,000
NT
TN
DC08: TTTTT ... TNTTTTT … TNTTTTT …
Mis-predictions: 2 / 100
DC20: TNTNTNTNTNTNTNTNTNTNTNTNTNTNT …
Mis-predictions: 2 / 2
Mis-predictions for every
first and last iterations
 99.998% Correct Prediction
98.0% Correct Prediction
0.0% Correct Prediction
10,000 iterations …
NNNNNNNNN …
Not taken and continue to the loop body
Taken to exit the loop

## Slide 33: Using 2-bit History
2-bit Saturating Counter in each branch prediction buffer entry
  Could have more than two bits but two bits cover most patterns (i.e. loops)
0
1
FSM for 1-bit
Prediction
00
01
10
11
FSM for 2-bit
Saturating Counter
Predict NT
Predict T
Transition on T outcome
Transition on NT outcome

## Slide 34: Pipelined CPU Performance Analysis
Critical path = max {
Tpcq + Ti-mem + Tsetup,
2 ( TRFread + Tmux + Teq + TAND + Tmux + Tsetup ),
Tpcq + Tmux + Tmux + TALU + Tsetup,
Tpcq + Tmemread + Tsetup,
2 ( Tpcq + Tmux + TRFwrite )
}
Function Unit | Parameter | Delay (ps)
Register clock-to-Q | Tpcq | 30
Clock setup time | Tsetup | 20
MUX | TMUX | 25
Sign-extend | Ts_ext | 25
ALU | TALU | 200
Mem read | Tmem | 250
AND | TAND | 15
EQ | Teq | 40
Register file read | TRFread | 150
Register file write | TRFwrite | 20
RF write and read need to be finished in the first and second half of each cycle, respectively

## Slide 35: Question: Pipelined CPI
SPECINT2000 benchmark:
  25% loads, 10% stores, 11% branches, 2% jumps, 52% R-type
Assume:
  40% of loads used by next instruction
  25% of branches mispredicted
  All jumps flush next instruction
Average CPI calculation:
  Load/Branch CPI = 1 when no stalling, 2 when stalling
  CPIlw = 1(0.6) + 2(0.4) = 1.4
  CPIbeq = 1(0.75) + 2(0.25) = 1.25
  Overall average CPI = (0.25 x 1.4) + (0.1 x 1) + (0.11 x 1.25) + (0.02 x 2) + (0.52 x 1) = 1.15
Average CPI
  = Total Clock Cycles / Total IC
  = / Total IC
  =

## Slide 36: CPU Performance Comparison
For a program with 100 billion instructions executing on the pipelined MIPS processor under discussion, execution time is
CPU time = # instructions x CPI x cycle time
= (100 x 109) x 1.15 x (550 x 10-12 sec)
= 63 seconds
When we ran the same code on a single-cycle processor, CPU time was 92.5 seconds.
Speedup of pipelined architecture = 92.5 / 63 = 1.47x

## Slide 37: Other Important Points
You do not have to know everything in the textbook. However, any content we have covered during the lecture so far could appear in the exam. If you have followed all our lectures, your hard work will pay off!
Check the exam related info in the exam Module on Canvas.
Good luck!