## Slide 1: Lecture 2. Processor Instruction Set Architecture & Language (1)
Haonan Wang
CMPE 200 Computer Architecture & Design

## Slide 2: Instruction Set Architecture & Microarchitecture
Instruction Set Architecture
  the programmer’s view of the computer, defined by a set of instructions that each specifies an operation and its operand(s)
Microarchitecture
  the way that the ISA is implemented in hardware
Application
Compiler/Libraries
Operating system
Circuits
Semiconductor physics
Instruction Set (ISA)
Microarchitecture

## Slide 3: What Does the ISA Deal With Specifically?
#include <stdio.h>
#include <string.h>
int numbers[2];
void myfunction(void)
{
FILE *fp;
int size = 2;
int sum = 0;
/* Open file for reading */
fp = fopen(“mynumbers.txt", “r");
/* Read and display data */
fread(numbers, sizeof(int), size, fp);
fclose(fp);
sum = numbers[0] + numbers[1];
printf(“Sum = %d\n”, sum);
}
int main (void) {
myfunction();
return(0);
}
Example: a C program that reads
two integer values from “file.txt” file
and prints the sum of them.
Processor
(CPU)
Understands and executes each line of the code.
Uses fast on-chip memories
Memory
(DRAM)
Provides operands to CPU
(*fp, size, sum, numbers[2])
Storage
(HDD)
Provides file inputs and program code
(file.txt)

## Slide 4: Memory Layout
Text: program code
Static data: global variables
  e.g., static variables in C, constant arrays and strings
Dynamic data: heap
  e.g., malloc in C, new in Java
  Grows from bottom (lower address) to top (higher address)
Stack: temporal storage for functions
  e.g., return address of sub-functions, local variables
  Grows from top to bottom
Address Content

## Slide 5: Memory Layout
#include <stdio.h>
#include <string.h>
int numbers[2];
void myfunction(void)
{
FILE *fp;
int size = 2;
int sum = 0;
/* Open file for reading */
fp = fopen(“mynumbers.txt", “r");
/* Read and display data */
fread(numbers, sizeof(int), size, fp);
fclose(fp);
sum = numbers[0] + numbers[1];
printf(“Sum = %d\n”, sum);
}
int main (void) {
myfunction();
return(0);
}
Compiled machine code
numbers[1]
numbers[0]
Compiled machine code

## Slide 6: Memory Layout
#include <stdio.h>
#include <string.h>
int numbers[2];
void myfunction(void)
{
FILE *fp;
int size = 2;
int sum = 0;
/* Open file for reading */
fp = fopen(“mynumbers.txt", “r");
/* Read and display data */
fread(numbers, sizeof(int), size, fp);
fclose(fp);
sum = numbers[0] + numbers[1];
printf(“Sum = %d\n”, sum);
}
int main (void) {
myfunction();
return(0);
}
Compiled machine code
Return address
*fp
size
sum
Stack region for myfunction
numbers[1]
numbers[0]

## Slide 7: Memory Layout
#include <stdio.h>
#include <string.h>
int numbers[2];
void myfunction(void)
{
FILE *fp;
int size = 2;
int sum = 0;
/* Open file for reading */
fp = fopen(“mynumbers.txt", “r");
/* Read and display data */
fread(numbers, sizeof(int), size, fp);
fclose(fp);
sum = numbers[0] + numbers[1];
printf(“Sum = %d\n”, sum);
}
int main (void) {
myfunction();
return(0);
}
Compiled machine code
Return address
*fp
size
sum
Stack region for myfunction
numbers[1]
numbers[0]

## Slide 8: Memory Access Is Slow
Variables are all stored in Memory, which is outside of CPU
  Slow..
How can we execute the operations faster?
  Use on-chip memory
Compiled machine code
Return address
*fp
size
sum
numbers[1]
numbers[0]

## Slide 9: Register File
Register File
  On-chip memory that stores “Registers”
Registers
  Temporal space to maintain operand values and calculation results before storing back to memory
  Presented with “$” + “register id” in MIPS processor
    i.e. $0 : 0th register,
    $1 : 1st register
Compiled machine code
Return address
*fp
size
sum
$0
$1
$2
…
$31
Register File
numbers[1]
numbers[0]

## Slide 10: Typical Execution Steps
  Load operand values from memory to registers
  Do computation on registers
  Move the results from register to memory
Compiled machine code
Return address
*fp
size
sum
$0
$1
$2
…
$31
Register File
numbers[1]
numbers[0]

## Slide 11: Operations in Hardware
Hardware can do one operation at a time
  Arithmetic operations
    add, sub, mult, div, …
  Data movement
    move, load data, store data, …
  Logical operations
    shift, and, or, xor, …
  Conditional operations
    jump, branch on condition, …
Format of assembly instructions that uses register operands
  Command Result, Operand 1, Operand 2
  E.g. C = A + B  Add C, A, B (A, B, C should be replaced by register id)

## Slide 12: HLL vs. Hardware Operations
HLL are designed to be understood and programmed easily by programmers
A HLL line may be a combination of multiple assembly instructions
Compile

## Slide 13: Code Example: Memory & Registers
C code
MIPS Assembly code
Compile
Operations involved:
Value of ‘a’ is loaded from mem to $3
Value of ‘b’ is loaded from mem to $2
Add operation done on $2 and $3
Value of ‘c’ is stored to mem

## Slide 14: Code Example: Memory & Registers
C code
MIPS Assembly code
Compile
Compiled machine code
$0
$1
$2
…
$31
Register File
executing line
$3
Stack region
allocation for test()

## Slide 15: Code Example: Memory & Registers
C code
MIPS Assembly code
Compile
Compiled machine code
$0
$1
$2
…
$31
Register File
executing line
$3
a = 1

## Slide 16: Code Example: Memory & Registers
C code
MIPS Assembly code
Compile
Compiled machine code
b = 2
a = 1
$0
$1
$2
…
$31
Register File
executing line
$3

## Slide 17: Code Example: Memory & Registers
C code
MIPS Assembly code
Compile
Compiled machine code
b = 2
a = 1
$0
$1
$2
…
$31
Register File
executing line
$3

## Slide 18: Code Example: Memory & Registers
C code
MIPS Assembly code
Compile
Compiled machine code
b = 2
a = 1
$0
$1
$2
…
$31
Register File
executing line
$3 (1)

## Slide 19: Code Example: Memory & Registers
C code
MIPS Assembly code
Compile
Compiled machine code
b = 2
a = 1
$0
$1
$2 (2)
…
$31
Register File
executing line
$3 (1)
+
$2 (3)

## Slide 20: Code Example: Memory & Registers
C code
MIPS Assembly code
Compile
Compiled machine code
b = 2
a = 1
$0
$1
$2 (2)
…
$31
Register File
executing line
$3 (1)
$2 (3)
c = 3

## Slide 21: Registers of MIPS CPUs
Assembler Name | Register Number | Description
$zero | $0 | Constant 0 value
$at | $1 | Assembler temporary
$v0-$v1 | $2-$3 | Function return values
$a0-$a3 | $4-$7 | Function Arguments
$t0-$t7 | $8-$15 | Temporaries
$s0-$s7 | $16-$23 | Saved Temporaries
$t8-$t9 | $24-$25 | Temporaries
$k0-$k1 | $26-$27 | Reserved for OS kernel
$gp | $28 | Global Pointer (Global and static variables/data)
$sp | $29 | Stack Pointer
$fp | $30 | Frame Pointer
$ra | $31 | Return Address

## Slide 22: Exercise: Register Reuse
Example:
- Assume g, h, i and j are loaded to registers, $t0, $t1, $t2, $t3
- HLL:
f = (g + h) – (i + j);
- Assembly (with add & sub operations)?
add $t0, $t0, $t1
add $t2, $t2, $t3
sub $t2, $t0, $t2
Register values are maintained unless overwritten

## Slide 23: A Brief Review
One line of HLL can involve:
  Load operand values from memory to registers
  Do computation on registers
  Move the results from register to memory
  Arithmetic operations
    add, sub, mult, div, …
  Logical operations
    shift, and, or, xor, …
  Conditional operations
    jump, branch on condition, …
  Data load operations
    move, load data, …
  Data store operations
    move, store data, …

## Slide 24: Operations of MIPS CPUs
Note: A, B, C in the table should be replaced by proper register ids
C operator | Assembly Operations | Comments
C = A + B | add C, A, B | Add two values
C = A - B | sub C, A, B | Subtract one from another
C = A * B | mul C, A, B | Multiply two values
C = A & B | and C, A, B | Logical AND operation
C = A ¦ B | or C, A, B | Logical OR operation
C = A ^ B | xor C, A, B | Logical XOR operation
C = A << shamt | sll C, A, shamt | Shift left by shamt
C = A >> shamt | srl C, A, shamt | Shift right by shamt
If (A < B) C = 1 | slt C, A, B | Set if less than
C = Memory | lw C, Memory address | Load value from memory
Memory = C | sw C, Memory address | Store value to memory
If (A == B) go to Addr | beq A, B, address | Jump if A == B
Many more … |  | 

## Slide 25: About MIPS Assembly
CPUs use their own assembly languages
  Assembly language of ARM, Pentium, Opteron… are all different
MIPS Assembly Features
  Very similar to ARM Assembly
  One of the earliest RISC architectures that used pipelined instruction processing
Developed by MIPS Technologies
  Now maintained by Wave Computing
  Various generations
    MIPS I~V
    MIPS32 (32-bit processor)
    MIPS64 (64-bit processor)
    microMIPS..

## Slide 26: Two types of Computers
  Reduced Instruction Set Computer (RISC): MIPS, ARM, …
    - Operands are in registers
    - Each instruction can do only one operation: Simple but longer codes
  Complex Instruction Set Computer (CISC): Intel, AMD, …
    - Operands can be in registers, stacks, accumulators, in memories
    - Each instruction can do multiple operations: Complex but shorter codes
    - Preferred when memory was very expensive

## Slide 27: MIPS Processor Organization
Memory
CPU
$0
...
$31
Integer
Registers
Arithmetic Unit
Multiply
Divide
Lo
Hi
Coprocessor 1 (FPU)
$0
...
$31
Floating
-point
Arithmetic Unit
Coprocessor 0
(Traps and Memory)
VAddr
Cause
Status
EPC
32~64bit
32 bit
Our Focus
Registers

## Slide 28: About MIPS32 Processor
  Instructions are 32-bit wide
  Registers and Computing Logic use 32-bit data
  Memory bus is logically 32-bit wide
  32 general purpose registers (GPRs) for integer and address values
    - A few special ones (i.e. $zero: constant 0, $fp: frame pointer, $sp: stack pointer..)
  32 floating point registers for floating point operations (not our focus)

## Slide 29: Conclusion Time
What is ISA?
What is Microarchitecture?
Hardware operation definition
ISA implementation
What is Register File?
On-chip memory