## Slide 1: Lecture 2. Processor Instruction Set Architecture & Language (2)
Haonan Wang
CMPE 200 Computer Architecture & Design

## Slide 2: MIPS Processor Organization
Memory
CPU
$0
...
$31
Integer
Registers
Arithmetic Unit
Multiply
Divide
Lo
Hi
Coprocessor 1 (FPU)
$0
...
$31
Floating
-point
Arithmetic Unit
Coprocessor 0
(Traps and Memory)
VAddr
Cause
Status
EPC
32~64bit
32 bit
Our Focus
Registers

## Slide 3: About MIPS32 Processor
  Instructions are 32-bit wide
  Registers and Computing Logic use 32-bit data
  Memory bus is logically 32-bit wide
  32 general purpose registers (GPRs) for integer and address values
    - A few special ones (i.e. $zero: constant 0, $fp: frame pointer, $sp: stack pointer..)
  32 floating point registers for floating point operations (not our focus)

## Slide 4: MIPS Data Sizes
Integer: 3 Sizes Defined
  Byte (B)
    8-bits
  Halfword (H)
    16-bits = 2 bytes
  Word (W)
    32-bits = 4 bytes
Floating-point: 2 Sizes Defined
  Single (S)
    32-bits = 4 bytes
  Double (D)
    64-bits = 8 bytes
    For a 32-bit data bus, a double needs 2 memory reads

## Slide 5: Byte-oriented vs. Word-oriented Memory
Most processors are byte-oriented
  Can access a word from any byte address
MIPS: Word-oriented
  Words must be aligned to multiples of its size
  Still byte-addressable!
  Provides some simplicity in design
Logical views can be arranged in rows of 4-bytes for word-oriented memories
Proc
Mem
A
D
/
32
/
32
…
12
F3
3B
0x00002
0x00001
0x00000
Logical Byte-Oriented View of Mem
12
F3
3B
7C
47
13
00
8E
…
0x00008
0x00004
0x00000
Logical Word-Oriented View

## Slide 6: Endian-ness
Endian-ness refers to the two alternate methods of ordering the bytes in a larger unit (word, long, etc.)
  Big-Endian: IBM, SPARC, Motorola
    Most Significant byte (MSB) is put at the
    starting (low) address
  Little-Endian: Intel, DEC
    Least Significant byte (LSB) is put at the
    starting (low) address
  Supporting both
    MIPS, PowerPC, ARM
The longword value:
Big-Endian
Little-Endian
0 x 1 2 3 4 5 6 7 8
can be stored differently
78
0x00
56
34
0x01
0x02
12
0x03
12
0x00
34
56
0x01
0x02
78
0x03

## Slide 7: Memory Characteristics & Assumptions
Half-word and Word data are addressed with lowest byte address among the bytes in the data
Addresses from left to right follows the same order as addresses from top to bottom
We will use Little-Endian for MIPS in this course
12
F3
3B
7C
47
13
00
8E
…
0x00008
0x00004
0x00000
Logical Word-Oriented View

## Slide 8: Memory Organization Example 1
  Example: If the memory layout is given like below
  The byte value in address
  0x0000 is ( )
  0x0001 is ( )
  0x0002 is ( )
  0x0003 is ( )
  0x0006 is ( )
12
F3
3B
7C
47
13
00
8E
…
0x00008
0x00004
0x00000
Logical Word-Oriented View
0x3B
0xF3
0x12
0x7C
0x47

## Slide 9: Memory Organization Example 2
  Example: If the memory layout in MIPS is given like below
  The half-word value in address
  0x0000 is ( )
  0x0001 is ( )
  0x0002 is ( )
  The word value in address
  0x0002 is ( )
  0x0004 is ( )
12
F3
3B
7C
47
13
00
8E
…
0x00008
0x00004
0x00000
Logical Word-Oriented View
0xF33B
Incorrect addressing
0x7C12
Incorrect addressing
0x8E471300

## Slide 10: Tips to Remember Endianness
Looks normal (same as writing order) when address is from low to high
Looks strange here
But same as writing order when address is from high to low
word value:
Little-Endian
0 x 1 2 3 4 5 6 7 8
78
0x03
56
34
0x02
0x01
12
0x00
12
0x00
34
56
0x01
0x02
78
0x03
34
56
78
12
…
0x00004
0x00000
Logical Word-Oriented View

## Slide 11: Basic Instruction Formats
Example: Format with 3 registers
  add Rd, Rs, Rt # Rd = Rs + Rt
Command
(operation)
Destination Register
(stores calculation result)
Source Register 1
(stores first operand value)
Source Register 2
(stores second operand value)
Comment

## Slide 12: Basic Instruction Formats
Example: Format with 3 registers
  add $4, $3, $2 # $4 = $3 + $2
$0
$1
$2 (3)
…
$31
Register File
$3 (2)
$4
If $2 and $3 have integer values 3 and 2 each,
$4 will have ( ) after executing this instruction
5
$4 (5)

## Slide 13: R-Type Instructions
We call the instructions that use three registers as R-type Instructions
  2 registers as source, 1 register for result
Examples:
  sub Rd, Rs, Rt # Rd = Rs – Rt
  mul Rd, Rs, Rt # Rd = Rs * Rt
  and Rd, Rs, Rt # Rd = Rs & Rt
  or Rd, Rs, Rt # Rd = Rs | Rt
  xor Rd, Rs, Rt # Rd = Rs ^ Rt
  slt Rd, Rs, Rt # if (Rs < Rt) Rd = 1; else Rd = 0;
  many more
Replace Rd, Rs, Rt with actual registers

## Slide 14: R-Type Instructions
Exercise:
  Assume that the initial state of register file is like below
  What is $2 value after executing all three instructions?
sub $4, $2, $3
add $3, $3, $4
slt $2, $3, $4
$0
$1
$2 (10)
…
$31
Register File
$3 (8)
$4 (4)
$4 (2)
# 2 = 10 - 8
# 10 = 8 + 2
$3 (10)
# (10 < 2)? No
 $2 = 0
$2 (0)

## Slide 15: Instructions Using Immediate Value
What if you want to use an immediate value?
  E.g. i = i + 1; // add immediate value 1 to i
  addi Rt, Rs, imm # Rt = Rs + imm
Command
(operation)
Destination Register
(stores calculation result)
Source Register
(stores operand value)
Immediate operand
(stores immediate operand value)

## Slide 16: Instructions Using Immediate Value
Example: Instruction format with immediate value
  addi $4, $3, 1 # $4 = $3 + 1
$0
$1
$2 (3)
…
$31
Register File
$3 (2)
$4
If $3 has integer value 2,
$4 will have ( ) after executing this instruction
3
$4 (3)

## Slide 17: I-Type Instructions
We call the instructions that use two registers and one immediate value as I-type Instructions
  1 register and 1 immediate value as source, 1 register for result
Examples:
  subi Rt, Rs, imm # Rt = Rs – imm
  andi Rt, Rs, imm # Rt = Rs & imm
  ori Rt, Rs, imm # Rt = Rs | imm
  xori Rt, Rs, imm # Rt = Rs ^ imm
  beq Rt, Rs, imm # if (Rt == Rs) goto imm; else continue
  lw Rt, imm(Rs) # load a word from (imm + Rs) address to Rt
  slti Rt, Rs, imm # if (Rs < imm) Rt = 1; else Rt = 0;
  many more

## Slide 18: I-Type: Branch Instructions
  Conditional Branches
    Branches only if a particular condition is true
      E.g., Compares Rs, Rt. If EQ/NE, branch to label, else continue
  Example:
if ( a == b ) {
a++;
}
else {
a--;
}
Check condition of if statement
Upon the condition result,
you execute either a++ or a--
TRUE
FALSE

## Slide 19: I-Type: Branch Instructions
  Conditional Branches
    Branches only if a particular condition is true
      E.g., Compares Rs, Rt. If EQ/NE, branch to label, else continue
  Example:
sub $4, $2, $3
add $3, $3, $4
slt $2, $3, $4
Without branch,
instructions are executed
sequentially; line by line
sub $4, $2, $3
beq $3, $4, Label
slt $2, $3, $4
Label: addi $3, $3, 1
Branch instruction checks the condition
and choose either executing next line or
jumping to the specified line
If $3 == $4
If $3 != $4

## Slide 20: I-Type: Branch Instructions
Conditional Branches
  Branch if condition satisfies
  beq Rs, Rt, imm # if (Rs == Rt) goto imm; else continue
  bne Rs, Rt, imm # if (Rs != Rt) goto imm; else continue
Unconditional Branches
  Always branch to label
  b imm # goto imm
  beq $0, $0, imm # goto imm
Pseudo-instruction
Instruction “b imm” is not actually supported by the hardware.
Assembler replaces “b imm” to “beq $0, $0, imm”
check more pseudo instructions in textbook
Comparing the same
register values
 always equal

## Slide 21: I-Type: Memory Instructions
  Memory operations use special format to present memory address
  Example:
  lw Rt, imm(Rs) # Load a word from address (Rs + imm) to Rt
Command
(operation)
Destination Register
(stores loaded value)
Immediate value
(stores offset value of
the target memory address)
Source operand
(stores base address of
the target memory address)

## Slide 22: I-Type: Memory Instructions
Memory Instruction Example:
  lw $4, 4($3) # $4 = a word data in ($3 + 4)
$0
$1
$2 (3)
…
$31
Register File
$3 (0x7000)
$4
If the initial state of register file and memory
is like illustrated,
a word in ( ) will be loaded to $4 so
$4 will have ( ) after executing this instruction
10
$4 (10)
Memory
10
512
0x0
0x7fffffff
0x7000
0x7004
0x7004

## Slide 23: I-Type: Memory Instructions
Load: move data from memory to register file
  lb Rt, imm(Rs) # Rt = 1-byte data in (Rs + imm)
  lh Rt, imm(Rs) # Rt = 2-byte (half-word) data in (Rs + imm)
  lw Rt, imm(Rs) # Rt = 4-byte (word) data in (Rs + imm)
Store: move data from register file to memory
  sb Rt, imm(Rs) # (Rs + imm) = 1-byte data in Rt
  sh Rt, imm(Rs) # (Rs + imm) = 2-byte (half-word) data in Rt
  sw Rt, imm(Rs) # (Rs + imm) = 4-byte (word) data in Rt

## Slide 24: I-Type: Memory Instructions
Example:
  The initial state of register file and memory are like below
  What is $2 value after executing each of the following instructions?
  lw $2, 0x40($3)
  lb $2, -1($4)
  lh $2, -6($4)
0
Register File
0x7000
0x704C
Memory
0x0
0x7fffffff
0x7040
0x7044
0x7048
0xF8BE97CD
0x134982FE
0x5A12C5B7
$0
$1
$2
$3
$4
$31
…
# $2 = word in 0x7040
# $2 = byte in 0x704B
# $2 = 2 bytes in 0x7046
0x5A12C5B7
0xFFFFFFF8
Note that when executing lb and lh which loads a signed data which is shorter than 4-byte word, the data should be sign-extended to fill 32-bit space of a register.
0x00001349

## Slide 25: I-Type: Memory Instructions
Example:
  The initial state of register file and memory are like below
  How the memory is updated?
  sw $2, 0x40($3)
  sb $2, -5($4)
  sh $2, -2($4)
0x123489AB
Register File
0x7000
0x704C
Memory
0x0
0x7fffffff
0x7040
0x7044
0x7048
0xF8BE97CD
0x134982FE
0x5A12C5B7
$0
$1
$2
$3
$4
$31
…
# 0x7040 = word in $2
# 0x7047 = byte in $2
# 0x704A = 2 bytes in $2
When you store 1- to 2- bytes to memory, other values in the same word should remain unchanged
0x1234589AB
0xAB4982FE
0x89AB97CD

## Slide 26: Signed vs. Unsigned Instructions
We use sign extension for lb and lh
  This is because lb and lh are signed instructions
Unsigned instructions
  No need to do sign extension because the values are regarded as positive values always; just fill zeros to the remaining bytes
  lbu $2, -1($4) # load byte unsigned
  # If lb in the earlier example is lbu,
  # $2 will be updated with 0x000000F8
  lhu $2, -6($4) # load half-word unsigned
  # If lh in the earlier example is lhu,
  # $2 will be updated with 0x00001349

## Slide 27: Signed vs. Unsigned Instructions
Other instructions also have unsigned versions
  addu, addiu, subu, divu, multu, …
Example:
  Assume that $2 = 0xFFFFFFFF, $3 = 0x00000001, what is $1 in each instruction?
  slt $1, $2, $3 # signed set less than
  # -1 < +1  $1 = 1
  sltu $1, $2, $3 # unsigned set less than
  # +4,294,967,295 > +1  $1 = 0

## Slide 28: Exercise-1
Translate the given high-level language code to MIPS assembly.
  Assume that the address of integer variables x, y, and z are in 0x400, 0x404, and 0x408 in the memory, respectively
  $1’s initial value is 0x400
x = y + z;
lw $2, 4($1)
lw $3, 8($1)
add $2, $2, $3
sw $2, 0($1)
MIPS
High-level language
Tasks to do:
Load y value to a register
Load z value to another register
Run add operation
Store the result to memory