## Slide 1: Lecture 2. Processor Instruction Set Architecture & Language (3)
Haonan Wang
CMPE 200 Computer Architecture & Design

## Slide 2: Machine Code of R-Type Instructions
All instructions in MIPS have 32-bit width
  Within 32-bit data, command and three register ids should be presented
  add Rd, Rs, Rt
Opcode
Rs
6 bits
5 bits
Rt
5 bits
Rd
5 bits
Shamt
5 bits
Function
6 bits
32 bits

## Slide 3: Machine Code of R-Type Instructions
Opcode
  Indicate Command/Operation of an instruction with combination of Function field
  Example:
    add
    and
    or
    many more
  R-type instructions always have all zeros in Opcode field and use Function field to distinguish the instructions
Opcode
Rs
6 bits
5 bits
Rt
5 bits
Rd
5 bits
Shamt
5 bits
Function
6 bits
32 bits
000000
Rs
Rt
Rd
Shamt
100000
000000
Rs
Rt
Rd
Shamt
100100
000000
Rs
Rt
Rd
Shamt
100101
0
0x20
0
0x24
0x25
0

## Slide 4: Machine Code of R-Type Instructions
Rs, Rt, Rd
  Indicate source and destination register ids used by an instruction
  Example:
    add $5, $4, $3
    and $13, $8, $2
    or $t8, $s0, $s1
  Each field has 5 bits because we have 32 (=25) registers in MIPS
Opcode
Rs
6 bits
5 bits
Rt
5 bits
Rd
5 bits
Shamt
5 bits
Function
6 bits
32 bits
000000
00100
00011
00101
Shamt
100000
000000
01000
00010
01101
Shamt
100100
000000
10000
10001
11000
Shamt
100101
$4
$3
$5
01000
00010
01101
$8
$2
$13
10000
10001
11000
$s0 (16)
$s1 (17)
$t8 (24)

## Slide 5: Machine Code of R-Type Instructions
Shamt
  Indicate the shift amount that is used for shift instructions only; the other R-type instructions have all zeros in this field
  Example:
    add $5, $4, $3
    and $13, $8, $2
    or $t8, $s0, $s1
Opcode
Rs
6 bits
5 bits
Rt
5 bits
Rd
5 bits
Shamt
5 bits
Function
6 bits
32 bits
000000
00100
00011
00101
00000
100000
000000
01000
00010
01101
00000
100100
000000
10000
10001
11000
00000
100101

## Slide 6: Shift Instructions
Special format R-type Instruction
  The second operand is an immediate value (shamt) that indicates the amount of shift
Logical Shifting
  Shift towards left/right with filling in 0s
  Example:
    sll Rd, Rt, shamt # Rd = Rt << shamt (Rt: unsigned data)
    srl Rd, Rt, shamt # Rd = Rt >> shamt (Rt: unsigned data)
Arithmetic Shifting
  Shift towards left/right with maintaining the value’s sign bit
  Example:
    sra Rd, Rt, shamt # Rd = Rt >> shamt (Rt: signed data)

## Slide 7: Example: Logical Shift
Shift towards left/right with filling in 0s
Example:
  Assume that the original value of $4 is 0x0000000C
  What is the value of $5 after executing the following shift instructions?
  sll $5, $4, 3 # shift left logical the value of $4 by 3 bits
  srl $5, $4, 2 # shift right logical the value of $4 by 2 bits
0 0 ... 0 0 1 1
Logical Right Shift by 2 bits:
... 0 1 1 0 0 0 0 0
Logical Left Shift by 3 bits:
0’s shifted in…
0’s shifted in…
0 ... 0 1 1 0 0
= +12
= +3
= +96
0x00000003
0x00000060
srl $5, $4, 2
sll $5, $4, 3
$4
0x0000000C
“Shift Right N bits” is used for division by 2N
“Shift Left N bits” is used for multiply by 2N
Careful: Could overflow!
$5
$5
Shift operation should be done in bit level  translate given value to binary first

## Slide 8: Example: Arithmetic Shift
Shift right with replicating MSB
Shift left with filling in 0s
Example:
  Assume that the original value of $4 is 0xFFFFFFFC (= -4)
  What is the value of $5 after executing the following shift instruction?
  sra $5, $4, 2 # shift right arithmetic the value of $4 by 2 bits
1 1 ... 1 1 1 1
Arithmetic Right Shift by 2 bits:
Arithmetic Left Shift by 3 bits:
MSB replicated and shifted in…
0’s shifted in…
1 ... 1 1 1 0 0
= -4
= -1
= -32
0xFFFFFFFF
0xFFFFFFE0
sra $5, $4, 2
sla? $5, $4, 3
$4
0xFFFFFFFC
$5
Notice if we shifted in 0s (like a logical right shift) our result would be a positive number and the division wouldn’t work
Notice there is no difference between an arithmetic and logical left shift. We always shift in 0s.
MIPS uses sll for both logical/arithmetic left shift (no separate sla instruction)
1.. 1 1 1 0 0 0 0 0
$5

## Slide 9: Machine Code of R-Type Instructions
Shamt
  Indicate the shift amount that is used for shift instructions only; the other R-type instructions have all zeros in this field
  Example:
    sll $5, $4, 3
    srl $5, $4, 2
    sra $5, $4, 2
Opcode
Rs
6 bits
5 bits
Rt
5 bits
Rd
5 bits
Shamt
5 bits
Function
6 bits
32 bits
000000
00000
00100
00101
00011
000000
000000
00000
00100
00101
00010
000010
000000
00000
00100
00101
00010
000011
3
2
2

## Slide 10: Machine Code of I-Type Instructions
All instructions in MIPS are 32-bit wide
  Within 32-bit data, command, two register ids, and an immediate value should be presented
  addi Rt, Rs, imm
Opcode
Rs
6 bits
5 bits
Rt
5 bits
16 bits
Immediate
32 bits

## Slide 11: Machine Code of I-Type Instructions
Opcode
  Indicate Command/Operation of an instruction
  Example:
    addi
    andi
    ori
    many more;
001000
Rs
Rt
Immediate
Opcode
Rs
6 bits
5 bits
Rt
5 bits
16 bits
Immediate
32 bits
001100
Rs
Rt
Immediate
001101
Rs
Rt
Immediate

## Slide 12: Machine Code of I-Type Instructions
Rs, Rt
  Indicate source and destination register ids used by an instruction
  Example:
    addi $5, $4, 1
    andi $13, $12, 0xA
    ori $t3, $t2, 12
001000
00100
00101
Immediate
Opcode
Rs
6 bits
5 bits
Rt
5 bits
16 bits
Immediate
32 bits
001100
01100
01101
Immediate
001101
01010
01011
Immediate
$4
$5
$12
$13
$t2 (10)
$t3 (11)

## Slide 13: Machine Code of I-Type Instructions
Immediate
  Indicate the immediate value
  Example:
    addi $5, $4, 1
    andi $13, $12, 0xA
    ori $t3, $t2, 12
001000
00100
00101
0000000000000001
Opcode
Rs
6 bits
5 bits
Rt
5 bits
16 bits
Immediate
32 bits
001100
01100
01101
0000000000001010
001101
01010
01011
0000000000001100
1
0xA
12

## Slide 14: Machine Code of I-Type Instructions
Special I-Type instructions: Load/Store
  Within 32-bit data, command, two register ids, and an offset value should be presented
  lw Rt, imm(Rs)
Opcode
Rs
6 bits
5 bits
Rt
5 bits
16 bits
Immediate
32 bits

## Slide 15: Machine Code of I-Type Instructions
Load/Store in I-Type machine code format
  Example:
    lb $5, 4($4)
    lh $13, 0x10($12)
    lw $t3, -16($t2)
    sb $3, 0xfff0($4)
    sh $2, 8($8)
    sw $s1, 10($s0)
100000
00100
00101
0000000000000100
Opcode
Rs
6 bits
5 bits
Rt
5 bits
16 bits
Immediate
32 bits
100001
01100
01101
0000000000010000
100011
01010
01011
1111111111110000
4
0x10
-16
101000
00100
00011
1111111111110000
101001
01000
00010
0000000000001000
101011
10000
10001
0000000000001010
0xfff0
8
10
0x20
0x21
0x23
0x28
0x29
0x2B

## Slide 16: Machine Code of I-Type Instructions
Special I-Type instructions: Branch
  uses the same format but needs a special treatment for immediate field value
  beq Rs, Rt, imm
Opcode
Rs
6 bits
5 bits
Rt
5 bits
16 bits
Immediate
32 bits
Label name to branch

## Slide 17: Branch Target Addressing
PC-relative addressing
  MIPS calculates the branch target address based on the branch instruction’s next instruction’s address
  “Branch to N lines above or below”; not branch to absolute address
  necessary because in many cases, we do not know (at compile time) where our code will be loaded in the memory space
80000 | Loop: sll $t1, $s3, 2
80004 | add $t1, $t1, $s6
80008 | lw $t0, 0($t1)
8000C | bne $t0, $s5, Exit
80010 | addi $s3, $s3, 1
80014 | b Loop
80018 | Exit: …
Assume that the code is loaded
to 0x00080000 in memory
Each instruction is 4-byte long
 Assembly code line address increases by 4 bytes
Branch two lines below from bne’s next instruction (addi)
 Immediate field will be filled with 2
Branch 6 lines above from b’s next line (Exit)
 Immediate field will be filled with -6

## Slide 18: Branch Target Addressing
Why branch’s next instruction should be considered?
  Because MIPS increments program counter (PC) by 4 before executing an instruction
  This already incremented PC value is used for branch target address calculation
Branch Target Address Calculation
  Target address = branch’s next instruction address + offset x 4
  bne $t0, $s5, Exit
    Exit (0x00080018) = addi address (0x00080010) + distance (2) x 4 byte/inst
  b Loop
    Loop (0x00080000) = Exit address (0x00080018) + distance (-6) x 4 byte/inst
80000 | Loop: sll $t1, $s3, 2
80004 | add $t1, $t1, $s6
80008 | lw $t0, 0($t1)
8000C | bne $t0, $s5, Exit
80010 | addi $s3, $s3, 1
80014 | b Loop
80018 | Exit: …

## Slide 19: Machine Code of I-Type Instructions
Branch in I-Type machine code format
  Example:
    bne $t0, $s5, Exit
    beq $0, $0, Loop
000101
01000
10101
0000000000000010
Opcode
Rs
6 bits
5 bits
Rt
5 bits
16 bits
Immediate
32 bits
000100
00000
00000
1111111111111010
2
-6
0x5
0x4
80000s | Loop: sll $t1, $s3, 2
80004 | add $t1, $t1, $s6
80008 | lw $t0, 0($t1)
8000C | bne $t0, $s5, Exit
80010 | addi $s3, $s3, 1
80014 | b Loop
80018 | Exit: …

## Slide 20: Loading an Immediate
What if you want to load an immediate value to a register?
If immediate (constant) is 16 bits or less
  Use ori or addi instruction with $0 register
  Examples : You want to load value 1 to $2
    addi $2, $0, 1 // R[2] = 0 + 1 = 1
    ori $2, $0, 0x1 // R[2] = 0 | 1 = 1
If immediate is more than 16 bits
  Immediates limited to 16 bits so we must load constant with a 2-instruction sequence using the special LUI (Load Upper Immediate) instruction
  To load $2 with 0x12345678
    lui $2, 0x1234
    ori $2, $2, 0x5678
12340000
R[2]
12345678
R[2]
OR 00005678
LUI
ORI
LUI: the immediate value is loaded to the MSB 16 bits of the target register

## Slide 21: Exercise-2
Translate the given high-level language code to MIPS assembly.
  Assume that the address of integer variable x and y are in $4 and $1 respectively.
lw $2, 0($4)
lw $3, 0($1)
slt $1, $3, $2
beq $1, $0, Else
add $2, $2, $3
b Next
addi $2, $0, 1
sw $2, 0($4)
if (x > y)
x = x + y; else x = 1;
MIPS
High-level language
Tasks to do:
Load x value to a register
Load y value to another register
Check if y is less than x
If true, run add operation
Else, store 1 to one register
Store the result value to x in memory
If false, you should
not execute add
 Create a label for else case and branch
Else:
Wait, when x > y, the calculation result should be also stored to the memory without executing the else code
 Add unconditional branch and skip addi
x > y
x <= y
Next: