## Slide 1: Lecture 2. Processor Instruction Set Architecture & Language (4)
Haonan Wang
CMPE 200 Computer Architecture & Design

## Slide 2: Mult & Div Instructions
Memory
CPU
$0
...
$31
Integer
Registers
Arithmetic Unit
Multiply
Divide
Lo
Hi
Coprocessor 1 (FPU)
$0
...
$31
Floating
-point
Arithmetic Unit
Coprocessor 0
(Traps and Memory)
VAddr
Cause
Status
EPC
32~64bit
32 bit
Registers
Lo
Hi

## Slide 3: Mult & Div Instructions
Mult & Div use special registers, lo and hi
Multiplication
  mult Rs, Rt # lo = lower 32-bit of Rs * Rt
    # hi = higher 32-bit of Rs * Rt
Division
  div Rs, Rt # lo = quotient of Rs/Rt
    # hi = remainder of Rs/Rt
Moves the contents of lo/hi registers to GPR
  mflo $2 # $2 = lo
  mfhi $3 # $3 = hi

## Slide 4: Machine Code of Mult/Div/Mflo/Mfhi
Mult/Div/Mflo/Mfhi
  Example:
    mult $5, $4
    div $5, $4
    mflo $5
    mfhi $4
Opcode
Rs
6 bits
5 bits
Rt
5 bits
Rd
5 bits
Shamt
5 bits
Function
6 bits
32 bits
000000
00101
00100
00000
00000
0x18
000000
00101
00100
00000
00000
0x1a
000000
00000
00000
00101
00000
0x12
000000
00000
00000
00100
00000
0x10

## Slide 5: J-Type Instruction
There is another type, J, in MIPS for Jump instruction
  Similar to unconditional branch
  j target # Jump to target
Opcode
Target
6 bits
26 bits
32 bits

## Slide 6: Jump Target Addressing
Jump instruction provides larger scale jump than branch
Target address = First 4 bits of jump’s next instruction address : Last 28 bits of (target x 4)
Example: j Loop (0x00080000)
  The first 4 bits of Exit = 0x0
  Last 28 bits of target x 4 = 0080000
  target field = 0x0020000
00080000 | Loop: sll $t1, $s3, 2
00080004 | add $t1, $t1, $s6
00080008 | lw $t0, 0($t1)
0008000C | bne $t0, $s5, Exit
00080010 | addi $s3, $s3, 1
00080014 | j Loop
00080018 | Exit: …
00
Target
PC [31:28]
Target address of Jump
4-bits
26-bits
2-bits
32 bits

## Slide 7: Machine Code of J-Type Instructions
Jump in J-Type machine code format
  Example:
    j Loop
000010
00000000000000100000000000000000
0x0020000
0x2
Opcode
Target
6 bits
26 bits
32 bits

## Slide 8: Loops in MIPS: While Loops
Loop code consists of
  Condition check code
    To decide to continue the loop iteration or exit
  Jump to the loop entry to run the next iteration
  Example: Find x where 2x = 128
int pow = 1;
int x = 0;
while (pow != 128)
{
pow = pow * 2;
x = x + 1;
}
# $s0 = pow, $s1 = x
addi $s0, $0, 1
add $s1, $0, $0
addi $t0, $0, 128
while: beq $s0, $t0, done
sll $s0, $s0, 1
addi $s1, $s1, 1
j while
done:
MIPS
High-level language

## Slide 9: Loops in MIPS: For Loop
Loop code consists of
  Condition check code
    To decide to continue the loop iteration or exit
  Jump to the loop entry to run the next iteration
  Example: Add numbers from 0 to 9
int sum = 0;
int i;
for (i = 0; i != 10; i++)
{
sum = sum + i;
}
# $s0 = i, $s1 = sum
add $s0, $0, $0
add $s1, $0, $0
addi $t0, $0, 10
for: beq $s0, $t0, done
add $s1, $s1, $s0
addi $s0, $s0, 1
j for
done:
MIPS
High-level language

## Slide 10: Less Than Comparisons
The previous for loop can be rewritten by using “less than” operation like below
  Example: Add numbers from 0 to 9
int sum = 0;
int i;
for (i = 0; i < 10; i++)
{
sum = sum + i;
}
# $s0 = i, $s1 = sum
add $s0, $0, $0
add $s1, $0, $0
addi $t0, $0, 10
for: slt $t1, $s0, $t0
beq $t1, $0, done
add $s1, $s1, $s0
addi $s0, $s0, 1
j for
done:
MIPS
High-level language
# $s0 = i, $s1 = sum
add $s0, $0, $0
add $s1, $0, $0
addi $t0, $0, 10
for: beq $s0, $t0, done
add $s1, $s1, $s0
addi $s0, $s0, 1
j for
done:

## Slide 11: Less Than Comparisons
To reduce the number of instructions, you can also use slti or sltui instead of slt
  Example: Add numbers from 0 to 9
int sum = 0;
int i;
for (i = 0; i < 10; i++)
{
sum = sum + i;
}
# $s0 = i, $s1 = sum
add $s0, $0, $0
add $s1, $0, $0
addi $t0, $0, 10
for: slt $t1, $s0, $t0
beq $t1, $0, done
add $s1, $s1, $s0
addi $s0, $s0, 1
j for
done:
MIPS
High-level language
# $s0 = i, $s1 = sum
add $s0, $0, $0
add $s1, $0, $0
for: slti $t1, $s0, 10
beq $t1, $0, done
add $s1, $s1, $s0
addi $s0, $s0, 1
j for
done:

## Slide 12: Calling a Subroutine
How are subroutines executed?
int sub_func(void) { … } int main () { a = 1; b = sub_func(); a += b; }
How can we jump back to the Caller function,
and resume the execution from the immediate
following line of the subroutine calling line?
We should record the return address before
jumping to the subroutine

## Slide 13: Special Registers
Assembler Name | Register Number | Description
$zero | $0 | Constant 0 value
$at | $1 | Assembler temporary
$v0-$v1 | $2-$3 | Function return values
$a0-$a3 | $4-$7 | Function Arguments
$t0-$t7 | $8-$15 | Temporaries
$s0-$s7 | $16-$23 | Saved Temporaries
$t8-$t9 | $24-$25 | Temporaries
$k0-$k1 | $26-$27 | Reserved for OS kernel
$gp | $28 | Global Pointer (Global and static variables/data)
$sp | $29 | Stack Pointer
$fp | $30 | Frame Pointer
$ra | $31 | Return Address
$ra register holds the return address

## Slide 14: Jump and Link Instruction
Most of assembly languages provide a special jump (or branch) instruction that Jump + Update Return Address Register
  JAL Label 1. Jump to Label and
  2. Update $ra with return address
  (JAL’s next instruction address)
Jump and Link
Target code line to jump

## Slide 15: Calling a Subroutine
How can we jump back to address in $ra?
int sub_func(void) { … } int main () { a = 1; b = sub_func(); a += b; }
jal sub_func
$pc  address of first line of sub_func
$ra  address of a += b;

## Slide 16: Jump with Register
We can return to the Caller by running Jump with Register instruction with $ra as an operand
  JR $ra ; Jump to address in $ra
  ; ($pc = $ra)
Jump with Register
Register holding the jump target address

## Slide 17: Jump with Register
Assume that the addresses in the previous example are like below
int sub_func(void) { … } int main () { a = 1; b = sub_func(); a += b; }
jal sub_func
$pc  address of first line of sub_func
$ra  address of a += b
0x00000160
0x00000200
0x00000204
0x00000208
0x00000208
0x000001600
jr $ra
$pc  $ra

## Slide 18: Jump with Register
Assume that the addresses in the previous example are like below
int sub_func(void) { … } int main () { a = 1; b = sub_func(); a += b; }
jal sub_func
$pc  address of first line of sub_func
$ra  address of a += b
0x00000160
0x00000200
0x00000204
0x00000208
0x00000208
0x000001600
jr $ra
$pc  $ra
0x000002080
Return to the return address in $ra

## Slide 19: Parameter Passing
How can we pass the parameters to/from a subroutine?
int sub_func(int a) { … } int main () { a = 1; b = sub_func(c); a += b; }
Input parameter “c” should be passed
Output “b” should be returned

## Slide 20: Registers For Parameter Passing
Input Parameters
  Up to 4 parameters in $a0 ~ $a3
  If more than 4 parameters, use stack from 5th parameter
Return Value
  For 32-bit return value, $v0 is used
  $v1 also is used when the return value is 64 bits long
    i.e. $v0 holds the bottom 32 bits and $v1 holds the top 32 bits

## Slide 21: Example 1
int t;
int main(void) {
int y;
…
y = diffofsums(2, 3, 4, 5);
…
}
int diffofsums (int f, int g, int h, int i) {
int result;
result = (f + g) – (h + i);
return result;
}
High-level language
main:
…
addi $a0, $0, 2 # arg 0 = 2
addi $a1, $0, 3 # arg 1 = 3
addi $a2, $0, 4 # arg 2 = 4
addi $a3, $0, 5 # arg 3 = 5
jal diffofsums # call subroutine
add $s0, $v0, $0 # y = returned value
…
diffofsums:
add $t0, $a0, $a1 # $t0 = f + g
add $t1, $a2, $a3 # $t1 = h + I
sub $s0, $t0, $t1 # result = (f + g) – (h + i)
add $v0, $s0, $0 # put return value in $v0
jr $ra # return to caller
MIPS Assembly

## Slide 22: Example 1 (Addressing)
Question: What values the following registers will have in each condition?
After jal
  $pc : 0x00000168
  $ra : 0x00000160
After jr
  $pc : 0x00000160
MIPS Assembly
Address
0x0000015C
0x00000160
0x00000168
.
.
.
0x0000016E
main:
…
addi $a0, $0, 2 # arg 0 = 2
addi $a1, $0, 3 # arg 1 = 3
addi $a2, $0, 4 # arg 2 = 4
addi $a3, $0, 5 # arg 3 = 5
jal diffofsums # call subroutine
add $s0, $v0, $0 # y = returned value
…
diffofsums:
add $t0, $a0, $a1 # $t0 = f + g
add $t1, $a2, $a3 # $t1 = h + I
sub $s0, $t0, $t1 # result = (f + g) – (h + i)
add $v0, $s0, $0 # put return value in $v0
jr $ra # return to caller

## Slide 23: Register Value Overwriting
Register file is a shared resource
Example:
  In the previous code, $t0, $t1, and $s0 are updated by Callee
  Assume that main function wanted to compare the diffofsums return value with value 10 and $t0 has value 10 before calling subroutine
  After calling the subroutine, $t0 is updated with intermediate compute result  incorrect comparison
main:
…
addi $t0, $0, 10 # main wanted to use $t0
addi $a0, $0, 2 # arg 0 = 2
addi $a1, $0, 3 # arg 1 = 3
addi $a2, $0, 4 # arg 2 = 4
addi $a3, $0, 5 # arg 3 = 5
jal diffofsums # call subroutine
add $s0, $v0, $0 # y = returned value
slt $t1, $s0, $t0 # to compare with comp result
…
diffofsums:
add $t0, $a0, $a1 # $t0 = f + g
add $t1, $a2, $a3 # $t1 = h + I
sub $s0, $t0, $t1 # result = (f + g) – (h + i)
add $v0, $s0, $0 # put return value in $v0
jr $ra # return to caller
After returning from diffofsums, main function will see the values of $t0, $t1, and $s0 are updated unexpectedly

## Slide 24: Register Value Overwriting
Use Stack memory to protect register values
  Callee backs up the values of registers to stack memory that will be updated in its function body
  Callee restores the values from stack to original registers before returning to Caller
diffofsums:
addi $sp, $sp, -12 # make space on stack
# to store 3 registers
sw $s0, 8($sp) # save $s0 on stack
sw $t0, 4($sp) # save $t0 on stack
sw $t1, 0($sp) # save $t1 on stack
add $t0, $a0, $a1 # $t0 = f + g
add $t1, $a2, $a3 # $t1 = h + I
sub $s0, $t0, $t1 # result = (f + g) – (h + i)
add $v0, $s0, $0 # put return value in $v0
lw $t1, 0($sp) # restore $t1 from stack
lw $t0, 4($sp) # restore $t0 from stack
lw $s0, 8($sp) # restore $s0 from stack
addi $sp, $sp, 12 # deallocate stack space
jr $ra # return to caller

## Slide 25: Register Value Overwriting
diffofsums:
addi $sp, $sp, -12 # make space on stack
# to store 3 registers
sw $s0, 8($sp) # save $s0 on stack
sw $t0, 4($sp) # save $t0 on stack
sw $t1, 0($sp) # save $t1 on stack
add $t0, $a0, $a1 # $t0 = f + g
add $t1, $a2, $a3 # $t1 = h + I
sub $s0, $t0, $t1 # result = (f + g) – (h + i)
add $v0, $s0, $0 # put return value in $v0
lw $t1, 0($sp) # restore $t1 from stack
lw $t0, 4($sp) # restore $t0 from stack
lw $s0, 8($sp) # restore $s0 from stack
addi $sp, $sp, 12 # deallocate stack space
jr $ra # return to caller
Compiled machine code
…
$t0 (10)
$t1 (2)
…
$ra
Register File
$s0 (9)
Stack region
allocation for
diffofsums
…
…
$sp
9
10
2
$t0 (5)
$t1 (9)
$s0 (-4)
After computations
in the function, registers are updated

## Slide 26: Register Value Overwriting
diffofsums:
addi $sp, $sp, -12 # make space on stack
# to store 3 registers
sw $s0, 8($sp) # save $s0 on stack
sw $t0, 4($sp) # save $t0 on stack
sw $t1, 0($sp) # save $t1 on stack
add $t0, $a0, $a1 # $t0 = f + g
add $t1, $a2, $a3 # $t1 = h + I
sub $s0, $t0, $t1 # result = (f + g) – (h + i)
add $v0, $s0, $0 # put return value in $v0
lw $t1, 0($sp) # restore $t1 from stack
lw $t0, 4($sp) # restore $t0 from stack
lw $s0, 8($sp) # restore $s0 from stack
addi $sp, $sp, 12 # deallocate stack space
jr $ra # return to caller
Compiled machine code
…
$t0 (10)
$t1 (2)
…
$ra
Register File
$s0 (9)
Stack region
allocation for
diffofsums
…
…
$sp
9
10
2
$t0 (5)
$t1 (9)
$s0 (-4)
Before returning to Caller,
Register values are revoked

## Slide 27: Example: Nested Function Call
func1:
addi $sp, $sp, -4 # make space on stack
# to store $ra register
sw $ra, 0($sp) # save $ra on stack
jal func2 # jump to func2
…
lw $ra, 0($sp) # restore $ra from stack
addi $sp, $sp, 4 # deallocate stack space
jr $ra # return to caller
func2:
addi $sp, $sp, -8 # make space on stack
# to store 2 registers
…
addi $sp, $sp, 8 # deallocate stack space
jr $ra # return to func1 (caller)
Compiled machine code
…
Used by func1
Used by func2
Used by func2
$sp before func1
$sp in func1
$sp in func2
Why does func1 store $ra in stack before calling func2?

## Slide 28: Example: Recursion
Recursive functions should keep its input parameters and return address to the stack because all the recursions will try to use the same registers for these.
Int factorial (int n)
{
if (n <= 1)
return 1;
else
return (n * factorial (n-1));
}
High-level language
MIPS Assembly
factorial: addi $sp, $sp, -8 # make room
sw $a0, 4($sp) # store input (n)
sw $ra, 0($sp) # store return address
addi $t0, $0, 2 # $t0 = 2
slt $t0, $a0, $t0 # n <= 1?
beq $t0, $0, else # no: go to else (recursion)
addi $v0, $0, 1 # yes: return 1
addi $sp, $sp, 8 # restore $sp
jr $ra # return
else: addi $a0, $a0, -1 # n = n -1
jal factorial # recursive call
lw $ra, 0($sp) # restore return address
lw $a0, 4($sp) # restore input
addi $sp, $sp, 8 # restore $sp
mul $v0, $a0, $v0 # n * factorial(n-1)
jr $ra # return

## Slide 29: Example: Recursion for 3!
Compiled machine code
…
$sp
0x000000FC
0x000000F8
0x000000F4
0x000000F0
0x000000EC
0x000000E8
0x000000E4
0x000000E0
0x000000DC
…
$a0 (0x3)
$ra
$sp
$a0 (0x2)
$ra
$sp
$a0 (0x1)
$ra
factorial: addi $sp, $sp, -8 # make room
sw $a0, 4($sp) # store input (n)
sw $ra, 0($sp) # store return address
addi $t0, $0, 2 # $t0 = 2
slt $t0, $a0, $t0 # n <= 1?
beq $t0, $0, else # no: go to else (recursion)
addi $v0, $0, 1 # yes: return 1
addi $sp, $sp, 8 # restore $sp
jr $ra # return
else: addi $a0, $a0, -1 # n = n -1
jal factorial # recursive call
lw $ra, 0($sp) # restore return address
lw $a0, 4($sp) # restore input
addi $sp, $sp, 8 # restore $sp
mul $v0, $a0, $v0 # n * factorial(n-1)
jr $ra # return
$sp
$v0 = 1
$sp
$a0 = 2
$v0 = 2 x 1
$sp
$a0 = 3
$v0 = 3 x 2
$v0 = 6

## Slide 30: Exercise 1
Translate the given high-level language code to MIPS assembly
  Assume that the base address of an integer array a is in register $s0
    base address of an array: the address of the first element of the array
a[1]++;
lw $t3, 4($s0)
addi $t3, $t3, 1
sw $t3, 4($s0)
MIPS
High-level language
a[0]
a[1]
a[2]
Address
of a[0] is in $s0
in this exercise
0x7000
0x7004
0x7008
If you defined int a[3]; and the system allocated
a chunk of memory for this 3-element array from 0x7000,
the address of elements would be like below
Memory allocation for Arrays
4 byte (integer)

## Slide 31: Exercise 2
Translate the given high-level language code to MIPS assembly
  Assume that the base address of a char array a is in register $s0
    base address of an array: the address of the first element of the array
  Assume that the value of i is in $t0.
a[i]--;
MIPS
High-level language
a[0]
Address
of a[0] is in $s0
in this exercise
0x7000
0x7004
If you defined char a[8]; and the system allocated
a chunk of memory for this 8-element array from 0x7000,
the address of elements would be like below
Memory allocation for Arrays
1 byte (char)
a[1]
a[2]
a[3]
a[4]
a[5]
a[6]
a[7]

## Slide 32: Exercise 2
Translate the given high-level language code to MIPS assembly
  Assume that the base address of a char array a is in register $s0
    base address of an array: the address of the first element of the array
  Assume that the value of i is in $t0.
a[i]--;
add $t2, $s0, $t0
lb $t3, 0($t2)
subi $t3, $t3, 1
sb $t3, 0($t2)
MIPS
High-level language
Now we know that the address of a[i] is $s0 + 1byte * i = $s0 + $t0
Is this a valid operation to get one byte from $s0 + $t0?
lb $t1, $t0($s0)
No, because offset should be an immediate value, not a register id
We should change the base address value, not offset value
i.e. new base: $t2 = $s0 + $t0
and then load one byte from 0($t2)