## Slide 1: Lecture 3. Processor Microarchitecture and Design (1)
Haonan Wang
CMPE 200 Computer Architecture & Design

## Slide 2: Instruction Processing
CPU
A 32-bit instruction
Decoder
The instruction is
- Opcode: add
- Rs: $4
- Rt: $3
- Rd: $5
Compiled machine code
Return address
*fp
size
sum
numbers[1]
numbers[0]
add*
Value of $4
Value of $3
Calculated result
To be stored to $5
Instruction Processing

## Slide 3: Instruction Execution on CPU
To run a software, CPU
  Fetches instructions from memory in the right order
  Decodes the instruction and Reads the operand values from register file
  Executes the computation by using ALU
  Loads/store data from/to memory
  Writes back the computation results to register file
Instruction Fetch
Decode & Register
Identify opcode & read operands
Execute
Mem
Write Result
Write to
dst register

## Slide 4: Implementing a Single-Cycle CPU
All instructions execute in a single clock cycle
  Instructions to Implement: LW, SW; ADD, SUB, AND, OR, SLT; BEQ
  CPI = 1
Different instructions need different execution times
  e.g., LW needs to access memory vs. ADD does not need to access memory
Single-cycle CPU’s clock cycle period should be set to the longest instruction’s execution time

## Slide 5: Fetch Components
Required operations
  Taking address from PC and reading instruction from memory
  Incrementing PC to point at next instruction
Components
  PC register
  Instruction Memory / Cache
  Adder to increment PC value
I-Cache / I-MEM
Addr.
Data
From PC
Instruction Word
PC
+
A
B
CLK
S
Register
Adder
Memory
/
32
/
32
/
32
/
32
/
32
/
32
/
32

## Slide 6: Fetch Data Path
I-Cache / I-MEM
Addr.
Data
Instruction Word
PC
+
A
B
CLK
S
4
Current PC / Read Address
“Next” PC = PC + 4

## Slide 7: Fetch Data Path
PC value serves as address to instruction memory while also being incremented by 4 using the adder
Instruction word is returned by memory after some delay
New PC value is clocked into PC register at the end of clock cycle
I-Cache / I-MEM
Addr.
Data
Instruction Word
PC
+
A
B
CLK
S
4
Current PC / Read Address
“Next” PC = PC + 4
ADD $3,$1,$2
000000
00001
00010
00000
00011
100000
opcode
rs
rt
shamt
rd
func
Current PC
Current PC + 4

## Slide 8: Decode
What is the instruction and operands?
Decode & Register
Identify opcode & read operands
Execute
Mem
Write Result
Write to
dst register

## Slide 9: Instruction Formats
0
rs
rt
rd
shamt
funct
31:26
5:0
25:21
20:16
15:11
10:6
35 or 43
rs
rt
address
31:26
25:21
20:16
15:0
4
rs
rt
address
31:26
25:21
20:16
15:0
R-type
Load/ Store
(I-type)
Branch
(I-type)
opcode
always read
read, except for load
write for R-type and load
sign-extend and add
different ALU instructions

## Slide 10: Decode Components
Register file is a collection of registers
To support R-type instruction,
  4 Input ports: two src register ids, a dst register id and the result value
  2 Output ports: two operand values
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Register File
/
5
/
5
/
5
RegWrite
/
32
/
32
/
32
CLK

## Slide 11: Decode Data Path
5
2
R-type
  Opcode and func. field are decoded to produce control signals
  Three register ids are passed to Register file
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
000000
00001
00010
00000
00011
100000
opcode
rs
rt
shamt
rd
func
Control Signals
Register File
5
1
Value of $1
Value of $2
5
3
Instruction Word
ADD $3,$1,$2
Control Signals for R-type
RegWrite
CLK

## Slide 12: Sign Extension Unit
In a ‘LW’ or ‘SW’ instructions with their base register + offset format, the instruction only contains the offset as a 16-bit value
  Example: LW $4,-8($1)
  Machine Code: 0x8c24fff8
A 16-bit offset must be extended to 32-bits to add to the base register
100011
00001
00100
1111 1111 1111 1000
opcode
rs
rt
offset
Sign Extend
16
32
offset = 0xfff8
0xfffffff8
LW $4,0xfff8($1)

## Slide 13: Decode Data Path
5
4
I-type
  Opcode field is decoded to produce control signals
  Two register ids are passed to Register file
  Offset is sign extended
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
010111
00001
00100
1111 1111 1111 1000
opcode
rs
rt
offset
Control Signals
Register File
5
1
Value of $1
Instruction Word
Sign Extend
16
32
LW $4,0xfff8($1)
RegWrite
CLK

## Slide 14: Execution & Write Result
Let’s execute the instruction!
Execute
Mem
Write Result
Write to
dst register

## Slide 15: Execution Components
ALU is used for
  R-type instructions to operate various arithmetic operations
  LW/SW instructions to operate (base address + offset) to generate the target memory address
  Branch instructions to compare (subtract) the two operand values
Data Memory for LW/SW instructions
Shift-left-2 and another Adder for Branch instructions to calculate new PC value
ALU
/
32
/
32
/
32
ALU Result
Zero
ALU Operation
Data Memory
Read Addr.
Read Data
Write Addr.
Read
Write Data
Write
ALU
Adder
Sum
PC+4 (incremented PC)
Shift Left 2
/
32
/
32
/
32
/
32
/
32
Shift-left-2
Adder
CLK

## Slide 16: Datapath for R-type Instructions
ALU takes inputs from register file and performs the add, sub, and, or, slt, operations
Result is written back to dest. register
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
ALU
Res.
$1 value
$2 value
Sum
1
2
3
Instruc. word
ADD
we_reg
ADD $3,$1,$2
CLK
ALU Operation is determined by a control logic according to Opcode & Funct

## Slide 17: Memory Access Datapath: LW
Operands are read from register file while offset is sign extended
ALU calculates target memory address
Memory access is performed
If LW, read data is written back to register
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
LW $4,0xfff8($1)
$1 value
32
0xffff fff8
Sum
Read Data
1
4
0xfff8
ADD
CLK
CLK

## Slide 18: Memory Access Datapath: SW
Operands are read from register file while offset is sign extended
ALU calculates target memory address
If SW, data is written to the memory
D-Cache /
D-Mem
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
ALU
Res.
Zero
Addr.
Read Data
Write Data
SW $3,0x1a($1)
32
0x0000001a
$1 value
Sum
1
3
$3 value
Write Data
0x001a
ADD
we_dm
CLK
CLK

## Slide 19: Branch Datapath: BEQ
ALU for comparison (examine ‘zero’ output)
Sign extension unit for branch offset
Adder to add PC and offset
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
ALU
Res.
Zero
BEQ $1,$2,offset
$1 value
$2 value
SUB
Sign Extend
extended word offset
Adder
Sum
PC+4 (incremented PC)
Shift Left 2
Branch Target Address to PC
word offset
ZERO
1
2
PC
if(zero == 1)
CLK

## Slide 20: Conclusion Time
What are the stages of single-cycle CPU execution?
What are the two different ways to calculate addresses in the CPU?
Fetch, Decode, Execute, Memory, Writeback
ALU
Shift-left-2 & Adder
 Byte addresses, data access.
 Label, PC.
 IF, ID, EX, MEM, WB