## Slide 1: Lecture 3. Processor Microarchitecture and Design (4)
Haonan Wang
CMPE 200 Computer Architecture & Design

## Slide 2: Cause of Data Hazards
Stalling the pipeline to prevent error:
  All instructions in front of the stalled instruction can continue
  All instructions behind the stalled instruction must also stall
Stalling inserts “bubbles” / nops (no-operations) into the pipeline
  A “nop” is an actual instruction in the MIPS ISA that does NOTHING

## Slide 3: Pipeline Stall for Data Hazards
ADD can read the updated register value from the register file in the same cycle as LW writes the loaded data to register
Do we really need to wait until LW updates the register file?
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10 | CC11 | CC12 | CC13
LW | IF | ID | EXE | MEM | WB |  |  |  |  |  |  |  | 
ADD |  | IF | ID |  |  | EXE | MEM | WB |  |  |  |  | 
Next instr. |  |  | IF |  |  | ID | EXE | MEM | WB |  |  |  | 
Next+1 |  |  |  |  |  | IF | ID | EXE | MEM | WB |  |  | 
Next+2 |  |  |  |  |  |  | IF | ID | EXE | MEM | WB |  | 
Next+3 |  |  |  |  |  |  |  | IF | ID | EXE | MEM | WB | 
Next+4 |  |  |  |  |  |  |  |  | IF | ID | EXE | MEM | WB
nop
nop
nop
nop
Why don’t we use this data directly?

## Slide 4: Data Hazards Solutions
Compiler
  Reorder Code
Hardware
  Use forwarding / bypassing
Data forwarding
  Take results still in the pipeline (not yet written back to a register) and pass them to dependent instructions
  Forwarding Path
    Load instruction: from WB to EXE
    R-type instructions: from MEM to EXE

## Slide 5: Data Forwarding
As far as earlier instruction’s result is in pipeline, the result value can be forwarded to the following instructions
In arithmetic operations, no stall is needed
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
ADD | IF | ID | EXE | MEM | WB |  |  |  |  | 
SUB |  | IF | ID | EXE | MEM | WB |  |  |  | 
XOR |  |  | IF | ID | EXE | MEM | WB |  |  | 
Next+1 |  |  |  | IF | ID | EXE | MEM | WB |  | 
Next+2 |  |  |  |  | IF | ID | EXE | MEM | WB | 
Next+3 |  |  |  |  |  | IF | ID | EXE | MEM | WB
ADD $t3,$t1,$t2
SUB $t5,$t3,$t4
XOR $t7,$t5,$t3

## Slide 6: Forwarding Logic
Forwarding from MEM
  if (we_regM and (rsE ≠ 0) and (rf_waM = rsE)) ForwardAE = 10
  if (we_regM and (rtE ≠ 0) and (rf_waM = rtE)) ForwardBE = 10
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
ADD | IF | ID | EXE | MEM | WB |  |  |  |  | 
SUB |  | IF | ID | EXE | MEM | WB |  |  |  | 
XOR |  |  | IF | ID | EXE | MEM | WB |  |  | 
Next+1 |  |  |  | IF | ID | EXE | MEM | WB |  | 
Next+2 |  |  |  |  | IF | ID | EXE | MEM | WB | 
Next+3 |  |  |  |  |  | IF | ID | EXE | MEM | WB
ADD $t3,$t1,$t2
SUB $t5,$t3,$t4
XOR $t7,$t5,$t3
rsE & rtE
: source register id in EXE stage
rf_waM
: destination register id in MEM stage
we_regM
: register file write enable in MEM stage

## Slide 7: Forwarding Logic
Forwarding from WB
  if (we_regW and (rsE ≠ 0) and (rf_waW = rsE)) ForwardAE = 01
  if (we_regW and (rtE ≠ 0) and (rf_waW = rtE)) ForwardBE = 01
ADD $t3,$t1,$t2
SUB $t5,$t3,$t4
XOR $t7,$t5,$t3
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
ADD | IF | ID | EXE | MEM | WB |  |  |  |  | 
SUB |  | IF | ID | EXE | MEM | WB |  |  |  | 
XOR |  |  | IF | ID | EXE | MEM | WB |  |  | 
Next+1 |  |  |  | IF | ID | EXE | MEM | WB |  | 
Next+2 |  |  |  |  | IF | ID | EXE | MEM | WB | 
Next+3 |  |  |  |  |  | IF | ID | EXE | MEM | WB
rf_waW
: destination register id in WB stage
we_regW
: register file write enable in WB stage

## Slide 8: Forwarding Path
ALU
Res.
D-Cache /
D-Mem
Addr.
Read Data
Write Data
I-Cache / I-MEM
Addr.
Data
PC
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
IF/ID
0
1
EX
M
WB
Control
M
WB
WB
0
1
0
1
2
0
1
2
Forwarding Logic
20:16
15:11
rtE
rdE
rf_waE
25:21
MEM/WB
EX/MEM
rsE
ForwardBE
ForwardAE
rf_waM
rf_waW
Note: Logics for sign extensions and next pc calculation are omitted for simplicity
ID/EX

## Slide 9: Stall With Forwarding
For LW sourced dependency, we still need to stall for one cycle
  Freeze the PC and IF/ID pipeline register for one clock cycle
  Flush the ID/EXE pipeline register
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10 | CC11 | CC12 | CC14
LW | IF | ID | EXE | MEM | WB |  |  |  |  |  |  |  | 
ADD |  | IF | ID | ID | EXE | MEM | WB |  |  |  |  |  | 
Next instr. |  |  | IF | IF | ID | EXE | MEM | WB |  |  |  |  | 
Next+1 |  |  |  |  | IF | ID | EXE | MEM | WB |  |  |  | 
Next+2 |  |  |  |  |  | IF | ID | EXE | MEM | WB |  |  | 
Next+3 |  |  |  |  |  |  | IF | ID | EXE | MEM | WB |  | 
Next+4 |  |  |  |  |  |  |  | IF | ID | EXE | MEM | WB | 
nop
nop

## Slide 10: Forwarding Path
ALU
Res.
D-Cache /
D-Mem
Addr.
Read Data
Write Data
I-Cache / I-MEM
Addr.
Data
PC
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
IF/ID
0
1
EX
M
WB
Control
M
WB
WB
0
1
0
1
2
0
1
2
Forwarding Logic
20:16
15:11
rtE
rdE
rf_waE
25:21
MEM/WB
EX/MEM
rsE
ForwardBE
ForwardAE
rf_waM
rf_waW
Note: Logics for sign extensions and next pc calculation are omitted for simplicity
Hazard detection unit
StallIF
en
StallID
FlushE
ID/EX

## Slide 11: Stalling Condition
Stalling Logic
  lwstall = ((rsD == rtE) or (rtD == rtE)) and dm2regE
  stallF = stallD = FlushE = lwstall
rsD & rtD
: source register id in ID stage
rtE
: destination register in EXE stage
dm2regE
: data memory to register write signal of the instruction in EXE stage

## Slide 12: Current Design

## Slide 13: Pipeline Latency with Forwarding/Stall
Number of cycles we must stall to execute a dependent instruction:
Instruction that is the dependency source | w/o Forwarding (cycles) | w/ Forwarding (cycles)
LW | 2 | 1
Other instructions that update register file | 2 | 0
Data Hazards Solutions:
  - Hardware: stalling & forwarding
  - Software: compiler -- code reordering

## Slide 14: Code Scheduling to Avoid Stalls
Compiler can reorder code to avoid the stalls
C code for A = B + E; C = B + F;
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
Find RAW dependencies and check if stall is needed

## Slide 15: Code Scheduling to Avoid Stalls
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
When forwarding is used,
only lw instruction causes stall
Leave lw instructions only
Compiler can reorder code to avoid the stalls
C code for A = B + E; C = B + F;
Find RAW dependencies and check if stall is needed

## Slide 16: Code Scheduling to Avoid Stalls
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
Compiler can reorder code to avoid the stalls
C code for A = B + E; C = B + F;
Find RAW dependencies and check if stall is needed
lw instructions cause 1-cycle stalls
Leave instructions that are executed back-to-back only

## Slide 17: Code Scheduling to Avoid Stalls
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
Now, check if the lw and dependent instructions must be executed back-to-back
Compiler can reorder code to avoid the stalls
C code for A = B + E; C = B + F;

## Slide 18: Code Scheduling to Avoid Stalls
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
lw $t1, 0($t0)
lw $t2, 4($t0)
lw $t4, 8($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
Compiler can reorder code to avoid the stalls
C code for A = B + E; C = B + F;

## Slide 19: Code Scheduling to Avoid Stalls
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
lw $t1, 0($t0)
lw $t2, 4($t0)
lw $t4, 8($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
stall
stall
5 cycles for the first inst +
6 cycles for the remaining insts +
2 x 1 stall cycles = 13 cycles
Total
execution time
5 cycles for the first inst +
6 cycles for the remaining insts +
0 stall cycles = 11 cycles
Compiler can reorder code to avoid the stalls
C code for A = B + E; C = B + F;

## Slide 20: Control Hazard
Branch outcomes: Taken (T) or Not-Taken (NT)
Not known until late in the pipeline
  Prevents us from fetching future instructions
  Solution: rather than stall, we can predict the outcome and keep fetching
  We only need to correct the pipeline if we guess wrong
Static Predictions
  Predict Taken
  Predict Not Taken
--- beq L1 L2 --- --- --- --- beq L2 L1 ---
T
T
NT
NT

## Slide 21: Statically Predict Not Taken
Keep fetching instructions from the PC + 4 by assuming that the branch will be not taken
Once branch is turned out to be taken, flush the incorrectly fetched instructions
In the following cycle, fetch the instruction from the branch target address

## Slide 22: Statically Predict Not Taken: Issues
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
IF/ID
ID/EX
EX/MEM
MEM/WB
0
1
Next instr. + 2
-- fetch
Next instr. + 1
-- decode
Next instr.
-- execute
BEQ -- If condition
satisfied, update PC
Next instr.
Next instr. + 1
Control / Displacement
Branch outcome only available in MEM stage
 Incorrect instructions already in pipeline

## Slide 23: Statically Predict Not Taken: Issues
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
IF/ID
ID/EX
EX/MEM
MEM/WB
0
1
Fetch from Branch Target Addr.
Flush
Flush
Flush
BEQ

## Slide 24: Static Branch Prediction Penalty
Penalty = number of instructions that need to be flushed on misprediction
For static branch prediction:
  The branch outcome and target address is available at the MEM stage and passed back to the Fetch stage
  If mispredicted, instructions of the correct path will be fetched on the next cycle
A 3-cycle branch penalty when mispredicted

## Slide 25: Statically Predict Not Taken
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM |  |  |  |  |  | 
ADD |  | IF | ID | EXE |  |  |  |  |  | 
SUB |  |  | IF | ID |  |  |  |  |  | 
OR |  |  |  | IF |  |  |  |  |  | 
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $a0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome
NT!

## Slide 26: Statically Predict Not Taken
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM |  |  |  |  | 
SUB |  |  | IF | ID | EXE |  |  |  |  | 
OR |  |  |  | IF | ID |  |  |  |  | 
BNE |  |  |  |  | IF |  |  |  |  | 
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $a0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome

## Slide 27: Statically Predict Not Taken
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM |  |  |  | 
OR |  |  |  | IF | ID | EXE |  |  |  | 
BNE |  |  |  |  | IF | ID |  |  |  | 
AND |  |  |  |  |  | IF |  |  |  | 
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $a0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome

## Slide 28: Statically Predict Not Taken
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM | WB |  |  | 
OR |  |  |  | IF | ID | EXE | MEM | WB |  | 
BNE |  |  |  |  | IF | ID | EXE | MEM |  | 
AND |  |  |  |  |  | IF | ID | EXE |  | 
SW |  |  |  |  |  |  | IF | ID |  | 
LW |  |  |  |  |  |  |  | IF |  | 
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $a0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome
T!
Flush

## Slide 29: Statically Predict Not Taken
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM | WB |  |  | 
OR |  |  |  | IF | ID | EXE | MEM | WB |  | 
BNE |  |  |  |  | IF | ID | EXE | MEM | WB | 
AND |  |  |  |  |  | IF | ID | EXE |  | 
SW |  |  |  |  |  |  | IF | ID |  | 
LW |  |  |  |  |  |  |  | IF |  | 
ADD |  |  |  |  |  |  |  |  | IF | ID
SUB |  |  |  |  |  |  |  |  |  | IF
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $a0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome
Instruction in the
target address (L2)
nop
nop
nop
nop
nop
nop

## Slide 30: Predict Taken?
It is not possible to statically predict all the branches to be taken
  The branch target address is not computed until the EX stage, so we don’t have the PC values even needed to predict taken
Dynamic branch prediction + branch target buffer enables to predict taken
  Predict untaken a few times to collect branch target address of each branch and then predict taken based on the history
Can we reduce branch penalty with change of datapath?

## Slide 31: Early Branch Determination
Target address can be calculated earlier by moving shift-left-2 and Adder
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
IF/ID
ID/EX
EX/MEM
MEM/WB
0
1

## Slide 32: Early Branch Determination
Target address can be calculated earlier by moving shift-left-2 and Adder
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
IF/ID
ID/EX
EX/MEM
MEM/WB
0
1
=
The comparison result is passed to control logic to take branch target address as next PC

## Slide 33: Early Determination w/ Predict NT
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM |  |  |  | 
OR |  |  |  | IF | ID | EXE |  |  |  | 
BNE |  |  |  |  | IF | ID |  |  |  | 
AND |  |  |  |  |  | IF |  |  |  | 
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $a0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome
T!
Flush

## Slide 34: Early Determination w/ Predict NT
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM | WB |  |  | 
OR |  |  |  | IF | ID | EXE | MEM | WB |  | 
BNE |  |  |  |  | IF | ID | EXE | MEM | WB | 
AND |  |  |  |  |  | IF |  |  |  | 
ADD |  |  |  |  |  |  | IF | ID | EXE | MEM
SUB |  |  |  |  |  |  |  | IF | ID | EXE
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $a0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome
Instruction in the
target address (L2)
nop
nop
T!
Flush
nop
nop

## Slide 35: Early Branch Determination: Issues
Target address can be calculated earlier by moving shift-left-2 and Adder
ALU
Res.
Zero
D-Cache /
D-Mem
Addr.
Read Data
Write Data
0
1
0
1
I-Cache / I-MEM
Addr.
Data
PC
CLK
Adder
Sum
Shift Left 2
+
A
B
S
4
0
1
Register File
Read Reg. 1 #
Read Reg. 2 #
Write Reg. #
Write Data
Read data 1
Read data 2
Sign Extend
32
16
IF/ID
ID/EX
EX/MEM
MEM/WB
0
1
=
This may need extra data forwarding and stall
because now the operand value is needed in ID stage (not in EXE stage)

## Slide 36: Early Determination w/ Predict NT
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM |  |  |  | 
OR |  |  |  | IF | ID | EXE |  |  |  | 
BNE |  |  |  |  | IF | ID |  |  |  | 
AND |  |  |  |  |  | IF |  |  |  | 
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $s0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome

## Slide 37: Early Determination w/ Predict NT
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM | WB |  |  | 
OR |  |  |  | IF | ID | EXE | MEM |  |  | 
BNE |  |  |  |  | IF | ID | ID |  |  | 
AND |  |  |  |  |  | IF | IF |  |  | 
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $s0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome
T!

## Slide 38: Early Determination w/ Predict NT
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM | WB |  |  | 
OR |  |  |  | IF | ID | EXE | MEM | WB |  | 
BNE |  |  |  |  | IF | ID | ID | EXE | MEM | WB
AND |  |  |  |  |  | IF | IF |  |  | 
ADD |  |  |  |  |  |  |  | IF | ID | EXE
SUB |  |  |  |  |  |  |  |  | IF | ID
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $s0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome
Instruction in the
target address (L2)
nop
nop
nop
T!
If BNE has dependency with its preceding instruction, OR, one cycle stall is required to get the OR’s result value
 Still better than normal 3 cycle flushing

## Slide 39: Early Branch Determination
Forwarding logic for early branch determination
  ForwardAD = branchD and we_regM and (rsD ≠ 0) and (rf_waM == rsD)
  ForwardBD = branchD and we_regM and (rtD ≠ 0) and (rf_waM == rtD)

## Slide 40: Early Branch Determination
Stalling logic for early branch determination
  branchstall =
  branchD and we_regE and ((rf_waE == rsD) or (rf_waE == rtD))
  or
  branchD and dm2regM and ((rf_waM == rsD) or (rf_waM == rtD))
  StallF = StallD = FlushE = lwstall OR branchstall

## Slide 41: Branch Delay Slot
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM | WB |  |  | 
OR |  |  |  | IF | ID | EXE | MEM | WB |  | 
BNE |  |  |  |  | IF | ID | EXE | MEM | WB | 
AND |  |  |  |  |  | IF |  |  |  | 
ADD |  |  |  |  |  |  | IF | ID | EXE | MEM
SUB |  |  |  |  |  |  |  | IF | ID | EXE
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $a0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome
Instruction in the
target address (L2)
nop
nop
T!
Flush
nop
nop
Find an instruction that
1) has to be executed regardless branch outcome
2) independent to branch
The instruction will be placed in the branch delay slot (right after branch instruction) instead of fetching wrong instruction and flushing

## Slide 42: Branch Delay Slot
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM | WB |  |  | 
BNE |  |  |  | IF | ID | EXE | MEM | WB |  | 
OR |  |  |  |  | IF | ID | EXE | MEM | WB | 
ADD |  |  |  |  |  | IF | ID | EXE | MEM | WB
SUB |  |  |  |  |  |  | IF | ID | EXE | MEM
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
BNE $a0,$s1,L2 (T)
OR $s0,$t6,$t7
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome
Instruction in the
target address (L2)
No Flush
& Better Performance

## Slide 43: Branch Delay Slot
Require implementation on both the CPU and the compiler
  If no suitable instruction can be found for the slot, then a NOP will be filled
Branch delay slot is more beneficial for unconditional branches such as j, jal, jr because they are always taken
For example, if jal uses branch delay slot,
  After jal, $ra is updated with PC + 8
  The instruction in PC + 4 is executed after jal before entering the subfunction
Does branch delay slot make branch prediction useless?

## Slide 44: Conclusion Time
What is the use of ForwardAE and ForwardBE Muxes?
How many cycles can be saved from data forwarding?
Selecting ALU input from different stages
1 or 2