## Slide 1: Lecture 3. Processor Microarchitecture and Design (5)
Haonan Wang
CMPE 200 Computer Architecture & Design

## Slide 2: Dynamic Branch Prediction
Monitor the branch patterns for better prediction
  i.e. loops usually have a few iterations, so the branch in the loop is likely to be not taken at least for a few times
Branch Prediction Buffer (branch history buffer) is used to maintain each branch’s outcome history
  Small storage space indexed with certain bits of branch instruction’s PC value
  Each entry maintains the previous outcome of each branch
  Once the branch outcome is available, the corresponding entry is updated

## Slide 3: Branch Prediction Buffer
Aliasing issue
  Different branch instructions may map to the same branch prediction buffer entry if their PC values have the same LSBs, affecting each others’ predictions
    E.g., 0x8004 and 0x8104 will access the same entry if [3:2] bits are used for indexing
    Inevitable but can be alleviated with larger buffer
1000 0000 0000 0100
Branch instruction’s PC value (i.e. 0x8004)
[3:2] bits
 | prediction bit
0 | 1
1 | 0
2 | 1
3 | 1
Branch Prediction Buffer
The bits to be included to the prediction
may be different depending on the prediction buffer size
1: Predict Taken
0: Predict Not Taken
Prediction bit field can have multiple bits to record more history
 PC can be recorded to predict Taken

## Slide 4: 1-bit Predictor
Each entry of branch prediction buffer is 1-bit (1: Taken, 0: Not Taken)
  The entry value is the latest outcome of the branch
  Next outcome of the branch is predicted based on current value
  Example: Assume that the actual outcomes of the branches at 0xDC04, 0xDC08, and 0xDC20 are untaken, taken, and untaken, respectively
0xDC04 for(i=0;i<10000;i++)
{
0xDC08 if( ( i % 100) == 0 )
tick( );
0xDC20 if( (i % 2) == 0)
even();
}
prediction bit
0
1
0
..
predicted T
predicted NT
predicted NT
Actual result: NT
0
Actual result: NT
1
Actual result: T

## Slide 5: Is 1 bit Enough?
DC04: NNNNNNN ... NNNNNNNNNNT
10,000 iterations
Mis-predictions: 2 / 10,000
NT
TN
DC08: TTTTT ... TNTTTTT … TNTTTTT …
Mis-predictions: 2 / 100
DC20: TNTNTNTNTNTNTNTNTNTNTNTNTNTNT …
Mis-predictions: 2 / 2
Mis-predictions for every
first and last iterations
 99.998% Correct Prediction
98.0% Correct Prediction
0.0% Correct Prediction
10,000 iterations …
NNNNNNNNN …
Not taken and continue to the loop body
Taken to exit the loop

## Slide 6: Using 2-bit History
2-bit Saturating Counter in each branch prediction buffer entry
  Could have more than two bits but two bits cover most patterns (i.e. loops)
0
1
FSM for 1-bit
Prediction
00
01
10
11
FSM for 2-bit
Saturating Counter
Predict NT
Predict T
Transition on T outcome
Transition on NT outcome

## Slide 7: Example
2
T

3
T
3
T


…
3
N

N
1

T
0

0
T
1
T
T
T
T
…
T
1
1
1
1






T
1

T
…
1

0
T
1
T
2
T
3
T
3
T
…
3
T






Initial Training/Warm-up
1-bit
Predictor
2-bit
Predictor
Only 1 Misprediction per N branches now!
Correct prediction rates:
DC04: 99.999% , DC08: 99.0%, DC20: 50%

## Slide 8: Pipelined CPU Performance Analysis
Critical path = max {
Tpcq + Ti-mem + Tsetup,
2 ( TRFread + Tmux + Teq + TAND + Tmux + Tsetup ),
Tpcq + Tmux + Tmux + TALU + Tsetup,
Tpcq + Tmemread + Tsetup,
2 ( Tpcq + Tmux + TRFwrite )
}
Function Unit | Parameter | Delay (ps)
Register clock-to-Q | Tpcq | 30
Clock setup time | Tsetup | 20
MUX | TMUX | 25
Sign-extend | Ts_ext | 25
ALU | TALU | 200
Mem read | Tmem | 250
AND | TAND | 15
EQ | Teq | 40
Register file read | TRFread | 150
Register file write | TRFwrite | 20
RF write and read need to be finished in the first and second half of each cycle, respectively

## Slide 9: Pipelined CPU Performance Analysis
Critical path = 2 ( TRFread + Tmux + Teq + TAND + Tmux + Tsetup )
= 2 ( 150 + 25 + 40 + 15 + 25 + 20 ) = 550 ps
Function Unit | Parameter | Delay (ps)
Register clock-to-Q | Tpcq | 30
Clock setup time | Tsetup | 20
MUX | TMUX | 25
Sign-extend | Ts_ext | 25
ALU | TALU | 200
Mem read | Tmem | 250
AND | TAND | 15
EQ | Teq | 40
Register file read | TRFread | 150
Register file write | TRFwrite | 20

## Slide 10: Pipelined CPU Performance Analysis
SPECINT2000 benchmark:
  25% loads, 10% stores, 11% branches, 2% jumps, 52% R-type
Assume:
  40% of loads used by next instruction
  25% of branches mispredicted
  All jumps flush next instruction
Average CPI calculation:
  Load/Branch CPI = 1 when no stalling, 2 when stalling
  CPIlw = 1(0.6) + 2(0.4) = 1.4
  CPIbeq = 1(0.75) + 2(0.25) = 1.25
  Overall average CPI = (0.25 x 1.4) + (0.1 x 1) + (0.11 x 1.25) + (0.02 x 2) + (0.52 x 1) = 1.15

## Slide 11: Pipelined CPU Performance Analysis
For a program with 100 billion instructions executing on the pipelined MIPS processor under discussion, execution time is
CPU time = # instructions x CPI x cycle time
= (100 x 109) x 1.15 x (550 x 10-12 sec)
= 63 seconds
Recall: when we ran the same code on a single-cycle processor (Lecture 4 – (3)), CPU time was 92.5 seconds.
Speedup of pipelined architecture = 92.5 / 63 = 1.47x

## Slide 12: Question
Suppose we are writing code for a machine with unknown branch predictor. We found that certain loops containing branch instructions have long execution times. What can we do?
Swap the branches