## Slide 1: Lecture 4. Memory Hierarchy (1)
Haonan Wang
CMPE 200 Computer Architecture & Design

## Slide 2: Computer Architecture Overview
Software/Applications
Processor
Operating System
Instruction Set
Architecture
Firmware
Compiler
Registers
Cache
Memory
HDD/SSD
Memory Hierarchy

## Slide 3: Memory Hierarchy
#include <stdio.h>
#include <string.h>
int numbers[2];
void myfunction(void)
{
FILE *fp;
int size = 2;
int sum = 0;
/* Open file for reading */
fp = fopen(“mynumbers.txt", “r");
/* Read and display data */
fread(numbers, sizeof(int), size, fp);
fclose(fp);
sum = numbers[0] + numbers[1];
printf(“Sum = %d\n”, sum);
}
int main (void) {
myfunction();
return(0);
}
Example: a C program that reads
two integer values from “file.txt” file
and prints the sum of them.
Processor
(CPU)
Understands and executes each line of the code.
Uses fast on-chip memories
Memory
(DRAM)
Provides operands to CPU
(*fp, size, sum, numbers[2])
Storage
(HDD)
Provides file inputs and program code
(file.txt)

## Slide 4: Memory Hierarchy
On-chip Memories (Memories inside of CPU)
  Register file, Caches
  Small but Fast
CPU
Register File
Instruction
Cache
Data
Cache

## Slide 5: Memory Hierarchy
Off-chip Memories (Memories outside CPU)
  System Memory, Storage
  Large but Slow
System Memory
Storage
CPU

## Slide 6: Memory Hierarchy
Processor
Registers
Cache
Memory
HDD/SSD
Fast
Slow
Cheap
Expensive
Access
Speed
Price/unit
0.5ns ~ 2.5ns
$2000 ~ $5000 per GB
50ns ~ 200ns
$20 ~ $75 per GB
5ms ~ 20ms
$0.2 ~ $2 per GB
On-chip:
Subset of memory
Volatile Memory
Non-volatile Memory
(NVM)
Off-chip:
full memory
Software managed
1 register = 1 word
Hardware managed
1 block = multiple words

## Slide 7: Memories in Your PC
Windows
  This PC  Properties
  cmd window  wmic
  3rd party tool like CPU-Z
Linux
  lscpu
  cat /proc/cpuinfo
  etc.
System Memory
Storage
Caches

## Slide 8: Discussion
Why should we use this hierarchy design?
How would you design the memory system?
Single piece of memory that does everything
Vs.
Multiple levels of memories

## Slide 9: Why?
Two Types of Locality:
  Temporal Locality (Locality in Time): If an address is referenced, it tends to be referenced again (e.g., loops, variable reuse)
  Spatial Locality (Locality in Space): If an address is referenced, neighboring addresses tend to be referenced (e.g., array, stack, etc.)
On-chip
Off-chip

## Slide 10: The “Memory Wall”
“Moore’s Law”
CPU ~55%/year
(2X/1.5yr)
DRAM
7%/year
(2X/10yrs)
Processor-Memory
Performance Gap (grows 50%/year)

## Slide 11: The Memory Hierarchy Goal
How do we create a memory system that gives the illusion of being large, cheap and fast (most of the time)?
  With hierarchy
    try the fast parts first -- most of the time, this works well
    if not, move the data so it works well the next time
  With parallelism
    use multiple identical parts operating simultaneously
    for large quantities of data, this works well
Example – keep a subset of the data in fast memory
Example – 1-byte-wide memory  4 × 1-byte-wide memory  4-byte-wide memory
  load word takes 4 memory cycles vs. 1 memory cycle

## Slide 12: Let us Conclude
What is cache?
What are the two types of data localities?
Fast memory
Temporal & Spatial
What are the two memory design directions inspired by the principle of locality?
Hierarchy & parallelism