## Slide 1: Lecture 4. Memory Hierarchy (2)
Haonan Wang
CMPE 200 Computer Architecture & Design

## Slide 2: Cache Design
Caches use SRAM for speed and technology compatibility
  Low density (6 transistor cells), high power, expensive, fast
  Static: content will last “forever” (until power turned off)
Example: A (2M X 16 bit) SRAM logic
Dout[15-0]
SRAM
2M x 16
Din[15-0]
Address
Chip select
Output enable
Write enable
16
16
21

## Slide 3: SRAM Cache Design
r
o
w
d
e
c
o
d
e
r
row
address
4-bit data word
SRAM Cell
Array
word (row)
select line
bit (data) lines
Each intersection represents a
6-T SRAM cell
Column Selector &
I/O Circuits
column
address
Each row holds a data block
Column address selects the requested word from block

## Slide 4: Cache Hit and Miss
Hit: Data appears in some block of the cache
  Hit Rate: # hits / total accesses on the cache
  Hit Time: Time to access the cache
Miss: Data needs to be retrieved from the lower level (and stored in cache)
  Miss Rate: 1 - (Hit Rate)
  Miss Penalty: Average delay in the processor caused by each miss
Lower Level Memory
(cache/main memory)
Cache
To Processor
From Processor
data block X
data block Y
Can’t find!
Miss
Hit
Hit
read
read

## Slide 5: Memory Hierarchy Performance
Average Memory Access Time (AMAT)
= Hit Time + Miss rate x Miss Penalty
Example:
  Cache Hit = 1 cycle
  Miss rate = 10% = 0.1
  Miss penalty = 300 cycles
  AMAT = Thit(L1) + Miss_rate(L1) x T(Memory) = 1 + 0.1 x 300 = 31 cycles
Main
Memory
(DRAM)
First-level
Cache
Hit Time
Miss penalty
1 cycle
300 cycles
Due to long-latency memory, AMAT is 30 cycles longer than cache latency.
Can we reduce the overhead?

## Slide 6: Reducing Penalty: Multi-Level Cache
Main
Memory
(DRAM)
Second
Level
Cache
Third
Level
Cache
300 cycles
20 cycles
10 cycles
On Processor Die
L1
L2
L3
First-level
Cache
Hit Time
1 cycle
Off-Chip

## Slide 7: Reducing Penalty: Multi-Level Cache
AMAT in multi-level cache organization
  = Thit(L1) + Miss_rate(L1) x Miss_penalty(L1)
Main
Memory
(DRAM)
Second
Level
Cache
Third
Level
Cache
300 cycles
20 cycles
10 cycles
On Processor Die
L1
L2
L3
First-level
Cache
Hit Time
1 cycle
Off-Chip

## Slide 8: Reducing Penalty: Multi-Level Cache
AMAT in multi-level cache organization
  = Thit(L1) + Miss_rate(L1) x
  [ Thit(L2) + Miss_rate(L2) x Miss_penalty(L2) ]
Main
Memory
(DRAM)
Second
Level
Cache
Third
Level
Cache
300 cycles
20 cycles
10 cycles
On Processor Die
L1
L2
L3
First-level
Cache
Hit Time
1 cycle
Off-Chip

## Slide 9: Reducing Penalty: Multi-Level Cache
AMAT in multi-level cache organization
  = Thit(L1) + Miss_rate(L1) x
  [ Thit(L2) + Miss_rate(L2) x
  { Thit(L3) + Miss_rate(L3) x Miss_penalty(L3) } ]
Main
Memory
(DRAM)
Second
Level
Cache
Third
Level
Cache
300 cycles
20 cycles
10 cycles
On Processor Die
L1
L2
L3
First-level
Cache
Hit Time
1 cycle
Off-Chip

## Slide 10: Reducing Penalty: Multi-Level Cache
AMAT in multi-level cache organization
  = Thit(L1) + Miss_rate(L1) x
  [ Thit(L2) + Miss_rate(L2) x
  { Thit(L3) + Miss_rate(L3) x T(memory) } ]
Main
Memory
(DRAM)
Second
Level
Cache
Third
Level
Cache
300 cycles
20 cycles
10 cycles
On Processor Die
L1
L2
L3
First-level
Cache
Hit Time
1 cycle
Off-Chip

## Slide 11: Reducing Penalty: Multi-Level Cache
AMAT in multi-level cache organization
  = Thit(L1) + Miss_rate(L1) x
  [ Thit(L2) + Miss_rate(L2) x
  { Thit(L3) + Miss_rate(L3) x T(memory) } ]
Example:
  Miss rate of L1, L2, L3 = 10%, 5%, 1%, respectively
  AMAT = 1 + 0.1 x [ 10 + 0.05 x { 20 + 0.01 x 300 } ] = 2.115 cycles
Second
Level
Cache
Third
Level
Cache
300 cycles
20 cycles
10 cycles
On Processor Die
L1
L2
L3
First-level
Cache
Hit Time
1 cycle
Vs. 31 cycles
14.7x speedup!
Main
Memory
(DRAM)
Off-Chip
Are more levels always good?

## Slide 12: Discussion
Background: The cache space is limited. We can only keep a subset of data in cache.
Question: What happens when the cache is full?
Question: What to keep in the cache (which block should be evicted)?

## Slide 13: What to Keep in Caches (1)?
It depends on the cache organization and replacing policy.
Cache organization:
  Cache line (block): The basic unit of data replacement. A longer cache line fetches and replaces more data per miss.
  Set: An entry that one cache line is mapped to according to certain bits of its address.
  Way: A slot within a cache set to hold one history cache line.
Way 0
Way 1
Set 0
Set 1
block 0
block 1
block 2
block 3
…
…

## Slide 14: What to Keep in Caches (2)?
It depends on the cache organization and replacing policy
Cache line replacing policy: which history line should be replaced?
  In a set entry, each cache line can be identified with a Tag (a portion of its address).
  Least recently used (LRU), First-in first-out (FIFO), Random, etc.
Block offset
Byte offset
Index
Tag
Selects the set
Used for tag compare
Selects the word in the block
Data (e.g., 64 Bytes)
Tag
Valid
Address decoding:
Cache line:
History bits

## Slide 15: Cache Indexing
Block offset
Byte offset
Index
Tag
Selects the set
Used for tag compare
Selects the word in the block
Way 0
Way 1
Set 0
Set 1
Example: a simple 2-set x 2-way cache
block 0
block 1
block 2
block 3
Address decoding:

## Slide 16: Cache Types
N-way Set-Associative: Number of ways > 1 & Number of sets > 1
  Slightly complex searching mechanism
Direct Mapped: Number of ways = 1
  Fast indexing mechanism
Fully-Associative: Number of sets = 1
  Extensive hardware resources required to search
Way 0
Way 1
Set 0
Set 1
block 0
block 1
block 2
block 3
…
…

## Slide 17: Cache Types
Block offset
Byte offset
Index
Tag
Decreasing associativity
Fully associative (only one set)
Direct mapped (only one way)
Increasing associativity
Selects the set
Used for tag compare
Selects the word in the block
Assuming fixed sized cache:
Way 0
Way 1
Set 0
Set 1
block 0
block 1
block 2
block 3
…
…