## Slide 1: Lecture 4. Memory Hierarchy (4)
Haonan Wang
CMPE 200 Computer Architecture & Design

## Slide 2: Cache Policies: Cases
Allocation policy: do we allocate a block in cache for the missed data?
Read policies:
  Read Hit: this is what we want. Only one data read from the cache.
  Read Miss: needs to fetch from lower level, but just write to the register once after that
    read-allocate (with replacement policy) vs. no-read-allocate (i.e., cache bypassing)
Write policies (only for the data cache): consistency & performance tradeoffs
  Write Hit: behavior and number of writes depends on write policy
    Write-through vs. write-back vs. write-evict
  Write Miss: needs to first read from lower level, then apply write policies
    Write-allocate (with replacement policy): Write-through vs. Write-back
    No-write-allocate (bypassing): Write-evict

## Slide 3: Write Policy: Write-back
Write-back: inconsistent with lower level
  The value is written only to the cache line.
  The modified (dirty) cache line is written to the lower level only when it is evicted.
    1 dirty bit is needed for each cache line.
  A write-back buffer to update lower level with evicted dirty blocks
    Must write a full block at this point since we do not know which word is modified
  Example: assume cache block containing word address A is initially in the cache
A
A
SW to A
A
B
dirty bit (A) = 1
dirty bit (A) = 0

## Slide 4: Write Policy: Write-back
A
LW B
A
B
A few cycles later...
L1 is full and A is selected to be replaced by B
dirty bit (A) = 1
Write-back: inconsistent with lower level
  The value is written only to the cache line.
  The modified (dirty) cache line is written to the lower level only when it is evicted.
    1 dirty bit is needed for each cache line.
  A write-back buffer to update lower level with evicted dirty blocks
    Must write a full block at this point since we do not know which word is modified
  Example: assume cache block containing word address A is initially in the cache
If A was not modified (dirty bit = 0) when replaced, A is not updated to lower mem.

## Slide 5: Write Policy: Write-through
Write-through: consistent with lower level
  The value is written to both the cache line and the lower-level memory.
    No need to write a full block to the lower level (e.g., only write 4B for a SW)
  Write buffer can be used so cache does not need to wait for the write to lower level
    stall only if the write buffer is full
  Example: assume cache block containing word address A is initially in the cache
A
A
SW to A
A
A

## Slide 6: Write Policy: Write-through
A
A
A
Write-through: consistent with lower level
  The value is written to both the cache line and the lower-level memory.
    No need to write a full block to the lower level (e.g., only write 4B for a SW)
  Write buffer can be used so cache does not need to wait for the write to lower level
    stall only if the write buffer is full
  Example: assume cache block containing word address A is initially in the cache

## Slide 7: Write Policy: Write-evict
Write-evict (no-write): no consistency issue
  The value is written only to the lower level (i.e., bypassing).
  No need to fetch the data first if it is missing in the cache
  If the block containing the write address exists in the cache, evict it.
  The write only needs to send the data specified by the store instruction (e.g., 4 Bytes).
  Write buffer can be used so cache does not need to wait for the write to lower level
  More expensive when there is read after write

## Slide 8: Cache Policies: Cases - Revisit
Allocation policy: do we allocate a block in cache for the missed data?
Read policies:
  Read Hit: this is what we want. Only one data read from the cache.
  Read Miss: needs to fetch from lower level, but just write to the register once after that
    read-allocate (with replacement policy) vs. no-read-allocate (i.e., cache bypassing)
Write policies (only for the data cache): consistency & performance tradeoffs
  Write Hit: behavior and number of writes depends on write policy
    Write-through vs. write-back vs. write-evict
  Write Miss: needs to first read from lower level, then apply write policies
    Write-allocate (with replacement policy): Write-through vs. Write-back
    No-write-allocate (bypassing): Write-evict
What else must be considered?
+ write policy of evicted data
+ write policy of evicted data

## Slide 9: Cache Miss Behavior Analysis
Read miss:
  +Write-through: evict victim block + fetch block from lower level
  +Write-back: evict victim block + write back evicted block if dirty + fetch block from lower level
  +No-write: find victim block + fetch block from lower level
Write miss:
  Write-allocate:
    +Write-through: evict victim block + fetch block from lower level + store word to block + store word to lower level
    +Write-back: evict victim block + write back evicted block if dirty + fetch block from lower level + store word to block
  No-write-allocate: +Write-evict: store word to lower level directly

## Slide 10: Other Cache Policy details
Some caches support multiple policies
  Can achieve different delay/bandwidth tradeoffs or even dynamically change
Write hit and write miss can use different policies
  E.g., write-hit write-evict + write-miss write-allocate-write-back
Different cache levels can also use different policies
  E.g., L1 use write-evict + L2 use write-back
Cache can also be completely bypassed (not the same as write-evict)
  E.g., bypassing L1

## Slide 11: Reduce Miss Rate (1): Code Optimization
Misses occur if sequentially accessed array elements come from different cache blocks
Code optimizations  No hardware change
  Rely on programmers or compilers
Examples:
  Loop interchange: In nested loops, outer loop becomes inner loop and vice versa
  Loop blocking: partition large array into smaller blocks, thus fitting the accessed array elements into cache size

## Slide 12: Loop Interchange
/* Before */
for (j=0; j<5; j++)
for (i=0; i<5; i++)
x[i][j] = 2*x[i][j]
/* After */
for (i=0; i<5; i++)
for (j=0; j<5; j++)
x[i][j] = 2*x[i][j]
Column-major ordering
Row-major ordering
i
j
i
j
each loop iteration accesses different cache line
The same cache line is accessed for a couple of iterations
Assume: cache line size = 5 words
What addresses are accessed in each iteration of inner loop?
five consecutive words belong to a cache line

## Slide 13: Loop Blocking
X
=
/* Before */
for (i=0; i<N; i++)
for (j=0; j<N; j++)
for (k=0; k<N; k++)
C[i][j] = C[i][j] + A[i][k] * B[k][j];
In the traditional matrix multiplication:
To generate one output element (red color), the 6 elements of each input matrix (gray color) will be accessed.

## Slide 14
X
=
Loop Blocking
/* Before */
for (i=0; i<N; i++)
for (j=0; j<N; j++)
for (k=0; k<N; k++)
C[i][j] = C[i][j] + A[i][k] * B[k][j];
In the traditional matrix multiplication:
To generate one output element (red color), the 6 elements of each input matrix (gray color) will be accessed.

## Slide 15: Loop Blocking
X
=
/* Before */
for (i=0; i<N; i++)
for (j=0; j<N; j++)
for (k=0; k<N; k++)
C[i][j] = C[i][j] + A[i][k] * B[k][j];
In the traditional matrix multiplication:
To generate one output element (red color), the 6 elements of each input matrix (gray color) will be accessed.

## Slide 16: Loop Blocking
X
=
/* Before */
for (i=0; i<N; i++)
for (j=0; j<N; j++)
for (k=0; k<N; k++)
C[i][j] = C[i][j] + A[i][k] * B[k][j];
In the traditional matrix multiplication:
To generate one output element (red color), the 6 elements of each input matrix (gray color) will be accessed.

## Slide 17: Loop Blocking
X
=
/* Before */
for (i=0; i<N; i++)
for (j=0; j<N; j++)
for (k=0; k<N; k++)
C[i][j] = C[i][j] + A[i][k] * B[k][j];
To generate one output element (red color), the 6 elements of each input matrix (gray color) will be accessed.
In the traditional matrix multiplication:

## Slide 18: Loop Blocking
X
=
/* Before */
for (i=0; i<N; i++)
for (j=0; j<N; j++)
for (k=0; k<N; k++)
C[i][j] = C[i][j] + A[i][k] * B[k][j];
The second matrix may always encounter misses because individual data are from different cache blocks
In the traditional matrix multiplication:
To generate one output element (red color), the 6 elements of each input matrix (gray color) will be accessed.

## Slide 19: Loop Blocking
X
=
/* Before */
for (i=0; i<N; i++)
for (j=0; j<N; j++)
for (k=0; k<N; k++)
C[i][j] = C[i][j] + A[i][k] * B[k][j];
If N is large, the cache line that has been accessed is likely to be replaced before next access
In the traditional matrix multiplication:
To generate one output element (red color), the 6 elements of each input matrix (gray color) will be accessed.

## Slide 20: Loop Blocking
X
=
/* After (block size = 4) */
for (i=0; i<N; i=i+b)
for (j=0; j<N; j=j+b)
for (k=0; k<N; k=k+b)
for (ii=i; ii<i+b; ii++)
for (jj=j; jj<j+b; jj++)
for (kk=k; kk<k+b; kk++)
C[ii][jj] = C[ii][jj] + A[ii][kk] * B[kk][jj];
Matrix is computed in a smaller block unit
 higher locality
In the block-based matrix multiplication:

## Slide 21: Loop Blocking
X
=
/* After (block size = 4) */
for (i=0; i<N; i=i+b)
for (j=0; j<N; j=j+b)
for (k=0; k<N; k=k+b)
for (ii=i; ii<i+b; ii++)
for (jj=j; jj<j+b; jj++)
for (kk=k; kk<k+b; kk++)
C[ii][jj] = C[ii][jj] + A[ii][kk] * B[kk][jj];
In the block-based matrix multiplication:

## Slide 22: Loop Blocking
X
=
/* After (block size = 4) */
for (i=0; i<N; i=i+b)
for (j=0; j<N; j=j+b)
for (k=0; k<N; k=k+b)
for (ii=i; ii<i+b; ii++)
for (jj=j; jj<j+b; jj++)
for (kk=k; kk<k+b; kk++)
C[ii][jj] = C[ii][jj] + A[ii][kk] * B[kk][jj];
In the block-based matrix multiplication:

## Slide 23: Loop Blocking
X
=
/* After (block size = 4) */
for (i=0; i<N; i=i+b)
for (j=0; j<N; j=j+b)
for (k=0; k<N; k=k+b)
for (ii=i; ii<i+b; ii++)
for (jj=j; jj<j+b; jj++)
for (kk=k; kk<k+b; kk++)
C[ii][jj] = C[ii][jj] + A[ii][kk] * B[kk][jj];
In the block-based matrix multiplication:

## Slide 24: Loop Blocking
X
=
/* After (block size = 4) */
for (i=0; i<N; i=i+b)
for (j=0; j<N; j=j+b)
for (k=0; k<N; k=k+b)
for (ii=i; ii<i+b; ii++)
for (jj=j; jj<j+b; jj++)
for (kk=k; kk<k+b; kk++)
C[ii][jj] = C[ii][jj] + A[ii][kk] * B[kk][jj];
In the block-based matrix multiplication:

## Slide 25: Loop Blocking
X
=
/* After (block size = 4) */
for (i=0; i<N; i=i+b)
for (j=0; j<N; j=j+b)
for (k=0; k<N; k=k+b)
for (ii=i; ii<i+b; ii++)
for (jj=j; jj<j+b; jj++)
for (kk=k; kk<k+b; kk++)
C[ii][jj] = C[ii][jj] + A[ii][kk] * B[kk][jj];
In the block-based matrix multiplication:

## Slide 26: Loop Blocking
X
=
/* After (block size = 4) */
for (i=0; i<N; i=i+b)
for (j=0; j<N; j=j+b)
for (k=0; k<N; k=k+b)
for (ii=i; ii<i+b; ii++)
for (jj=j; jj<j+b; jj++)
for (kk=k; kk<k+b; kk++)
C[ii][jj] = C[ii][jj] + A[ii][kk] * B[kk][jj];
In the block-based matrix multiplication:

## Slide 27: Cache Miss Classification: The 3 C’s
Compulsory (cold) Misses
  On the 1st reference to a block
  Related to # blocks accessed by a code, not related to the configuration of a cache
Capacity Misses
  The program’s working set size exceeds the cache capacity
Conflict Misses
  Multiple memory blocks map to the same set in set-associative caches

## Slide 28: Reduce Miss Rate (2): Reduce the 3 C’s
Increase Cache Size
  Reduce miss for: capacity miss, conflict miss
  But has many limitations
Increase Associativity (cache size unchanged)
  Reduce miss for: conflict miss
  But may increase access latency
Increase Cache Block Size (cache size unchanged)
  Reduce miss for: compulsory
  But may increase miss penalty (more data will be evicted and fetched)
  Very large blocks could increase miss rate (i.e., increase capacity miss)

## Slide 29: Increase Cache Size

## Slide 30
Miss Rate vs Block Size vs Cache Size
Chart: Block size (bytes)
| 16 | 32 | 64 | 128 | 256
8 KB | 8.5 | 7.5 | 7.25 | 7.75 | 9.5
16 KB | 4 | 2.75 | 2.75 | 3 | 3.5
64 KB | 2 | 1.7 | 1.55 | 1.4 | 1.4
256 KB | 1 | 0.7 | 0.5 | 0.5 | 0.6
Cache size – the larger the better
Block size – tradeoffs
Why?

## Slide 31
Miss
Penalty
Block Size
Miss
Rate
Exploits Spatial Locality
Fewer blocks -- increases capacity misses
Block Size
Average
Access
Time
Increased Miss Penalty
& Miss Rate
Block Size
Average Memory Access Time = Hit Time + Miss Penalty x Miss Rate
Block Size Tradeoff

## Slide 32
Benefits of Set Associative Caches
Data from Hennessy & Patterson, Computer Architecture
Largest gains when going from direct mapped to 2-way (20%+ reduction in miss rate)

## Slide 33: Reduce Miss Rate (3): Policies
Use appropriate policies
  LRU + write-back works for most applications
  Many GPUs use write-hit write-evict + write-miss no-write-allocate
  Can even dynamically change policy according to profiling
Use more advanced policies
  E.g., ML based

## Slide 34: Reduce Miss Rate (4): Multi-level Caches
Having a unified L2 cache (i.e., it holds both instructions and data) and in some cases even a unified L3 cache
L1 cache should focus on minimizing hit time in support of a shorter clock cycle
Secondary cache(s) should focus on reducing miss rate to reduce the penalty of long main memory access times

## Slide 35: Split vs. Unified Caches
Split L1I$ and L1D$: to optimize thit
  Low capacity/associativity/block size (reduce thit)
  Minimize structural hazards
  Can optimize L1I$ for wide output and no writes
Unified L2: to optimize hit rate
  thit is less important due to less frequent accesses & long delay already
  High capacity/associativity/block size (reduce %miss)
    Unused instr capacity can be used for data (fewer capacity misses)
    Instr / data conflicts (small to no increase for conflict misses in a large cache)
  Instr / data structural hazards are rare (would take a simultaneous L1I$ and L1D$ miss)

## Slide 36: Reduce Miss Rate (5): Prefetching
Hardware prefetching
  Fetch blocks into the cache proactively (speculatively)
  Key is to anticipate the upcoming miss addresses accurately
  Relies on having unused memory bandwidth available
A simple case is to use next block prefetching
  Miss on address X → anticipate next reference miss on X + block-size
  Works well for instructions (sequential execution) and for arrays of data
Need to initiate prefetches sufficiently in advance
If prefetched instruction/data is not used, the cache is polluted with unnecessary data (possibly evicting useful data)

## Slide 37: Other than Miss Rates
Cache bypassing (e.g., L1D)
  Reduce latency if L1 misses
Sector cache
  Fetch only a portion of the cache line
  Not the same as reducing cache line size
Value prediction
  Using history value to predict future values
  Roll back if predict wrong
  Or accept a certain quality loss if the application is error tolerant

## Slide 38: Let us Conclude
What are the operations in cache for write-miss when using write-back?
List two ways of code optimizations to improve locality?
evict victim block + write back evicted block if dirty + fetch block from lower level + store word to block
Loop interchange, Loop blocking

## Slide 39: Conclusion Time
What are some ways to reduce cache misses?
Software methods, reduce 3C’s, changing policies, multi-level caches, prefetching, value prediction …