## Slide 1: Lecture 4. Memory Hierarchy (5)
Haonan Wang
CMPE 200 Computer Architecture & Design

## Slide 2: DRAM Subsystem Organization
  Dram: Dynamic RAM
DRAM Organization:
Channel
DIMM
Rank
Chip
Bank
Row/Column
Connected to an on-die memory controller

## Slide 3: DRAM Cells
A DRAM cell consists of a capacitor and an access transistor
It stores data in terms of charge in the capacitor
Cheaper and larger than SRAM
  A DRAM chip consists of (10s of 1000s of) rows of such cells
wordline
bitline
bitline
bitline
(row enable)
row
column
column
column

## Slide 4: DRAM Refresh
DRAM capacitor charge leaks over time
The memory controller needs to refresh each row periodically to restore charge
  Dynamic (i.e., never in a stable state)
  Activate each row every N ms (e.g., typical N = 64)
Downsides of refresh
  Energy consumption: Each refresh consumes energy
  Performance degradation: DRAM rank/bank unavailable while refreshed
  QoS/predictability impact: (Long) pause times during refresh
  Refresh rate limits DRAM capacity scaling

## Slide 5: Recall: SRAM Cache Design
r
o
w
d
e
c
o
d
e
r
row
address
4-bit data word
SRAM Cell
Array
word (row)
select line
bit (data) lines
Each intersection represents a
6-T SRAM cell
Column Selector &
I/O Circuits
column
address
Each row holds a data block
Column address selects the requested word from block

## Slide 6
data bit
data bit
r
o
w
d
e
c
o
d
e
r
row
Address
(RAS)
Column Selector &
I/O Circuits
column
Address
(CAS)
data bit
bit (data) lines
Each intersection represents a 1-T DRAM cell
The column address selects the requested bit from the row in each plane
data word
. . .
. . .
DRAM Cell Array
word (row) select line
m planes
DRAM Design 1: The Classical
DRAM Bank

## Slide 7
DRAM addresses are divided into 2 halves (row and column)
  RAS or Row Access Strobe that triggers the row decoder
  CAS or Column Access Strobe that triggers the column selector
Latency: Time to access one word
  Access Time: time taken when word is read or written
    read access and write access times can be different
  Cycle Time: time between successive (read or write) requests
Bandwidth: How much data can be supplied per unit time
  Width of the data channel * channel usage frequency
DRAM Performance Metrics

## Slide 8
DRAM Organization:
  N rows x N column x M-bit (planes)
  Reads or Writes M-bit at a time
  Each M-bit access requires a RAS / CAS cycle
Row Address
CAS
RAS
Col Address
Row Address
Col Address
Access Time
Cycle Time
1st M-bit
2nd M-bit
DRAM Design 1: The Classical

## Slide 9
Row Address
CAS
RAS
Col Address
Col Address
1st M-bit
Col Address
Col Address
2nd M-bit
3rd M-bit
4th M-bit
Cycle Time
Page Mode: A row is kept “open” by keeping the RAS asserted
  Pulse CAS to access other M-bit blocks on that row
  Successive reads or writes within the row are faster since don’t have to precharge and (re)access that row
DRAM Design 1: The Classical

## Slide 10: DRAM Design 2: Synchronous DRAMs
Like page mode DRAMs, synchronous DRAMs (SDRAMs) can transfer a burst of data from a series of sequential addresses in the same row
For words in the same burst, don’t have to provide the complete (row and column) addresses
  The entire row is loaded into a row buffer (SRAM).
  Specify the starting (row+column) address and the burst length (burst must be in the same row).
  Data words in the burst are then accessed from that SRAM under control of a clock signal.

## Slide 11
Row Address
CAS
RAS
Col Address
1st
M-bit
http://en.wikipedia.org/wiki/DDR_SDRAM
2nd
M-bit
3rd
M-bit
clock
Synchronous DRAM (SDRAM) Operation
After RAS loads a row into the SRAM cache
  Input CAS as the starting “burst” address along with a burst length to read a burst of data from a series of sequential addresses within that row on the clock edge
…

## Slide 12
Row Address
CAS
RAS
Col Address
1st
M-bit
Row Address
http://en.wikipedia.org/wiki/DDR_SDRAM
2nd
M-bit
3rd
M-bit
4th
M-bit
clock
DDR (Double Data Rate) SDRAMs
Transfers burst data on both the rising and falling edge of the clock (so twice fast)
  2n core prefectch

## Slide 13
DDR (Double Data Rate) SDRAMs
DDR1 VS DDR1+:
DDR2 vs. QDR

## Slide 14: DRAM Subsystem Organization
  Dram: Dynamic RAM
DRAM Organization:
Channel
DIMM
Rank
Chip
Bank
Row/Column
Chip:
  Consists of multiple banks (2-16 in Synchronous DRAM)
    Banks works in parallel to overlap delay
  Banks share command/address/data buses
  The chip itself has a narrow interface (4-16 bits per read)

## Slide 15: DRAM Subsystem Organization
  Dram: Dynamic RAM
DRAM Organization:
Channel
DIMM
Rank
Chip
Bank
Row/Column
Rank:
  Multiple chips operated together to form a wide interface
  All chips comprising a rank are controlled at the same time
    Respond to a single command
    Share address and command buses, but provide different data
  E.g., Using 8 chips with 8-bit interface to form a 64-bit wide Rank

## Slide 16: DRAM Subsystem Organization
  Dram: Dynamic RAM
DRAM Organization:
Channel
DIMM
Rank
Chip
Bank
Row/Column
DIMM (dual inline memory module):
  A DRAM module consists of one or more ranks
  This is what you plug into your motherboard

## Slide 17: DIMM (Dual Inline Memory Module)
Contains DRAM chips each have data widths of x4 or x8
  Can be on both sides
Can have more than one rank
  Increase storage capacity
  Only one rank accessible at a time
SIMM vs DIMM
  DIMM has separate contacts on each side of the board to provides twice as much data rate.

## Slide 18: A 64-bit Wide DIMM (One Rank)
Advantages:
  Acts like a high-capacity DRAM chip with a wide interface
  Flexibility: memory controller does not need to deal with individual chips
Disadvantages:
  Granularity: Accesses cannot be smaller than the interface width

## Slide 19: DRAM Subsystem Organization
  Dram: Dynamic RAM
DRAM Organization:
Channel
DIMM
Rank
Chip
Bank
Row/Column
Channel: Independent memory subsystem
  E.g., 2 independent Channels:

## Slide 20: The DRAM subsystem
Memory channel
Memory channel
DIMM (Dual in-line memory module)
Processor
“Channel”
Each channel is connected to its own on-die memory controller

## Slide 21
Row Buffer
(Row 0, Column 0)
Row decoder
Column mux
Row address 0
Column address 0
Data
Row 0
Empty
(Row 0, Column 1)
Column address 1
(Row 1, Column 0)
HIT
Row address 1
Row 1
Column address 0
CONFLICT !
Columns
Rows
Access Address: Row Operation:
R0
R0
R1
Activation
Restore, Precharge, Activation
No operation
RBL=2
RBL=1
Credit: Onur Mutlu.
Row Operations & Row Buffer Locality
Improving Row Buffer Locality (RBL) is the key to improve DRAM efficiency

## Slide 22
……
Activation Counter:
R1: Activation = 1
R5: Activation = 2
R1: Activation = 3
R5: Activation = 4
R5: Activation = 4
Avg RBL = 5 / 4 = 1.25
……
requests currently
in the pending queue
oldest
request
R1
R5
R1
R5
future
requests
R2
R4
R3
In-order scheduling
(FIFO):
Request Stream
R5
……
Activation Counter:
R1: Activation = 1
R1: Activation = 1
R5: Activation = 2
R5: Activation = 2
R5: Activation = 2
Avg RBL = 5 / 2 = 2.5
……
requests currently
in the pending queue
oldest
request
R1
R5
R1
R5
future
requests
R2
R4
R3
Out-of-order scheduling
(FR-FCFS):
Request Stream
R5
Visible to the memory scheduler
Same
activation
Same
activation
Same
activation
RBL & Memory Scheduling Schemes

## Slide 23: DRAM Milestones
In the time that the memory to processor bandwidth has more than doubled the memory latency has improved by a factor of only 1.2 to 1.4
 | DRAM | Page DRAM | Page DRAM | Page DRAM | SDRAM | DDR SDRAM
Module Width | 16b | 16b | 32b | 64b | 64b | 64b
Year | 1980 | 1983 | 1986 | 1993 | 1997 | 2000
Mb/chip | 0.06 | 0.25 | 1 | 16 | 64 | 256
Die size (mm2) | 35 | 45 | 70 | 130 | 170 | 204
Pins/chip | 16 | 16 | 18 | 20 | 54 | 66
BWidth (MB/s) | 13 | 40 | 160 | 267 | 640 | 1600
Latency (nsec) | 225 | 170 | 125 | 75 | 62 | 52
Patterson, CACM Vol 47, #10, 2004

## Slide 24: Review: DRAM vs. SRAM
DRAM
  Slower access (capacitor)
  Higher density (1T 1C cell)
  Lower cost
  Requires refresh (power, performance, circuitry)
  Manufacturing requires putting capacitor and logic together
SRAM
  Faster access (no capacitor)
  Lower density (6T cell)
  Higher cost
  No need for refresh
  Manufacturing compatible with logic process (no capacitor)

## Slide 25: Conclusion Time
What are the levels in the DRAM organization?
Channel, DIMM, Rank, Chip, Bank, Row, Column
What is the idea behind having multiple memory banks?
What is row buffer?
Hiding latency
Cache for DRAM rows