## Slide 1: Lecture 4. Memory Hierarchy (6)
Haonan Wang
CMPE 200 Computer Architecture & Design

## Slide 2
Row Buffer
(Row 0, Column 0)
Row decoder
Column mux
Row address 0
Column address 0
Data
Row 0
Empty
(Row 0, Column 1)
Column address 1
(Row 1, Column 0)
HIT
Row address 1
Row 1
Column address 0
CONFLICT !
Columns
Rows
Access Address: Row Operation:
R0
R0
R1
Activation
Restore, Precharge, Activation
No operation
RBL=2
RBL=1
Credit: Onur Mutlu.
Row Operations & Row Buffer Locality
Improving Row Buffer Locality (RBL) is the key to improve DRAM efficiency

## Slide 3
……
Activation Counter:
R1: Activation = 1
R5: Activation = 2
R1: Activation = 3
R5: Activation = 4
R5: Activation = 4
Avg RBL = 5 / 4 = 1.25
……
requests currently
in the pending queue
oldest
request
R1
R5
R1
R5
future
requests
R2
R4
R3
In-order scheduling
(FIFO):
Request Stream
R5
……
Activation Counter:
R1: Activation = 1
R1: Activation = 1
R5: Activation = 2
R5: Activation = 2
R5: Activation = 2
Avg RBL = 5 / 2 = 2.5
……
requests currently
in the pending queue
oldest
request
R1
R5
R1
R5
future
requests
R2
R4
R3
Out-of-order scheduling
(FR-FCFS):
Request Stream
R5
Visible to the memory scheduler
Same
activation
Same
activation
Same
activation
RBL & Memory Scheduling Schemes

## Slide 4: DRAM Milestones
In the time that the memory to processor bandwidth has more than doubled the memory latency has improved by a factor of only 1.2 to 1.4
 | DRAM | Page DRAM | Page DRAM | Page DRAM | SDRAM | DDR SDRAM
Module Width | 16b | 16b | 32b | 64b | 64b | 64b
Year | 1980 | 1983 | 1986 | 1993 | 1997 | 2000
Mb/chip | 0.06 | 0.25 | 1 | 16 | 64 | 256
Die size (mm2) | 35 | 45 | 70 | 130 | 170 | 204
Pins/chip | 16 | 16 | 18 | 20 | 54 | 66
BWidth (MB/s) | 13 | 40 | 160 | 267 | 640 | 1600
Latency (nsec) | 225 | 170 | 125 | 75 | 62 | 52
Patterson, CACM Vol 47, #10, 2004

## Slide 5: Review: DRAM vs. SRAM
DRAM
  Slower access (capacitor)
  Higher density (1T 1C cell)
  Lower cost
  Requires refresh (power, performance, circuitry)
  Manufacturing requires putting capacitor and logic together
SRAM
  Faster access (no capacitor)
  Lower density (6T cell)
  Higher cost
  No need for refresh
  Manufacturing compatible with logic process (no capacitor)

## Slide 6
Purpose: Long term, nonvolatile storage
  Lowest level in the memory hierarchy: large, cheap, slow
General structure
  1 to 4 rotating platter coated with a magnetic surface (2 sides recordable)
    Rotational speeds of 5,400 to 15,000 RPM
  Moveable read/write head to access the information for each platter
  10,000 to 50,000 tracks per surface
    Cylinder - all the tracks under the head at a given point on all surfaces
  100 to 500 sectors per track
    The smallest unit that can be read/written (typically 512B)
    Outer tracks can hold more sectors than the inner tracks
Magnetic Disk
Sector
Track
Cylinder
Head
Platter
Controller
+
Cache

## Slide 7
  Rotational latency: wait for the desired sector to rotate under the head
    ½ of 1/RPM converted to ms: 0.5R/5400RPM = 5.6ms to 0.5R/15000RPM = 2.0ms
  Transfer time: transfer a block of bits (one or more sectors) under the head to the disk controller’s cache (70 to 125 MB/s are typical disk transfer rates)
    the disk controller’s “cache” takes advantage of spatial locality in disk accesses
    cache transfer rates are much faster (e.g., 375 MB/s)
  Controller time: the overhead the disk controller imposes in performing a disk I/O access (typically < 0.2 ms)
Sector
Track
Cylinder
Head
Platter
Controller
+
Cache
Magnetic Disk Characteristic
  Seek time: position the head over the proper track
    3 to 12/15 ms on average
    Due to locality of disk references, the actual average seek time may be only 25% to 33% of the advertised number

## Slide 8: Typical Disk Access Time
  If the measured average seek time is 25% of the advertised average seek time, then
Avg disk read/write
= 4.0 ms + 0.5/(15,000RPM/(60sec/min)) + 0.5KB/(100MB/sec) + 0.2 ms
= 4.0 + 2.0 + 0.005 + 0.2 = 6.2 ms
Avg disk read/write = 1.0 + 2.0 + 0.005 + 0.2 = 3.2 ms
The average time to read or write a 512B sector for a disk rotating at 15,000 RPM with average seek time of 4 ms, a 100MB/sec transfer rate, and a 0.2 ms controller overhead

## Slide 9: Disk Latency & Bandwidth Improvement
Disk latency = average seek time + rotational latency.
Disk bandwidth is the peak transfer speed of formatted data from the media (not from the cache).
Patterson, CACM Vol 47, #10, 2004
Chart: Year of Introduction
| 1983 | 1990 | 1994 | 1998 | 2003
Bandwidth (MB/s) | 0.6 | 4 | 9 | 24 | 86
Latency (msec) | 48.3 | 17.1 | 12.7 | 8.8 | 5.7

## Slide 10: Flash Storage
Flash memory is semiconductor memory that is nonvolatile like disks but has latency 100 to 1000 times lower and is smaller, more power efficient, and more shock resistant.
  Flash memory bits wear out. But with wear leveling it is unlikely that the write limits of the flash will be exceeded.
  Example:
Storage | Write throughput | Read throughput | Latency
SSD | 2,500 MB/S | 3,500 MB/S | 0.025 ms
DISK | 250 MB/S | 250 MB/S | 5 ms

## Slide 11
Flash memory is organized into blocks of pages
  page size 512B to 4KB, block size 32 to 128 pages (typical)
  “read” is page read
  “write” is block erase (~ 1 ms) followed by page write (and additional copying of other pages in that block)
Comes in two flavors: NOR Flash and NAND Flash
  NOR Flash is randomly addressable (Minimum access size 512 bytes)
  NAND Flash is less expensive (greater storage density) and is not randomly addressable (minimum access size 2048 bytes); so more popular
Flash Storage Characteristics

## Slide 12: Dependability, Reliability, Availability
Reliability – measured by the mean time to failure (MTTF). Service interruption is measured by mean time to repair (MTTR)
Availability – a measure of service accomplishment
  Availability = MTTF / (MTTF + MTTR)
To increase MTTF, either improve the quality of components or design the system to continue operating in the presence of faulty components
  Fault avoidance: preventing fault occurrence by construction
  Fault tolerance: using redundancy to correct or bypass faulty components (hardware)

## Slide 13
Arrays of independent physical disks working together as one logical disk
  Increase potential throughput by having many disk drives
    Data can be spread across multiple disk
    Multiple disk accesses can be made simultaneously for higher throughput
Reliability for the array is lower than for a single disk
Availability can be improved by adding redundant disks
  Lost information can be reconstructed from redundant information
  MTTR: mean time to repair is in the order of hours
  MTTF: mean time to failure of disks is tens of years
RAID: Redundant Array of Independent Disks
RAID Disk Array

## Slide 14
sec1
sec3
sec2
sec4
sec1,b0
sec1,b2
sec1,b1
sec1,b3
Assumes one stripe = four blocks
RAID: Level 0 (Striping, No Redundancy)
Multiple smaller disks as opposed to one big disk
  Multiple blocks can be accessed in parallel to increase the performance
  Works well for large data requests
E.g., a 4-disk system gives four times the throughput (R/W) of a 1-disk system
  Same cost as one big disk – assuming 4 small disks cost the same as one big disk
What if one disk fails?
  No redundancy, data is lost
  More likely to fail as the number of disks increases

## Slide 15
# redundant disks = # of data disks, so always two copies of the data
  Twice the cost of one big disk
  Writes are made to both sets of disks and have no speed improvement
  Reads can be 2 times faster
If a disk fails, the system just goes to the “mirror” for the data
redundant (check) data
sec1
sec3
sec2
sec4
sec1m
sec3m
sec2m
sec4m
RAID: Level 1 (Redundancy via Mirroring)

## Slide 16
Category | Level | Disks | Features
Striping | 0 | N | No fault tolerance
Mirroring, no striping | 1 | 2N | Expensive
Striping Rarely used | 2 3 | N + m N + 1 | Hamming code Parity disk
Block level Striping Parity | 4 5 6 | N + 1 N + 1 N + 2 | Parity disk Distributed parity Dual distributed parity
RAID: Design Choices
Parity: used for error detection
  E.g., data: 00001111, parity bit: 0
Hamming code: limited error correction
  Using multiple parity bits to locate 1 error bit