## Slide 1: Lecture 4. Memory Hierarchy (7)
Haonan Wang
CMPE 200 Computer Architecture & Design

## Slide 2
registers  memory
  by compiler (or programmer)
registers  cache  main memory
  by the cache & memory controller hardware
main memory  external storage (flash, disk)
  Static: by the programmer with OS support (files)
  Dynamic: by the operating system (virtual memory)
    virtual address to physical address mapping
    assisted by the hardware (TLB, page tables)
How is the Hierarchy Managed?

## Slide 3
Virtual Address (VA)
Page offset
Virtual page number
31 30 . . . 12 11 . . . 0
Page offset
Physical page number
Physical Address (PA)
29 . . . 12 11 0
Translation
A virtual address must first be translated to a physical address to access memory
  Basic unit: page (e.g., 1KB to 64KB)
Virtual memory size can be larger than physical memory size
  Pages can be stored in the secondary storage
Virtual Memory

## Slide 4: Address Space Isolation
Program 1 page table
Main (physical) memory
Program 2 page table
Allows efficient and safe sharing of main memory among multiple processes
  The starting location of each page is contained in the program’s page table
  Create the illusion that each program has a large consecutive memory space
  Improving memory utilization: code can be loaded anywhere the OS can find space
Virtual address space

## Slide 5: Address Translation Mechanisms
Physical page
base addr
Main memory
Disk storage
Virtual page #
V
1
1
1
1
1
1
0
1
0
1
0
Page Table (in main memory)
Offset
Physical page #
Offset
Page table register
virtual address
physical address
Page walk: Search (walk) the page table
Page fault: a DRAM miss for the page
 Page in disk

## Slide 6: Virtual Addressing with a Cache
It takes an extra memory access to translate a VA to a PA
CPU
Trans-
lation
Cache
Main
Memory
VA
PA
miss
hit
data
This makes memory (cache) accesses very expensive
The hardware solution is to use a Translation Lookaside Buffer (TLB)
  A small cache that keeps track of recently used address mappings to avoid having to do a page table lookup in main memory

## Slide 7: Making Address Translation Fast
Physical page
base address
Main memory
Disk storage
Virtual page #
V
1
1
1
1
1
1
0
1
0
1
0
1
1
1
0
1
Tag
Physical page
base address
V
TLB
Page Table (in physical memory)
Page table register

## Slide 8: A TLB in the Memory Hierarchy
A TLB miss – is it a page fault or merely a TLB miss?
  If the page is loaded into main memory, then the TLB miss can be handled by loading the translation information from the page table into the TLB (10’s of cycles )
  If the page is not in main memory, then it’s a true page fault (1,000,000’s)
TLB misses are much more frequent than true page faults
CPU
TLB
Lookup
Cache
Main
Memory
VA
PA
miss
hit
data
Trans-
lation
hit
miss
¾ t
¼ t
  What about virtually addressed caches?

## Slide 9: TLB Event Combinations
TLB | Page Table | Cache | Possible? Under what circumstances?
Hit | Hit | Hit | 
Hit | Hit | Miss | 
Miss | Hit | Hit | 
Miss | Hit | Miss | 
Miss | Miss | Miss | 
Hit | Miss | Miss/ Hit | 
Miss | Miss | Hit | 
Yes – this is what we want!
Yes – although the page table is not
checked after the TLB hits
Yes – TLB missed, but PA is in page table and data is in cache
Yes – TLB missed, but PA is in page table, data not in cache
Yes – page fault
No – TLB translation is not possible if the page is not present in main memory
No – data is not allowed in the cache if the
page is not in memory

## Slide 10: Measuring Performance with Caches
Assuming cache hit costs are included as part of the normal CPU execution cycle, then
  CPU time = IC × CPI × CP
  = IC × (CPIideal + Memory-stall cycles) × CP
CPIstall
Memory-stall cycles come from cache misses (a sum of read-stalls and write-stalls)
  Read-stall cycles = read miss ratio × read miss penalty
  Write-stall cycles = write miss ratio × write miss penalty + write buffer stalls
For write-through caches, we can simplify this to
  Memory-stall cycles = miss ratio × miss penalty
Note: this is miss ratio with regard to all instructions (not only LW)
= read ratio * cache miss rate

## Slide 11: Impacts of Cache Performance
Relative cache penalty increases as processor performance improves (faster clock rate and/or lower CPI)
  The memory speed is unlikely to improve as fast as processor cycle time. When calculating CPIstall, the cache miss penalty is measured in processor clock cycles needed to handle a miss
  The lower the CPIideal, the higher the impact of stalls
Example: A processor with a CPIideal of 2, a 100 cycle miss penalty, 36% load/store instructions, and 2% I$ and 4% D$ miss rates
  Memory-stall cycles = 2% × 100 + 36% × 4% × 100 = 3.44
  CPIstalls = 2 + 3.44 = 5.44
What if the CPIideal is reduced to 1? Or the processor clock rate is doubled (doubling the miss penalty)?

## Slide 12: Memory (DRAM) + Caches
It is important to match the cache characteristics
  Caches want information provided to them one block at a time (and a block is usually more than one word)
Memory design considerations:
  With the main memory characteristics
    Use DRAMs that support fast multiple word accesses, preferably ones that match the block size of the cache
  With the memory-bus characteristics
    Make sure the memory-bus can support the DRAM access rates and patterns
    With the goal of increasing the Memory-Bus-to-Cache bandwidth

## Slide 13: Memory Systems that Support Caches
The off-chip interconnect and memory architecture can affect overall system performance in dramatic ways
CPU
Cache
DRAM
Memory
bus
One word wide organization
(one word wide bus & memory)
32-bit data
&
32-bit addr
per cycle
on-chip
Assume:
1 memory bus clock cycle to send the address
15 memory bus clock cycles to get the 1st word in the block from DRAM (row cycle time), 5 memory bus clock cycles for 2nd, 3rd, 4th words (column access time)
1 memory bus clock cycle to return a word of data
Memory-Bus to Cache bandwidth
number of bytes accessed from memory and transferred to cache/CPU per memory bus clock cycle

## Slide 14
If the block size is one word, then for a cache miss, the pipeline will have to stall for:
  memory bus clock cycle to send address
  memory bus clock cycles to read DRAM
  memory bus clock cycle to return data
  total clock cycles miss penalty
Number of bytes transferred per clock cycle (bandwidth) for a single miss is
  bytes per memory bus clock cycle
  1
  15
  1
  17
  4 / 17 = 0.235
One Word Wide Bus, One Word Blocks
CPU
Cache
DRAM
Memory
bus
One word wide organization
(one word wide bus & memory)
32-bit data
&
32-bit addr
per cycle
on-chip

## Slide 15
What if the block size is four words and each word is in a different DRAM row?
  cycle to send 1st address
  cycles to read DRAM
  cycles to return last data word
  total clock cycles miss penalty
Number of bytes transferred per clock cycle (bandwidth) for a single miss is
  bytes per memory bus clock cycle
1
  4 x 15 = 60
  1
  62
  (4 x 4) / 62 = 0.258
One Word Wide Bus, Four Word Blocks
CPU
Cache
DRAM
Memory
bus
One word wide organization
(one word wide bus & memory)
32-bit data
&
32-bit addr
per cycle
on-chip

## Slide 16
What if the block size is four words and all words are in the same DRAM row?
  cycle to send 1st address
  cycles to read DRAM
  cycles to return last data word
  total clock cycles miss penalty
Number of bytes transferred per clock cycle (bandwidth) for a single miss is
  bytes per memory bus clock cycle
1
15 + 3 x 5 = 30
1
  32
  (4 x 4) / 32 = 0.5
CPU
Cache
DRAM
Memory
bus
One word wide organization
(one word wide bus & memory)
32-bit data
&
32-bit addr
per cycle
on-chip
One Word Wide Bus, Four Word Blocks

## Slide 17
For a block size of four words
  cycle to send 1st address
  cycles to read DRAM banks
  cycles to return last data word
  total clock cycles miss penalty
CPU
Cache
bus
on-chip
Number of bytes transferred per clock cycle (bandwidth) for a single miss is
  bytes per memory bus clock cycle
  (4 x 4) / 20 = 0.8
1
15
  4 x 1 = 4
  20
DRAM
Memory
bank 1
DRAM
Memory
bank 0
DRAM
Memory
bank 2
DRAM
Memory
bank 3
Interleaved Memory, One Word Wide Bus
  What about interleaving channels?

## Slide 18: Conclusion Time
What is TLB?
Cache for page table
What are the three cases (in terms of delay) for address translation?
TLB hit, page table hit, page fault