## Slide 1: Lecture 4. Memory Hierarchy
Haonan Wang
CMPE 200 Computer Architecture & Design

## Slide 2: Computer Architecture Overview
Software/Applications
Processor
Operating System
Instruction Set
Architecture
Firmware
Compiler
Registers
Cache
Memory
HDD/SSD
Memory Hierarchy

## Slide 3: Memory Hierarchy
#include <stdio.h>
#include <string.h>
int numbers[2];
void myfunction(void)
{
FILE *fp;
int size = 2;
int sum = 0;
/* Open file for reading */
fp = fopen(“mynumbers.txt", “r");
/* Read and display data */
fread(numbers, sizeof(int), size, fp);
fclose(fp);
sum = numbers[0] + numbers[1];
printf(“Sum = %d\n”, sum);
}
int main (void) {
myfunction();
return(0);
}
Example: a C program that reads
two integer values from “file.txt” file
and prints the sum of them.
Processor
(CPU)
Understands and executes each line of the code.
Uses fast on-chip memories
Memory
(DRAM)
Provides operands to CPU
(*fp, size, sum, numbers[2])
Storage
(HDD)
Provides file inputs and program code
(file.txt)

## Slide 4: Memory Hierarchy
On-chip Memories (Memories inside of CPU)
  Register file, Caches
  Small but Fast
CPU
Register File
Instruction
Cache
Data
Cache

## Slide 5: Memory Hierarchy
Off-chip Memories (Memories outside CPU)
  System Memory, Storage
  Large but Slow
System Memory
Storage
CPU

## Slide 6: Memory Hierarchy
Processor
Registers
Cache
Memory
HDD/SSD
Fast
Slow
Cheap
Expensive
Access
Speed
Price/unit
0.5ns ~ 2.5ns
$2000 ~ $5000 per GB
50ns ~ 200ns
$20 ~ $75 per GB
5ms ~ 20ms
$0.2 ~ $2 per GB
On-chip:
Subset of memory
Volatile Memory
Non-volatile Memory
(NVM)
Off-chip:
full memory
Software managed
1 register = 1 word
Hardware managed
1 block = multiple words

## Slide 7: Memories in Your PC
Windows
  This PC  Properties
  cmd window  wmic
  3rd party tool like CPU-Z
Linux
  lscpu
  cat /proc/cpuinfo
  etc.
System Memory
Storage
Caches

## Slide 8: Why?
Two Types of Locality:
  Temporal Locality (Locality in Time): If an address is referenced, it tends to be referenced again (e.g., loops, variable reuse)
  Spatial Locality (Locality in Space): If an address is referenced, neighboring addresses tend to be referenced (e.g., array, stack, etc.)
On-chip
Off-chip

## Slide 9: The “Memory Wall”
“Moore’s Law”
CPU ~55%/year
(2X/1.5yr)
DRAM
7%/year
(2X/10yrs)
Processor-Memory
Performance Gap (grows 50%/year)

## Slide 10: The Memory Hierarchy Goal
How do we create a memory system that gives the illusion of being large, cheap and fast (most of the time)?
  With hierarchy
    try the fast parts first -- most of the time, this works well
    if not, move the data so it works well the next time
  With parallelism
    use multiple identical parts operating simultaneously
    for large quantities of data, this works well
Example – keep a subset of the data in fast memory
Example – 1-byte-wide memory  4 × 1-byte-wide memory  4-byte-wide memory
  load word takes 4 memory cycles vs. 1 memory cycle

## Slide 11: Cache Design
Caches use SRAM for speed and technology compatibility
  Low density (6 transistor cells), high power, expensive, fast
  Static: content will last “forever” (until power turned off)
Example: A (2M X 16 bit) SRAM logic
Dout[15-0]
SRAM
2M x 16
Din[15-0]
Address
Chip select
Output enable
Write enable
16
16
21

## Slide 12: SRAM Cache Design
r
o
w
d
e
c
o
d
e
r
row
address
4-bit data word
SRAM Cell
Array
word (row)
select line
bit (data) lines
Each intersection represents a
6-T SRAM cell
Column Selector &
I/O Circuits
column
address
Each row holds a data block
Column address selects the requested word from block

## Slide 13: Cache Hit and Miss
Hit: Data appears in some block of the cache
  Hit Rate: # hits / total accesses on the cache
  Hit Time: Time to access the cache
Miss: Data needs to be retrieved from the lower level (and stored in cache)
  Miss Rate: 1 - (Hit Rate)
  Miss Penalty: Average delay in the processor caused by each miss
Lower Level Memory
(cache/main memory)
Cache
To Processor
From Processor
data block X
data block Y
Can’t find!
Miss
Hit
Hit
read
read

## Slide 14: Principle of Locality
Temporal Locality: If an address is referenced, it tends to be referenced again
Spatial Locality: If an address is referenced, neighboring addresses tend to be referenced
How to create a memory system that gives the illusion of being large, cheap and fast?
  With hierarchy
  With parallelism
On-chip
Off-chip

## Slide 15: SRAM Cache Design
r
o
w
d
e
c
o
d
e
r
row
address
4-bit data word
SRAM Cell
Array
word (row)
select line
bit (data) lines
Each intersection represents a
6-T SRAM cell
Column Selector &
I/O Circuits
column
address
Each row holds a data block
Column address selects the requested word from block

## Slide 16: Cache Hit and Miss
Hit: Data appears in some block of the cache
  Hit Rate: # hits / total accesses on the cache
  Hit Time: Time to access the cache
Miss: Data needs to be retrieved from the lower level (and stored in cache)
  Miss Rate: 1 - (Hit Rate)
  Miss Penalty: Average delay in the processor caused by each miss
Lower Level Memory
(cache/main memory)
Cache
To Processor
From Processor
data block X
data block Y
Can’t find!
Miss
Hit
Hit
read
read

## Slide 17: Memory Hierarchy Performance
Average Memory Access Time (AMAT)
= Hit Time + Miss rate x Miss Penalty
Example:
  Cache Hit = 1 cycle
  Miss rate = 10% = 0.1
  Miss penalty = 300 cycles
  AMAT = Thit(L1) + Miss_rate(L1) x T(Memory) = 1 + 0.1 x 300 = 31 cycles
Main
Memory
(DRAM)
First-level
Cache
Hit Time
Miss penalty
1 cycle
300 cycles
Due to long-latency memory, AMAT is 30 cycles longer than cache latency.
Can we reduce the overhead?

## Slide 18: Reducing Penalty: Multi-Level Cache
Main
Memory
(DRAM)
Second
Level
Cache
Third
Level
Cache
300 cycles
20 cycles
10 cycles
On Processor Die
L1
L2
L3
First-level
Cache
Hit Time
1 cycle
Off-Chip

## Slide 19: Reducing Penalty: Multi-Level Cache
AMAT in multi-level cache organization
  = Thit(L1) + Miss_rate(L1) x Miss_penalty(L1)
Main
Memory
(DRAM)
Second
Level
Cache
Third
Level
Cache
300 cycles
20 cycles
10 cycles
On Processor Die
L1
L2
L3
First-level
Cache
Hit Time
1 cycle
Off-Chip

## Slide 20: Reducing Penalty: Multi-Level Cache
AMAT in multi-level cache organization
  = Thit(L1) + Miss_rate(L1) x
  [ Thit(L2) + Miss_rate(L2) x Miss_penalty(L2) ]
Main
Memory
(DRAM)
Second
Level
Cache
Third
Level
Cache
300 cycles
20 cycles
10 cycles
On Processor Die
L1
L2
L3
First-level
Cache
Hit Time
1 cycle
Off-Chip

## Slide 21: Reducing Penalty: Multi-Level Cache
AMAT in multi-level cache organization
  = Thit(L1) + Miss_rate(L1) x
  [ Thit(L2) + Miss_rate(L2) x
  { Thit(L3) + Miss_rate(L3) x Miss_penalty(L3) } ]
Main
Memory
(DRAM)
Second
Level
Cache
Third
Level
Cache
300 cycles
20 cycles
10 cycles
On Processor Die
L1
L2
L3
First-level
Cache
Hit Time
1 cycle
Off-Chip

## Slide 22: Reducing Penalty: Multi-Level Cache
AMAT in multi-level cache organization
  = Thit(L1) + Miss_rate(L1) x
  [ Thit(L2) + Miss_rate(L2) x
  { Thit(L3) + Miss_rate(L3) x T(memory) } ]
Main
Memory
(DRAM)
Second
Level
Cache
Third
Level
Cache
300 cycles
20 cycles
10 cycles
On Processor Die
L1
L2
L3
First-level
Cache
Hit Time
1 cycle
Off-Chip

## Slide 23: Reducing Penalty: Multi-Level Cache
AMAT in multi-level cache organization
  = Thit(L1) + Miss_rate(L1) x
  [ Thit(L2) + Miss_rate(L2) x
  { Thit(L3) + Miss_rate(L3) x T(memory) } ]
Example:
  Miss rate of L1, L2, L3 = 10%, 5%, 1%, respectively
  AMAT = 1 + 0.1 x [ 10 + 0.05 x { 20 + 0.01 x 300 } ] = 2.115 cycles
Second
Level
Cache
Third
Level
Cache
300 cycles
20 cycles
10 cycles
On Processor Die
L1
L2
L3
First-level
Cache
Hit Time
1 cycle
Vs. 31 cycles
14.7x speedup!
Main
Memory
(DRAM)
Off-Chip
Are more levels always good?

## Slide 24: What to Keep in Caches?
It depends on the cache organization and replacing policy
Cache organization:
  Cache line (block): The basic unit of data replacement. A longer cache line fetches and replaces more data per miss.
  Set: An entry that one cache line is mapped to according to certain bits of its address.
  Way: A slot within a cache set to hold one history cache line.
Cache line replacing policy: which history line should be replaced?
  In a set entry, each cache line can be identified with a Tag (a portion of its address).
  Least recently used (LRU), First-in first-out (FIFO), Random, etc.

## Slide 25: Cache Indexing
Block offset
Byte offset
Index
Tag
Selects the set
Used for tag compare
Selects the word in the block
Way 0
Way 1
Set 0
Set 1
Example: a simple 2-set x 2-way cache
block 0
block 1
block 2
block 3
Address decoding:

## Slide 26: Cache Types
N-way Set-Associative: Number of ways > 1 & Number of sets > 1
  Slightly complex searching mechanism
Direct Mapped: Number of ways = 1
  Fast indexing mechanism
Fully-Associative: Number of sets = 1
  Extensive hardware resources required to search
Block offset
Byte offset
Index
Tag
Decreasing associativity
Fully associative (only one set)
Direct mapped (only one way)
Increasing associativity
Selects the set
Used for tag compare
Selects the word in the block
Assuming fixed sized cache:
Way 0
Way 1
Set 0
Set 1
block 0
block 1
block 2
block 3
…
…

## Slide 27: MIPS Direct Mapped Cache Example
20
Tag
10
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
1021
1022
1023
31 30 . . . 13 12 11 . . . 2 1 0
Byte offset
20
Data
32
Hit
  32bit address from the PC (Instr Fetch) or ALU (load, store addr)

## Slide 28: Multiword Block Direct Mapped Cache
8
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
253
254
255
31 30 . . . 13 12 11 . . . 4 3 2 1 0
Byte offset
20
20
Tag
Hit
Data
32
Block offset

## Slide 29: Four-Way Set Associative Cache
31 30 . . . 11 10 9 . . . 2 1 0
Byte offset
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Index
Data
Tag
V
0
1
2
.
.
.
253
254
255
8
Index
22
Tag
Hit
Data
32
4x1 select

## Slide 30: Costs of Set Associative Caches
Must have hardware to keep track of when each way’s block was used relative to the other blocks in the set (for replacement policy)
  E.g., for 2-way set associative, takes one bit per set → set the bit when a block is referenced (and reset the other way’s bit)
N-way set associative cache costs
  N comparators (delay and area)
  MUX delay (set selection) before data is available
  Data is available after set selection (and Hit/Miss decision). In a direct mapped cache, the cache block is available before the Hit/Miss decision
    So its not possible to just assume a hit and continue and recover later if it was a miss
Total cache line size = valid field size + tag size + block data size + data for cache policy (e.g., time stamp, modified bit, etc.)

## Slide 31: Cache Miss Classification: The 3 C’s
Compulsory (cold) Misses
  On the 1st reference to a block
  Related to # blocks accessed by a code, not related to the configuration of a cache
Capacity Misses
  The program’s working set size exceeds the cache capacity
Conflict Misses
  Multiple memory blocks map to the same set in set-associative caches

## Slide 32: More Detailed Mapping Example
1st step: Find data block no. that the word belongs to
0x77FF1C68 = 0111 0111 1111 1111 0001 1100 0110 1000
We have a cache that has following configuration
  Consists of 8 cache blocks (lines)
  A data word is 4-byte
  A block is 32-byte (8 words per block)
  Direct mapped
We load a word from 0x77FF1C68
Offset within a data word
Each data word’s offset
within a block
(2nd word in a block)
Block no.
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
cache blocks

## Slide 33: More Detailed Mapping Example
2nd step: Map the block no. to cache block no.
0x77FF1C68 = 0111 0111 1111 1111 0001 1100 0110 1000
We have a cache that has following configuration
  Consists of 8 cache blocks (lines)
  A data word is 4-byte
  A block is 32-byte (8 words per block)
  Direct mapped
We load a word from 0x77FF1C68
Offset within a data word
Each data word’s offset
within a block
(2nd word in a block)
Block no.
% 8 blocks
= cache block no. 3
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
cache blocks

## Slide 34: More Detailed Mapping Example
1st step: Calculate how many sets exist
8 blocks / 4 entries per set = 2 sets
We have a cache that has following configuration
  Consists of 8 cache blocks (lines)
  A data word is 4-byte
  A block is 32-byte (8 words per block)
  4-way Set-Associative
We load a word from 0x77FF1C68
0 |  |  |  | 1 |  |  | 
cache blocks
set no.
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
cache blocks

## Slide 35: More Detailed Mapping Example
2nd step: Find data block no. that the word belongs to
0x77FF1C68 = 0111 0111 1111 1111 0001 1100 0110 1000
We have a cache that has following configuration
  Consists of 8 cache blocks (lines)
  A data word is 4-byte
  A block is 32-byte (8 words per block)
  4-way Set-Associative
We load a word from 0x77FF1C68
Offset within a data word
Each data word’s offset
within a block
(2nd word in a block)
Block no.
0 |  |  |  | 1 |  |  | 
cache blocks
set no.

## Slide 36: More Detailed Mapping Example
3rd step: Map the block no. to cache block no.
0x77FF1C68 = 0111 0111 1111 1111 0001 1100 0110 1000
We have a cache that has following configuration
  Consists of 8 cache blocks (lines)
  A data word is 4-byte
  A block is 32-byte (8 words per block)
  4-way Set-Associative
We load a word from 0x77FF1C68
Offset within a data word
Each data word’s offset
within a block
(2nd word in a block)
Block no.
% 2 sets
= cache block no. 1
0 |  |  |  | 1 |  |  | 
cache blocks
set no.
pick any available block within set 1

## Slide 37: More Detailed Mapping Example
1st and all step: Find any available cache block and map
We have a cache that has following configuration
  Consists of 8 cache blocks (lines)
  A data word is 4-byte
  A block is 32-byte (8 words per block)
  Fully-Associative
We load a word from 0x77FF1C68
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
cache blocks
pick any available block

## Slide 38: Cache Replacement Policy
When loading a new block (on miss), if the cache is already full, which block should be replaced (in the set)?
  Random: Replace a randomly chosen line
  FIFO: Replace the oldest line
  LRU (Least Recently Used): Replace the least recently used line
  Many others: Round Robin, LIFO, MRU, etc..

## Slide 39: LRU Example
Cache configuration:
  Size: 4 blocks
  Mapping: fully-associative
  Replacement: LRU
Mem access sequence: (each character indicates a block address)
  ABCDCDECG
Accesses |  | A | B | C | D | C | D | E | C | G
priority order (LRU) | 0 (MRU) | A |  |  |  |  |  |  |  | 
 | 1 |  |  |  |  |  |  |  |  | 
 | 2 |  |  |  |  |  |  |  |  | 
 | 3 (LRU) |  |  |  |  |  |  |  |  | 
cache miss |  | m |  |  |  |  |  |  |  | 

## Slide 40: LRU Example
Accesses |  | A | B | C | D | C | D | E | C | G
priority order (LRU) | 0 (MRU) | A | B |  |  |  |  |  |  | 
 | 1 |  | A |  |  |  |  |  |  | 
 | 2 |  |  |  |  |  |  |  |  | 
 | 3 (LRU) |  |  |  |  |  |  |  |  | 
cache miss |  | m | m |  |  |  |  |  |  | 
Cache configuration:
  Size: 4 blocks
  Mapping: fully-associative
  Replacement: LRU
Mem access sequence: (each character indicates a block address)
  ABCDCDECG

## Slide 41: LRU Example
Accesses |  | A | B | C | D | C | D | E | C | G
priority order (LRU) | 0 (MRU) | A | B | C |  |  |  |  |  | 
 | 1 |  | A | B |  |  |  |  |  | 
 | 2 |  |  | A |  |  |  |  |  | 
 | 3 (LRU) |  |  |  |  |  |  |  |  | 
cache miss |  | m | m | m |  |  |  |  |  | 
Cache configuration:
  Size: 4 blocks
  Mapping: fully-associative
  Replacement: LRU
Mem access sequence: (each character indicates a block address)
  ABCDCDECG

## Slide 42: LRU Example
Accesses |  | A | B | C | D | C | D | E | C | G
priority order (LRU) | 0 (MRU) | A | B | C | D |  |  |  |  | 
 | 1 |  | A | B | C |  |  |  |  | 
 | 2 |  |  | A | B |  |  |  |  | 
 | 3 (LRU) |  |  |  | A |  |  |  |  | 
cache miss |  | m | m | m | m |  |  |  |  | 
Cache configuration:
  Size: 4 blocks
  Mapping: fully-associative
  Replacement: LRU
Mem access sequence: (each character indicates a block address)
  ABCDCDECG

## Slide 43: LRU Example
Accesses |  | A | B | C | D | C | D | E | C | G
priority order (LRU) | 0 (MRU) | A | B | C | D | C |  |  |  | 
 | 1 |  | A | B | C | D |  |  |  | 
 | 2 |  |  | A | B | B |  |  |  | 
 | 3 (LRU) |  |  |  | A | A |  |  |  | 
cache miss |  | m | m | m | m | h |  |  |  | 
Cache configuration:
  Size: 4 blocks
  Mapping: fully-associative
  Replacement: LRU
Mem access sequence: (each character indicates a block address)
  ABCDCDECG

## Slide 44: LRU Example
Accesses |  | A | B | C | D | C | D | E | C | G
priority order (LRU) | 0 (MRU) | A | B | C | D | C | D |  |  | 
 | 1 |  | A | B | C | D | C |  |  | 
 | 2 |  |  | A | B | B | B |  |  | 
 | 3 (LRU) |  |  |  | A | A | A |  |  | 
cache miss |  | m | m | m | m | h | h |  |  | 
LRU to be replaced for E
Cache configuration:
  Size: 4 blocks
  Mapping: fully-associative
  Replacement: LRU
Mem access sequence: (each character indicates a block address)
  ABCDCDECG

## Slide 45: LRU Example
Accesses |  | A | B | C | D | C | D | E | C | G
priority order (LRU) | 0 (MRU) | A | B | C | D | C | D | E |  | 
 | 1 |  | A | B | C | D | C | D |  | 
 | 2 |  |  | A | B | B | B | C |  | 
 | 3 (LRU) |  |  |  | A | A | A | B |  | 
cache miss |  | m | m | m | m | h | h | m |  | 
Cache configuration:
  Size: 4 blocks
  Mapping: fully-associative
  Replacement: LRU
Mem access sequence: (each character indicates a block address)
  ABCDCDECG

## Slide 46: LRU Example
Accesses |  | A | B | C | D | C | D | E | C | G
priority order (LRU) | 0 (MRU) | A | B | C | D | C | D | E | C | 
 | 1 |  | A | B | C | D | C | D | E | 
 | 2 |  |  | A | B | B | B | C | D | 
 | 3 (LRU) |  |  |  | A | A | A | B | B | 
cache miss |  | m | m | m | m | h | h | m | h | 
LRU to be
replaced for G
Cache configuration:
  Size: 4 blocks
  Mapping: fully-associative
  Replacement: LRU
Mem access sequence: (each character indicates a block address)
  ABCDCDECG

## Slide 47: LRU Example
Accesses |  | A | B | C | D | C | D | E | C | G
priority order (LRU) | 0 (MRU) | A | B | C | D | C | D | E | C | G
 | 1 |  | A | B | C | D | C | D | E | C
 | 2 |  |  | A | B | B | B | C | D | E
 | 3 (LRU) |  |  |  | A | A | A | B | B | D
cache miss |  | m | m | m | m | h | h | m | h | m
Cache configuration:
  Size: 4 blocks
  Mapping: fully-associative
  Replacement: LRU
Mem access sequence: (each character indicates a block address)
  ABCDCDECG

## Slide 48: Cache Policies
Read policies:
  Read Hit: this is what we want
  Read Miss: replacement policy
Write policies (L1D only): consistency issues & performance tradeoffs
  Write-through vs. write-back vs. write-evict (no-write)
    also slightly different between write hit and write miss
  Write Hit: write policy
  Write Miss: write allocation policies (2 policies to categorize 3 write policies) + replacement policy

## Slide 49: Cache Write Policy
Write-through: consistent with lower level
  The value is written to both the cache line and the lower-level memory.
    No need to write a full block
  Write buffer can be used so cache does not need to wait for the write to lower level
    stall only if the write buffer is full
  Example: assume cache block containing word address A is initially in the cache
A
A
SW to A
A
A

## Slide 50: Cache Write Policy
A
A
A
Write-through: consistent with lower level
  The value is written to both the cache line and the lower-level memory.
    No need to write a full block
  Write buffer can be used so cache does not need to wait for the write to lower level
    stall only if the write buffer is full
  Example: assume cache block containing word address A is initially in the cache

## Slide 51: Cache Write Policy
Write-back: inconsistent with lower level
  The value is written only to the cache line. The modified (dirty) cache line is written to main memory only when it is evicted.
    1 dirty bit is needed for each cache line.
  A write-back buffer to update lower level with evicted dirty blocks
    Must write a full block at this point since we do not know which word is modified
  Example: assume cache block containing word address A is initially in the cache
A
A
SW to A
A
B
dirty bit (A) = 1
dirty bit (A) = 0

## Slide 52: Cache Write Policy
A
LW B
A
B
A few cycles later...
L1 is full and A is selected to be replaced by B
dirty bit (A) = 1
Write-back: inconsistent with lower level
  The value is written only to the cache line. The modified (dirty) cache line is written to main memory only when it is evicted.
    1 dirty bit is needed for each cache line.
  A write-back buffer to update lower level with evicted dirty blocks
    Must write a full block at this point since we do not know which word is modified
  Example: assume cache block containing word address A is initially in the cache
If A was not modified (dirty bit = 0) when replaced, A is not updated to lower mem.

## Slide 53: Cache Write Policy
Write-evict (no-write/bypassing): no consistency issue
  The value is written only to the lower level.
  If the block containing the write address exists in the cache, evict it.
  The write only need to send the data specified by the store instruction.
  A write buffer can also be used to reduce the delay.

## Slide 54: Cache Policies
Read policies:
  Read Hit: this is what we want
  Read Miss: replacement policy
Write policies: consistency issues & performance tradeoffs
  Write-through vs. write-back vs. write-evict (no-write)
    also slightly different between write hit and write miss
  Write Hit: write policy
  Write Miss: write allocation policy (+ replacement policy)
+ write policy of evicted data
+ write policy of evicted data

## Slide 55: Cache Write Policy
Read miss:
  Write-through: find victim block + fetch block from lower level
  write-back: find victim block + write back evicted block if dirty + fetch block from lower level
  No-write: find victim block + fetch block from lower level
Write miss: write allocation policies
  Write-allocate:
    Write-through: find victim block + fetch block from lower level + store value to block and lower level
    write-back: find victim block + write back evicted block if dirty + fetch block from lower level + store value to block
  No-write-allocate: bypass the cache, store value to lower level directly
Write hit and write miss can use different policies
  e.g., write-hit write-evict + write-miss write-allocate-write-back

## Slide 56: Reduce Miss Rate (1): Code Optimization
Misses occur if sequentially accessed array elements come from different cache blocks
Code optimizations  No hardware change
  Rely on programmers or compilers
Examples:
  Loop interchange: In nested loops, outer loop becomes inner loop and vice versa
  Loop blocking: partition large array into smaller blocks, thus fitting the accessed array elements into cache size

## Slide 57: Loop Interchange
/* Before */
for (j=0; j<5; j++)
for (i=0; i<5; i++)
x[i][j] = 2*x[i][j]
/* After */
for (i=0; i<5; i++)
for (j=0; j<5; j++)
x[i][j] = 2*x[i][j]
Column-major ordering
Row-major ordering
i
j
i
j
each loop iteration accesses different cache line
The same cache line is accessed for a couple of iterations
Assume: cache line size = 5 words
What addresses are accessed in each iteration of inner loop?
five consecutive words belong to a cache line

## Slide 58: Loop Blocking
X
=
/* Before */
for (i=0; i<N; i++)
for (j=0; j<N; j++)
for (k=0; k<N; k++)
C[i][j] = C[i][j] + A[i][k] * B[k][j];
In the traditional matrix multiplication:
To generate one output element (red color), the 6 elements of each input matrix (gray color) will be accessed.

## Slide 59
X
=
Loop Blocking
/* Before */
for (i=0; i<N; i++)
for (j=0; j<N; j++)
for (k=0; k<N; k++)
C[i][j] = C[i][j] + A[i][k] * B[k][j];
In the traditional matrix multiplication:
To generate one output element (red color), the 6 elements of each input matrix (gray color) will be accessed.

## Slide 60: Loop Blocking
X
=
/* Before */
for (i=0; i<N; i++)
for (j=0; j<N; j++)
for (k=0; k<N; k++)
C[i][j] = C[i][j] + A[i][k] * B[k][j];
In the traditional matrix multiplication:
To generate one output element (red color), the 6 elements of each input matrix (gray color) will be accessed.

## Slide 61: Loop Blocking
X
=
/* Before */
for (i=0; i<N; i++)
for (j=0; j<N; j++)
for (k=0; k<N; k++)
C[i][j] = C[i][j] + A[i][k] * B[k][j];
In the traditional matrix multiplication:
To generate one output element (red color), the 6 elements of each input matrix (gray color) will be accessed.

## Slide 62: Loop Blocking
X
=
/* Before */
for (i=0; i<N; i++)
for (j=0; j<N; j++)
for (k=0; k<N; k++)
C[i][j] = C[i][j] + A[i][k] * B[k][j];
To generate one output element (red color), the 6 elements of each input matrix (gray color) will be accessed.
In the traditional matrix multiplication:

## Slide 63: Loop Blocking
X
=
/* Before */
for (i=0; i<N; i++)
for (j=0; j<N; j++)
for (k=0; k<N; k++)
C[i][j] = C[i][j] + A[i][k] * B[k][j];
The second matrix may always encounter misses because individual data are from different cache blocks
In the traditional matrix multiplication:
To generate one output element (red color), the 6 elements of each input matrix (gray color) will be accessed.

## Slide 64: Loop Blocking
X
=
/* Before */
for (i=0; i<N; i++)
for (j=0; j<N; j++)
for (k=0; k<N; k++)
C[i][j] = C[i][j] + A[i][k] * B[k][j];
If N is large, the cache line that has been accessed is likely to be replaced before next access
In the traditional matrix multiplication:
To generate one output element (red color), the 6 elements of each input matrix (gray color) will be accessed.

## Slide 65: Loop Blocking
X
=
/* After (block size = 4) */
for (i=0; i<N; i=i+b)
for (j=0; j<N; j=j+b)
for (k=0; k<N; k=k+b)
for (ii=i; ii<i+b; ii++)
for (jj=j; jj<j+b; jj++)
for (kk=k; kk<k+b; kk++)
C[ii][jj] = C[ii][jj] + A[ii][kk] * B[kk][jj];
Matrix is computed in a smaller block unit
 higher locality
In the block-based matrix multiplication:

## Slide 66: Loop Blocking
X
=
/* After (block size = 4) */
for (i=0; i<N; i=i+b)
for (j=0; j<N; j=j+b)
for (k=0; k<N; k=k+b)
for (ii=i; ii<i+b; ii++)
for (jj=j; jj<j+b; jj++)
for (kk=k; kk<k+b; kk++)
C[ii][jj] = C[ii][jj] + A[ii][kk] * B[kk][jj];
In the block-based matrix multiplication:

## Slide 67: Loop Blocking
X
=
/* After (block size = 4) */
for (i=0; i<N; i=i+b)
for (j=0; j<N; j=j+b)
for (k=0; k<N; k=k+b)
for (ii=i; ii<i+b; ii++)
for (jj=j; jj<j+b; jj++)
for (kk=k; kk<k+b; kk++)
C[ii][jj] = C[ii][jj] + A[ii][kk] * B[kk][jj];
In the block-based matrix multiplication:

## Slide 68: Loop Blocking
X
=
/* After (block size = 4) */
for (i=0; i<N; i=i+b)
for (j=0; j<N; j=j+b)
for (k=0; k<N; k=k+b)
for (ii=i; ii<i+b; ii++)
for (jj=j; jj<j+b; jj++)
for (kk=k; kk<k+b; kk++)
C[ii][jj] = C[ii][jj] + A[ii][kk] * B[kk][jj];
In the block-based matrix multiplication:

## Slide 69: Loop Blocking
X
=
/* After (block size = 4) */
for (i=0; i<N; i=i+b)
for (j=0; j<N; j=j+b)
for (k=0; k<N; k=k+b)
for (ii=i; ii<i+b; ii++)
for (jj=j; jj<j+b; jj++)
for (kk=k; kk<k+b; kk++)
C[ii][jj] = C[ii][jj] + A[ii][kk] * B[kk][jj];
In the block-based matrix multiplication:

## Slide 70: Loop Blocking
X
=
/* After (block size = 4) */
for (i=0; i<N; i=i+b)
for (j=0; j<N; j=j+b)
for (k=0; k<N; k=k+b)
for (ii=i; ii<i+b; ii++)
for (jj=j; jj<j+b; jj++)
for (kk=k; kk<k+b; kk++)
C[ii][jj] = C[ii][jj] + A[ii][kk] * B[kk][jj];
In the block-based matrix multiplication:

## Slide 71: Loop Blocking
X
=
/* After (block size = 4) */
for (i=0; i<N; i=i+b)
for (j=0; j<N; j=j+b)
for (k=0; k<N; k=k+b)
for (ii=i; ii<i+b; ii++)
for (jj=j; jj<j+b; jj++)
for (kk=k; kk<k+b; kk++)
C[ii][jj] = C[ii][jj] + A[ii][kk] * B[kk][jj];
In the block-based matrix multiplication:

## Slide 72: Reduce Miss Rate (2): Reduce the 3 C’s
Increase Cache Size
  Reduce miss for: capacity miss, conflict miss
  But has many limitations
Increase Associativity
  Reduce miss for: conflict miss
  But may increase access latency
Increase Cache Block Size
  Reduce miss for: compulsory
  But may increase miss penalty (more data will be evicted and fetched)
  Very large blocks could increase miss rate

## Slide 73
Miss Rate vs Block Size vs Cache Size
Chart: Block size (bytes)
| 16 | 32 | 64 | 128 | 256
8 KB | 8.5 | 7.5 | 7.25 | 7.75 | 9.5
16 KB | 4 | 2.75 | 2.75 | 3 | 3.5
64 KB | 2 | 1.7 | 1.55 | 1.4 | 1.4
256 KB | 1 | 0.7 | 0.5 | 0.5 | 0.6
Cache size – the larger the better
Block size – tradeoffs

## Slide 74
Miss
Penalty
Block Size
Miss
Rate
Exploits Spatial Locality
Fewer blocks -- increases capacity misses
Block Size
Average
Access
Time
Increased Miss Penalty
& Miss Rate
Block Size
Average Memory Access Time = Hit Time + Miss Penalty x Miss Rate
Block Size Tradeoff

## Slide 75
Benefits of Set Associative Caches
Data from Hennessy & Patterson, Computer Architecture
Largest gains when going from direct mapped to 2-way (20%+ reduction in miss rate)

## Slide 76: Reduce Miss Rate (3): Policies
Use appropriate policies
  LRU + write-back works for most applications
  Many GPUs use write-hit write-evict + write-miss no-write-allocate
  Can even dynamically change policy according to profiling
Use more advanced policies
  E.g., ML based

## Slide 77: Reduce Miss Rate (4): Multi-level Caches
Having a unified L2 cache (i.e., it holds both instructions and data) and in some cases even a unified L3 cache
L1 cache should focus on minimizing hit time in support of a shorter clock cycle
Secondary cache(s) should focus on reducing miss rate to reduce the penalty of long main memory access times

## Slide 78: Split vs. Unified Caches
Split L1I$ and L1D$: to optimize thit
  Low capacity/associativity/block size (reduce thit)
  Minimize structural hazards
  Can optimize L1I$ for wide output and no writes
Unified L2: to optimize hit rate
  thit is less important due to less frequent accesses & long delay already
  High capacity/associativity/block size (reduce %miss)
    Unused instr capacity can be used for data (fewer capacity misses)
    Instr / data conflicts (small to no increase for conflict misses in a large cache)
  Instr / data structural hazards are rare (would take a simultaneous L1I$ and L1D$ miss)

## Slide 79: Reduce Miss Rate (5): Prefetching
Hardware prefetching
  Fetch blocks into the cache proactively (speculatively)
  Key is to anticipate the upcoming miss addresses accurately
  Relies on having unused memory bandwidth available
A simple case is to use next block prefetching
  Miss on address X → anticipate next reference miss on X + block-size
  Works well for instr’s (sequential execution) and for arrays of data
Need to initiate prefetches sufficiently in advance
If prefetched instr/data is not used, the cache is polluted with unnecessary data (possibly evicting useful data)

## Slide 80: Measuring Performance with Caches
Assuming cache hit costs are included as part of the normal CPU execution cycle, then
  CPU time = IC × CPI × CP
  = IC × (CPIideal + Memory-stall cycles) × CP
CPIstall
Memory-stall cycles come from cache misses (a sum of read-stalls and write-stalls)
  Read-stall cycles = read miss ratio × read miss penalty
  Write-stall cycles = write miss ratio × write miss penalty + write buffer stalls
For write-through caches, we can simplify this to
  Memory-stall cycles = miss ratio × miss penalty
Note: this is miss ratio with regard to all instructions
= read ratio * cache miss rate

## Slide 81: Impacts of Cache Performance
Relative cache penalty increases as processor performance improves (faster clock rate and/or lower CPI)
  The memory speed is unlikely to improve as fast as processor cycle time. When calculating CPIstall, the cache miss penalty is measured in processor clock cycles needed to handle a miss
  The lower the CPIideal, the higher the impact of stalls
Example: A processor with a CPIideal of 2, a 100 cycle miss penalty, 36% load/store instructions, and 2% I$ and 4% D$ miss rates
  Memory-stall cycles = 2% × 100 + 36% × 4% × 100 = 3.44
  CPIstalls = 2 + 3.44 = 5.44
What if the CPIideal is reduced to 1? Or the processor clock rate is doubled (doubling the miss penalty)?

## Slide 82: Other than Miss Rates
Cache bypassing (e.g., L1D)
  Reduce latency if L1 misses
Sector cache
  Fetch only a portion of the cache line
  Not the same as reducing cache line size
Value prediction
  Using history value to predict future values
  Roll back if predict wrong
  Or accept a certain quality loss if the application is error tolerant

## Slide 83: DRAM Subsystem Organization
  Dram: Dynamic RAM
DRAM Organization:
Channel
DIMM
Rank
Chip
Bank
Row/Column
Connected to an on-die memory controller

## Slide 84: DRAM Cells
A DRAM cell consists of a capacitor and an access transistor
It stores data in terms of charge in the capacitor
Cheaper and larger than SRAM
  A DRAM chip consists of (10s of 1000s of) rows of such cells
wordline
bitline
bitline
bitline
(row enable)
row
column
column
column

## Slide 85: DRAM Refresh
DRAM capacitor charge leaks over time
The memory controller needs to refresh each row periodically to restore charge
  Dynamic (i.e., never in a stable state)
  Activate each row every N ms (e.g., typical N = 64 ms)
Downsides of refresh
  Energy consumption: Each refresh consumes energy
  Performance degradation: DRAM rank/bank unavailable while refreshed
  QoS/predictability impact: (Long) pause times during refresh
  Refresh rate limits DRAM capacity scaling

## Slide 86
data bit
data bit
r
o
w
d
e
c
o
d
e
r
row
Address
(RAS)
Column Selector &
I/O Circuits
column
Address
(CAS)
data bit
bit (data) lines
Each intersection represents a 1-T DRAM cell
The column address selects the requested bit from the row in each plane
data word
. . .
. . .
DRAM Cell Array
word (row) select line
m planes
DRAM Design 1: The Classical
DRAM Bank

## Slide 87
DRAM addresses are divided into 2 halves (row and column)
  RAS or Row Access Strobe that triggers the row decoder
  CAS or Column Access Strobe that triggers the column selector
Latency: Time to access one word
  Access Time: time between request and when word is read or written
    read access and write access times can be different
  Cycle Time: time between successive (read or write) requests
  Usually, cycle time > access time
Bandwidth: How much data can be supplied per unit time
  Width of the data channel * channel usage frequency
DRAM Performance Metrics

## Slide 88
DRAM addresses are divided into 2 halves (row and column)
  RAS or Row Access Strobe that triggers the row decoder
  CAS or Column Access Strobe that triggers the column selector
Latency: Time to access one word
  Access Time: time between request and when word is read or written
    read access and write access times can be different
  Cycle Time: time between successive (read or write) requests
  Usually, cycle time > access time
Bandwidth: How much data can be supplied per unit time
  Width of the data channel * channel usage frequency
DRAM Performance Metrics

## Slide 89
DRAM Organization:
  N rows x N column x M-bit (planes)
  Reads or Writes M-bit at a time
  Each M-bit access requires a RAS / CAS cycle
Row Address
CAS
RAS
Col Address
Row Address
Col Address
Access Time
Cycle Time
1st M-bit
2nd M-bit
DRAM Design 1: The Classical

## Slide 90
Row Address
CAS
RAS
Col Address
Col Address
1st M-bit
Col Address
Col Address
2nd M-bit
3rd M-bit
4th M-bit
Cycle Time
Page Mode: A row is kept “open” by keeping the RAS asserted
  Pulse CAS to access other M-bit blocks on that row
  Successive reads or writes within the row are faster since don’t have to precharge and (re)access that row
DRAM Design 1: The Classical

## Slide 91: DRAM Design 2: Synchronous DRAMs
Like page mode DRAMs, synchronous DRAMs (SDRAMs) can transfer a burst of data from a series of sequential addresses in the same row
For words in the same burst, don’t have to provide the complete (row and column) addresses
  Specify the starting (row+column) address and the burst length (burst must be in the same row). The row is accessed from the DRAM and loaded into a row buffer (SRAM).
  Data words in the burst are then accessed from that SRAM under control of a clock signal.

## Slide 92
Row Address
CAS
RAS
Col Address
1st
M-bit
http://en.wikipedia.org/wiki/DDR_SDRAM
2nd
M-bit
3rd
M-bit
clock
Synchronous DRAM (SDRAM) Operation
After RAS loads a row into the SRAM cache
  Input CAS as the starting “burst” address along with a burst length to read a burst of data from a series of sequential addresses within that row on the clock edge
…

## Slide 93
Row Address
CAS
RAS
Col Address
1st
M-bit
Row Address
http://en.wikipedia.org/wiki/DDR_SDRAM
2nd
M-bit
3rd
M-bit
4th
M-bit
clock
DDR (Double Data Rate) SDRAMs
Transfers burst data on both the rising and falling edge of the clock (so twice fast)
  2n core prefectch

## Slide 94
DDR (Double Data Rate) SDRAMs
DDR1 VS DDR1+:
DDR2 vs. QDR

## Slide 95: DRAM Subsystem Organization
  Dram: Dynamic RAM
DRAM Organization:
Channel
DIMM
Rank
Chip
Bank
Row/Column
Chip:
  Consists of multiple banks (2-16 in Synchronous DRAM)
    Banks works in parallel to overlap delay
  Banks share command/address/data buses
  The chip itself has a narrow interface (4-16 bits per read)

## Slide 96: DRAM Subsystem Organization
  Dram: Dynamic RAM
DRAM Organization:
Channel
DIMM
Rank
Chip
Bank
Row/Column
Rank:
  Multiple chips operated together to form a wide interface
  All chips comprising a rank are controlled at the same time
    Respond to a single command
    Share address and command buses, but provide different data
  E.g., Using 8 chips with 8-bit interface to form a 64-bit wide Rank

## Slide 97: DRAM Subsystem Organization
  Dram: Dynamic RAM
DRAM Organization:
Channel
DIMM
Rank
Chip
Bank
Row/Column
DIMM (dual inline memory module):
  A DRAM module consists of one or more ranks
  This is what you plug into your motherboard

## Slide 98: DIMM (Dual Inline Memory Module)
Contains DRAM chips each have data widths of x4 or x8
  Can be on both sides
Can have more than one rank
  Increase storage capacity
  Only one rank accessible at a time
SIMM vs DIMM
  DIMM has separate contacts on each side of the board to provides twice as much data rate.

## Slide 99: A 64-bit Wide DIMM (One Rank)
Advantages:
  Acts like a high-capacity DRAM chip with a wide interface
  Flexibility: memory controller does not need to deal with individual chips
Disadvantages:
  Granularity: Accesses cannot be smaller than the interface width

## Slide 100: DRAM Subsystem Organization
  Dram: Dynamic RAM
DRAM Organization:
Channel
DIMM
Rank
Chip
Bank
Row/Column
Channel: Independent memory subsystem
  E.g., 2 independent Channels:

## Slide 101: The DRAM subsystem
Memory channel
Memory channel
DIMM (Dual in-line memory module)
Processor
“Channel”
Each channel is connected to its own on-die memory controller

## Slide 102
Row Buffer
(Row 0, Column 0)
Row decoder
Column mux
Row address 0
Column address 0
Data
Row 0
Empty
(Row 0, Column 1)
Column address 1
(Row 1, Column 0)
HIT
Row address 1
Row 1
Column address 0
CONFLICT !
Columns
Rows
Access Address: Row Operation:
R0
R0
R1
Activation
Restore, Precharge, Activation
No operation
RBL=2
RBL=1
Credit: Onur Mutlu.
Row Operations & Row Buffer Locality
Improving Row Buffer Locality (RBL) is the key to reduce DRAM energy consumption

## Slide 103
……
Activation Counter:
R1: Activation = 1
R5: Activation = 2
R1: Activation = 3
R5: Activation = 4
R5: Activation = 4
Avg RBL = 5 / 4 = 1.25
……
requests currently
in the pending queue
oldest
request
R1
R5
R1
R5
future
requests
R2
R4
R3
In-order scheduling
(FIFO):
Request Stream
R5
……
Activation Counter:
R1: Activation = 1
R1: Activation = 1
R5: Activation = 2
R5: Activation = 2
R5: Activation = 2
Avg RBL = 5 / 2 = 2.5
……
requests currently
in the pending queue
oldest
request
R1
R5
R1
R5
future
requests
R2
R4
R3
Out-of-order scheduling
(FR-FCFS):
Request Stream
R5
Visible to the memory scheduler
Same
activation
Same
activation
Same
activation
RBL & Memory Scheduling Schemes

## Slide 104: DRAM Milestones
In the time that the memory to processor bandwidth has more than doubled the memory latency has improved by a factor of only 1.2 to 1.4
To deliver such high bandwidth, the internal DRAM has to be organized as interleaved memory banks
 | DRAM | Page DRAM | Page DRAM | Page DRAM | SDRAM | DDR SDRAM
Module Width | 16b | 16b | 32b | 64b | 64b | 64b
Year | 1980 | 1983 | 1986 | 1993 | 1997 | 2000
Mb/chip | 0.06 | 0.25 | 1 | 16 | 64 | 256
Die size (mm2) | 35 | 45 | 70 | 130 | 170 | 204
Pins/chip | 16 | 16 | 18 | 20 | 54 | 66
BWidth (MB/s) | 13 | 40 | 160 | 267 | 640 | 1600
Latency (nsec) | 225 | 170 | 125 | 75 | 62 | 52
Patterson, CACM Vol 47, #10, 2004

## Slide 105: Memory (DRAM) + Caches
It is important to match the cache characteristics
  Caches want information provided to them one block at a time (and a block is usually more than one word)
Memory design considerations:
  With the main memory characteristics
    Use DRAMs that support fast multiple word accesses, preferably ones that match the block size of the cache
  With the memory-bus characteristics
    Make sure the memory-bus can support the DRAM access rates and patterns
    With the goal of increasing the Memory-Bus-to-Cache bandwidth

## Slide 106: Review: DRAM vs. SRAM
DRAM
  Slower access (capacitor)
  Higher density (1T 1C cell)
  Lower cost
  Requires refresh (power, performance, circuitry)
  Manufacturing requires putting capacitor and logic together
SRAM
  Faster access (no capacitor)
  Lower density (6T cell)
  Higher cost
  No need for refresh
  Manufacturing compatible with logic process (no capacitor)

## Slide 107
Purpose: Long term, nonvolatile storage
  Lowest level in the memory hierarchy: large, cheap, slow
General structure
  1 to 4 rotating platter coated with a magnetic surface (2 sides recordable)
    Rotational speeds of 5,400 to 15,000 RPM
  Moveable read/write head to access the information for each platter
  10,000 to 50,000 tracks per surface
    Cylinder - all the tracks under the head at a given point on all surfaces
  100 to 500 sectors per track
    The smallest unit that can be read/written (typically 512B)
    Outer tracks hold more sectors than the inner tracks
Magnetic Disk
Sector
Track
Cylinder
Head
Platter
Controller
+
Cache

## Slide 108
  Rotational latency: wait for the desired sector to rotate under the head
    ½ of 1/RPM converted to ms: 0.5R/5400RPM = 5.6ms to 0.5R/15000RPM = 2.0ms
  Transfer time: transfer a block of bits (one or more sectors) under the head to the disk controller’s cache (70 to 125 MB/s are typical disk transfer rates)
    the disk controller’s “cache” takes advantage of spatial locality in disk accesses
    cache transfer rates are much faster (e.g., 375 MB/s)
  Controller time: the overhead the disk controller imposes in performing a disk I/O access (typically < 0.2 ms)
Sector
Track
Cylinder
Head
Platter
Controller
+
Cache
Magnetic Disk Characteristic
  Seek time: position the head over the proper track
    3 to 12/15 ms on average
    Due to locality of disk references, the actual average seek time may be only 25% to 33% of the advertised number

## Slide 109: Typical Disk Access Time
  If the measured average seek time is 25% of the advertised average seek time, then
Avg disk read/write
= 4.0 ms + 0.5/(15,000RPM/(60sec/min)) + 0.5KB/(100MB/sec) + 0.2 ms
= 4.0 + 2.0 + 0.005 + 0.2 = 6.2 ms
Avg disk read/write = 1.0 + 2.0 + 0.005 + 0.2 = 3.2 ms
The average time to read or write a 512B sector for a disk rotating at 15,000 RPM with average seek time of 4 ms, a 100MB/sec transfer rate, and a 0.2 ms controller overhead

## Slide 110: Disk Latency & Bandwidth Improvement
Disk latency = average seek time + rotational latency.
Disk bandwidth is the peak transfer speed of formatted data from the media (not from the cache).
Patterson, CACM Vol 47, #10, 2004
Chart: Year of Introduction
| 1983 | 1990 | 1994 | 1998 | 2003
Bandwidth (MB/s) | 0.6 | 4 | 9 | 24 | 86
Latency (msec) | 48.3 | 17.1 | 12.7 | 8.8 | 5.7

## Slide 111: Flash Storage
Flash memory is the first credible challenger to disks. It is semiconductor memory that is nonvolatile like disks but has latency 100 to 1000 times lower and is smaller, more power efficient, and more shock resistant.
  Flash memory bits wear out. But with wear leveling it is unlikely that the write limits of the flash will be exceeded.
  Example:
Storage | Write throughput | Read throughput | Latency
SSD | 2,500 MB/S | 3,500 MB/S | 0.025 ms
DISK | 250 MB/S | 250 MB/S | 5 ms

## Slide 112
Flash memory is organized into blocks of pages
  page size 512B to 4KB, block size 32 to 128 pages (typical)
  “read” is page read
  “write” is block erase (~ 1 ms) followed by page write (and additional copying of other pages in that block)
Typically a type of Electrically Erasable PROGRAMMABLE Read-Only Memory (EEPROM)
Comes in two flavors: NOR Flash and NAND Flash
  NOR Flash is randomly addressable (Minimum access size 512 bytes)
  NAND Flash is less expensive (greater storage density) and is not randomly addressable (minimum access size 2048 bytes); so more popular
Flash Storage Characteristics

## Slide 113: Dependability, Reliability, Availability
Reliability – measured by the mean time to failure (MTTF). Service interruption is measured by mean time to repair (MTTR)
Availability – a measure of service accomplishment
  Availability = MTTF / (MTTF + MTTR)
To increase MTTF, either improve the quality of components or design the system to continue operating in the presence of faulty components
  Fault avoidance: preventing fault occurrence by construction
  Fault tolerance: using redundancy to correct or bypass faulty components (hardware)

## Slide 114
Arrays of independent physical disks working together as one logical disk
  Increase potential throughput by having many disk drives
    Data can be spread across multiple disk
    Multiple disk accesses can be made simultaneously for higher throughput
Reliability for the array is lower than for a single disk
Availability can be improved by adding redundant disks
  Lost information can be reconstructed from redundant information
  MTTR: mean time to repair is in the order of hours
  MTTF: mean time to failure of disks is tens of years
RAID: Redundant Array of Independent Disks
RAID Disk Array

## Slide 115
sec1
sec3
sec2
sec4
sec1,b0
sec1,b2
sec1,b1
sec1,b3
Assumes one stripe = four blocks
RAID: Level 0 (Striping, No Redundancy)
Multiple smaller disks as opposed to one big disk
  Multiple blocks can be accessed in parallel to increase the performance
  Works well for large data requests
E.g., a 4-disk system gives four times the throughput (R/W) of a 1-disk system
  Same cost as one big disk – assuming 4 small disks cost the same as one big disk
What if one disk fails?
  No redundancy, data is lost
  More likely to fail as the number of disks increases

## Slide 116
# redundant disks = # of data disks, so always two copies of the data
  Twice the cost of one big disk
  Writes are made to both sets of disks and have no speed improvement
  Reads can be 2 times faster
If a disk fails, the system just goes to the “mirror” for the data
redundant (check) data
sec1
sec3
sec2
sec4
sec1m
sec3m
sec2m
sec4m
RAID: Level 1 (Redundancy via Mirroring)

## Slide 117
Category | Level | Disks | Features
Striping | 0 | N | No fault tolerance
Mirroring, no striping | 1 | 2N | Expensive
Striping Rarely used | 2 3 | N + m N + 1 | Hamming code Parity disk
Block level Striping Parity | 4 5 6 | N + 1 N + 1 N + 2 | Parity disk Distributed parity Dual distributed parity
RAID: Design Choices
Parity: used for error detection
  E.g., data: 00001111, parity bit: 0
Hamming code: limited error correction
  Using multiple parity bits to locate 1 error bit

## Slide 118
registers  memory
  by compiler (or programmer)
registers  cache  main memory
  by the cache & memory controller hardware
main memory  external storage (flash, disk)
  Static: by the programmer with OS support (files)
  Dynamic: by the operating system (virtual memory)
    virtual address to physical address mapping
    assisted by the hardware (TLB, page tables)
How is the Hierarchy Managed?

## Slide 119
Virtual Address (VA)
Page offset
Virtual page number
31 30 . . . 12 11 . . . 0
Page offset
Physical page number
Physical Address (PA)
29 . . . 12 11 0
Translation
A virtual address must first be translated to a physical address to access memory
  Basic unit: page (e.g., 1KB to 64KB)
Virtual memory size can be larger than physical memory size
  Pages can be stored in the secondary storage
Virtual Memory

## Slide 120: Address Space Isolation
Program 1 page table
Main (physical) memory
Program 2 page table
Allows efficient and safe sharing of main memory among multiple processes
  The starting location of each page is contained in the program’s page table
  Create the illusion that each program has a large consecutive memory space
  Improving memory utilization: code can be loaded anywhere the OS can find space
Virtual address space

## Slide 121: Address Translation Mechanisms
Physical page
base addr
Main memory
Disk storage
Virtual page #
V
1
1
1
1
1
1
0
1
0
1
0
Page Table (in main memory)
Offset
Physical page #
Offset
Page table register
virtual address
physical address
Page walk: Search (walk) the page table
Page fault: a DRAM miss for the page
 Page in disk

## Slide 122: Virtual Addressing with a Cache
It takes an extra memory access to translate a VA to a PA
CPU
Trans-
lation
Cache
Main
Memory
VA
PA
miss
hit
data
This makes memory (cache) accesses very expensive
The hardware solution is to use a Translation Lookaside Buffer (TLB)
  A small cache that keeps track of recently used address mappings to avoid having to do a page table lookup in main memory

## Slide 123: Making Address Translation Fast
Physical page
base address
Main memory
Disk storage
Virtual page #
V
1
1
1
1
1
1
0
1
0
1
0
1
1
1
0
1
Tag
Physical page
base address
V
TLB
Page Table (in physical memory)
Page table register

## Slide 124: A TLB in the Memory Hierarchy
A TLB miss – is it a page fault or merely a TLB miss?
  If the page is loaded into main memory, then the TLB miss can be handled by loading the translation information from the page table into the TLB (10’s of cycles )
  If the page is not in main memory, then it’s a true page fault (1,000,000’s)
TLB misses are much more frequent than true page faults
CPU
TLB
Lookup
Cache
Main
Memory
VA
PA
miss
hit
data
Trans-
lation
hit
miss
¾ t
¼ t

## Slide 125: Why Not a Virtually Addressed Cache?
A virtually addressed cache would only require address translation on cache misses
data
CPU
Trans-
lation
Cache
Main
Memory
VA
hit
PA
Aliasing issue:
Two programs which are sharing data will have two different VA for the same PA
  Two copies of the data in cache and two entries in the TLB  coherence issues
  Must update all cache entries with the same physical address or the memory becomes inconsistent
No address space isolation: data can be corrupted

## Slide 126: Reducing Translation Time
Overlapping the cache access with the TLB access
  Higher bits for TLB; lower bits for cache.
Tag
Data
=
Tag
Data
=
Cache Hit
Desired word
VA Tag
PA
Tag
TLB Hit
2-way Set Associative Cache
Index
PA Tag
Block offset
Page offset
Virtual page #
Byte offset