## Slide 1: Lecture 5. Parallel Processing (1)
Haonan Wang
CMPE 200 Computer Architecture & Design

## Slide 2: Processor Performance Analysis
Performance = =
CPI = 1 is ideal
  But, practically not achievable due to hazards in pipelined architecture
Cycle Time is determined by
  The longest instruction execution time in single-cycle CPU
  The longest stage execution time in pipelined CPU
    If execution times of stages are well-balanced, the speedup of N-stage pipeline is N time
Decided by Microarchitecture design

## Slide 3: Can We Do Better?
Latency vs. throughput
Levels of Parallelism:
  Instruction-level Parallelism (ILP)
    Executing independent instructions (in one thread) in parallel
  Data-level Parallelism (DLP)
    Executing the same instruction on different data subsets
  Thread-level Parallelism (or Task-level Parallelism, TLP)
    Executing independent computing tasks in parallel (on same or different data)

## Slide 4: Instruction Level Parallelism (ILP)
Basic idea: Execute several instructions in parallel
Pipelining is one example
  But it can only push through at most 1 inst/cycle
How about multiple instruction/cycle?
  More complicated and more transistors/logic (e.g., superscalar)
Simple ILP recipe
  Read and decode a few instructions each cycle
  If instructions are independent, do them at the same time
  If not, do them one at a time

## Slide 5: Example-1: MIPS with Dual Issue
Issue an arithmetic and a memory instruction concurrently
  At most 2x speedup
8

## Slide 6: Example-2: Floating-point Pipeline
MIPS has separate pipeline for floating-point operations

## Slide 7: Issue Multiple Instructions
Static multiple issue
  Compiler groups instructions to be issued together
  Packages them into “issue slots”
  Compiler detects and avoids hazards
Dynamic multiple issue
  CPU examines instruction stream and chooses instructions to issue each cycle
  Compiler can help by reordering instructions
  CPU resolves hazards using advanced techniques at runtime

## Slide 8: 2-way Superscalar Example
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10 | CC11
ld.s $f0, 0($r1) | IF | ID | EXE | MEM | WB |  |  |  |  |  | 
ld.s $f1, 0($t2) |  | IF | ID | EXE | MEM | WB |  |  |  |  | 
subi $t3, $t3, 1 |  |  | IF | ID | EXE | MEM | WB |  |  |  | 
add.s $f2, $f1, $f0 |  |  | IF | ID | ID | FP1 | FP2 | FP3 | FP4 | FP5 | WB
addi $t1, $t1, 4 |  |  |  | IF | ID | EXE | MEM | WB |  |  | 
IF
ID
EX
ME
IF
ID
FP1
FP2
FP3
FP4
FP5
WB
Forwarding paths:
MEM  EX & FP1
WB  EX & FP1
Code
ld.s $f0, 0($t1)
ld.s $f1, 0($t2)
subi $t3, $t3, 1
add.s $f2, $f1, $f0
addi $t1, $t1, 4
ld.s : load single precision data to fp reg
st.s : store single precision data from fp reg
add.s : add two single precision fp data

## Slide 9: Enhance Compiler Scheduling Performance
Loop Unrolling: transforms an M-iteration loop to a M/N-iteration loop
  “Loop has been unrolled N times”
  Effectively decrease the number of branches from M to M/N
  If the loop is short (i.e. 4 iterations in this code), it can even be eliminated
for(i=0;i<100;i+=4){
a[i]*=2;
a[i+1]*=2;
a[i+2]*=2;
a[i+3]*=2;
}
for(i=0;i<100;i++)
a[i]*=2;

## Slide 10: More Aggressive Method?
Static pipelines can only exploit ILP exposed by the compiler
  Instructions are stalled in ID stage until they are hazard free
  Must search for the ILP across branches
Dynamic pipeline scheduling
  Allow out-of-order (OOO) execution to avoid stalls
  Keeps track of dependency (commit result to registers in order)
  Decoded instructions wait in queues for operands (stall only when queues are full)
Example
  lw $t0, 20($s2) addu $t1, $t0, $t2 sub $s2, $s4, $t3 slti $t0, $s2, 20
Why should sub wait for lw and addu?

## Slide 11: Dynamically Scheduled CPU
Results also sent to any waiting reservation stations
Reorders buffer for register writes
Can supply operands for issued instructions
Preserves dependencies
Hold pending operands

## Slide 12: Dynamic Pipeline Scheduling
Challenges
  All data hazards (memory and registers) must be resolved by hardware
Data Dependencies
  RAW (Read After Write) : True dependency
    Dynamic pipeline preserves only this dependency
  WAR (Write After Read) & WAW (Write After Write) : False dependencies
    Dynamic pipeline removes false dependencies by using register renaming

## Slide 13: Dependencies Among Instructions
lw $t0, 20($s2) addu $t1, $t0, $t2 sub $s2, $s4, $t3 slti $t0, $s2, 20
lw $t0, 20($s2) addu $t1, $t0, $t2 sub $s2, $s4, $t3 slti $t0, $s2, 20
lw $t0, 20($s2) addu $t1, $t0, $t2 sub $s2, $s4, $t3 slti $t0, $s2, 20
RAW
WAW
WAR
lw $t0, 20($s2) addu $t1, $t0, $t2 sub $s2, $s4, $t3 slti $t0, $s2, 20
P2
Preserve only RAW and remove false dependencies by renaming destination registers of each instruction
P3
P3
P1
P1
P4
lw P1, 20($s2) addu P2, P1, $t2 sub P3, $s4, $t3 slti P4, P3, 20
Now can sub execute before lw and addu?

## Slide 14: Dependencies Among Instructions
lw $t0, 20($s2) addu $t1, $t0, $t2 sub $s2, $s4, $t3 slti $t0, $s2, 20
P2
P3
P3
P1
P1
P4
lw P1, 20($s2) addu P2, P1, $t2 sub P3, $s4, $t3 slti P4, P3, 20
Logical | initial | lw | addu | sub | slti
l1 | t0 | P1 | P1 | P1 | P4
l2 | t1 | t1 | P2 | P2 | P2
l3 | t2 | t2 | t2 | t2 | t2
l4 | t3 | t3 | t3 | t3 | t3
l5 | s2 | s2 | s2 | P3 | P3
l6 | s4 | s4 | s4 | s4 | s4
initial | lw | addu | sub | slti
P1 | P2 | P3 | P4 | P5
P2 | P3 | P4 | P5 | …
P3 | P4 | P5 | … | 
P4 | P5 | … |  | 
P5 | … |  |  | 
Mapping table status
Free list status

## Slide 15: Recall Power Wall
With super-pipelining, super-scalar, and dynamic pipelining, CPU performance was easily increased alongside higher clock frequency until early 2000s
Power = Capacitive load x Voltage2 x Frequency
Solution: Add more cores with the same frequency instead (DLP & TLP)

## Slide 16
Programs: sequential or concurrent
  Sequential: only one activity during a period of time
  Concurrent: multiple independent or cooperating activities during a period, but not necessarily simultaneous (e.g., multithreading on 1 core)
Computers: serial or parallel
  Parallel: multiple instructions or multiple operations per cycle (ILP, DLP, TLP)
Key challenge: Scalability of programs
  Issues: scheduling, load balancing, synchronization, communication overhead
Concurrency vs. Parallelism

## Slide 17
Matrix addition
  matrix A, B, C; // dimensions m × n
  C = A + B;
  for (i = 0; i < m; i++) for (j = 0; j < n; j++) C[i][j] = A[i][j] + B[i][j];
Database search
  find an item with a given property by examining all items
Web search
  Google’s MapReduce algorithm
Concurrency and Parallelism Examples

## Slide 18: Conclusion Time
What is the key idea behind register renaming?
Prevent overwriting
What are the three levels of parallelism?
ILP, DLP, TLP