## Slide 1: Lecture 5. Parallel Processing (2)
Haonan Wang
CMPE 200 Computer Architecture & Design

## Slide 2: Multiprocessor
Parallelism in processor unit  Multiprocessor
  Multiple CPUs or Multiple Cores within a CPU
Two representative types:
  Shared-memory
  Message-passing
Platform variety: #cores, hierarchy, #memory controllers, interconnect, …
L1
L1
L1
L1
L2
L2
0
1
2
3
L1
L1
L1
L1
L3
L2
L1
L1
L2
L2
0
1
2
3
4
5
L1
L1
L1
L1
L3
L2
L2
L2
L2
3
2
1
0

## Slide 3
For power management, you can turn off whole cores, vary the core frequency (lower or higher), and run fewer threads.
Multicore Power Management
Power reduction modes
  Nap: optimal wakeup latency relative to power reduction
    Clocks turned off to the execution units, core frequency reduced, caches and TLB’s still active, remain coherent
  Sleep: optimal power reduction relative to wakeup latency
    Caches and TLB’s are purged, all clocks turned off, voltage lowered, some state info is retained

## Slide 4
Q1 – How do they share data?
Q2 – How do they coordinate?
Q3 – How scalable is the architecture? How many processors can be supported?
Multiprocessor Key Questions

## Slide 5
Q1 – How do they share data?
Q2 – How do they coordinate?
Q3 – How scalable is the architecture? How many processors can be supported?
Multiprocessor Key Questions

## Slide 6
Shared Memory multi-Processor (SMP)
  Single address space shared by all cores
  Cores coordinate/communicate through shared variables (via loads and stores)
    Need synchronization primitives (e.g., locks)
  Two styles
    Uniform memory access (UMA): easier for programming
    Non-uniform memory access (NUMA): more scalable & lower latency to local memory
Message Passing multi-Processor (MPP)
  Each core has its own private address space
    Cores share data by explicitly sending and receiving information (message passing)
  Coordination is built into MP primitives (message send & message receive)
How to Share Data?

## Slide 7: Shared Memory Model
Interconnection Network
Parallel programs communicate through shared memory
  E.g., processor A writes to an address, then processor B reads from the same address
Each read should receive the most up-to-date value
Memory
Mem[A] = 1
...
...
Read Mem[A]
A
cache
cache
Processor
A
Processor
B

## Slide 8: Shared Data Management
Processor
A
Processor
B
If multiple processors cache the same block in their private cache, how do they ensure they all see a consistent state?
Interconnection Network
cache
Memory
cache
A: 200
ld t1, 0[A]
t1 = 200
A: 200

## Slide 9: Shared Data Management
Processor
A
Processor
B
If multiple processors cache the same block in their private cache, how do they ensure they all see a consistent state?
Interconnection Network
cache
Memory
cache
A: 200
ld t5, 0[A]
t1 = 200
t5 = 200
A: 200
A: 200

## Slide 10: Shared Data Management
Processor
A
Processor
B
If multiple processors cache the same block in their private cache, how do they ensure they all see a consistent state?
Interconnection Network
cache
Memory
cache
A: 200
t1 = 200
t5 = 200
A: 200
A: 200
addi t1, t1, #200
st t1, 0[A]
t1 = 400
A: 400
Writeback cache updates memory only when the block is replaced

## Slide 11: Shared Data Management
Processor
A
Processor
B
If multiple processors cache the same block in their private cache, how do they ensure they all see a consistent state?
Interconnection Network
cache
Memory
cache
A: 200
t5 = 200
t6 = 200
A: 200
A: 200
t1 = 400
A: 400
ld t6, 0[A]
Processor B’s program expected to load the latest value, 400!

## Slide 12: A Coherent Memory System
Coherence: writes to the same location are seen in the same order by all cores (serialized)
Cache coherent multiprocessor: provide migration & replication
  Migration: data items are moved to local caches and used in a transparent fashion
    Reduces latency and the bandwidth demand on the shared memory
  Replication: simultaneous reads make copies of the data item in local caches
    Reduces both latency and contention for a read shared data item

## Slide 13: Cache Coherence Methods
Snooping-based protocol
  Each processor’s cache controller constantly snoops on the bus
  Processors observe other processors’ actions
    E.g., processor A makes “read-exclusive” request for A on bus, processor B sees this and invalidates its own copy of A
Interconnection Network
Memory
P
$
P
$
...
Snooper
P
$
P
$
Snooper
Snooper
Snooper
I’m going to modify block X
X
X
X
invalidate X
invalidate X

## Slide 14: Cache Coherence Methods
Directory-based protocol
  Directory tracks ownership (sharer set) for each block (who has what)
    A modified bit and multiple presence bits per cache block
  Directory coordinates invalidation appropriately
    E.g., processor A asks directory for “read-exclusive” copy, directory asks processor B to invalidate the requested copy, waits for ACK from processor B, then responds to processor A
Interconnection Network
Memory
P
$
P
$
P
$
P
$
...
Directory
Presence bits, one bit for each processor
Modified bit
X
X
X
I’m going to modify block X
Invalidate X
Done
Done
OK
0

## Slide 15: Write Invalidate (All Other Copies)
Can enforce write serialization
  Two processors attempt to write the same data at the same time  one of them wins the race  the other core’s copy is invalidated
  The other core must obtain a new copy of the data  must now contain the updated value
False sharing problem
  Two cores writes to two different variables in the same cache block  increases miss rate
  Compilers can help reduce this by allocating correlated data to the same cache block
A
B
Core1
Core2
4 word cache block

## Slide 16
Each core has its own private address space
  Cores share data by explicitly sending and receiving information (message passing)
Coordination is built into message passing primitives (message send and message receive)
Core
Core
Core
Cache
Cache
Cache
Interconnection Network
Memory
Memory
Memory
Message Passing multi-Processors (MPP)

## Slide 17: Pros and Cons of Message Passing
Cons:
  Performance
  Harder to port a sequential program to an MPP
    Every communication must be identified in advance
Pros:
  Easier for hardware design
  Communication is explicit, fewer “performance surprises”
    Message passing standard: MPI

## Slide 18
Q1 – How do they share data?
Q2 – How do they coordinate?
Q3 – How scalable is the architecture? How many processors can be supported?
Multiprocessor Key Questions

## Slide 19: SMP Example with 10 Cores
C0
C1
C2
C3
C4
C5
C6
C7
C8
C9
sum[C0]
sum[C1]
sum[C2]
sum[C3]
sum[C4]
sum[C5]
sum[C6]
sum[C7]
sum[C8]
sum[C9]
C0
C0
C1
C2
C3
C4
half = 10
half = 5
C1
half = 2
C0
half = 1
final sum

## Slide 20
We need to coordinate processes working on a common task
  Locks (e.g., spin locks, semaphores)
    Mutual exclusion: restrict data access to one core at a time
    Sequential ordering: must complete the first operation before starting the second
Need architectural support to implement the lock
  Arbitration mechanism
    Single bus provides an arbitration mechanism, since the bus is the only path to memory  the core that gets the bus wins
  Architecture-supported operation
    Atomic swap operation (e.g., ll and sc on MIPS) allows a core to both read a location and set it to the locked state (test-and-set) in the same bus operation
Process Synchronization

## Slide 21: Process Synchronization
sum[C0]
sum[C1]
sum[C2]
sum[C3]
sum[C4]
sum[C5]
sum[C6]
sum[C7]
sum[C8]
sum[C9]
C0
C1
C2
C3
C4
C5
C6
C7
C8
C9
C0
C1
C2
C3
C4
synch(): Cores must synchronize before the “consumer” core tries to read the results from the memory location written by the “producer” core
  Barrier synchronization: a synchronization scheme where cores wait at the barrier, not proceeding until every core has reached it

## Slide 22: MPP Example with 10 Cores
C0
C1
C2
C3
C4
C5
C6
C7
C8
C9
C0
C1
C2
C3
C4
half = 10
half = 5
half = 3
half = 2
sum
sum
sum
sum
sum
sum
sum
sum
sum
sum
send
receive
C0
C1
C2
limit = 10
limit = 5
limit = 3
limit = 2
half = 1
C0
C1
C0
send
receive
send
receive
send
receive

## Slide 23
Load balancing is important for multiprocessor performance
  E.g., a single core with twice the load of the others cuts the speedup almost in half
S = serial part, W = parallel part, N cores
  Time on 1 processor is S + W
Suppose the workload is equally distributed and there is no extra overhead to accumulate partial results
  Time on N processors is S + W/N
Suppose the workload is almost equally distributed (and still no overhead)
  One core does 2(W/N), one does nothing, most do W/N
   Time is S + max(2(W/N), 0, W/N) = S + 2(W/N) = S + W/(N/2)
Load Balancing

## Slide 24
Q1 – How do they share data?
Q2 – How do they coordinate?
Q3 – How scalable is the architecture? How many processors can be supported?
Multiprocessor Key Questions
 |  |  | # of Cores
Communication model | Message passing |  | 8 to 2048
 | SMP | NUMA | 8 to 256
 |  | UMA | 2 to 64
Physical connection | Network |  | 8 to 256
 | Bus |  | 2 to 36

## Slide 25: Conclusion Time
What is the difference between concurrency and parallelism?
Software implementation vs. hardware capability
What is the main difference between UMA and NUMA?
Memory access latency