## Slide 1: Lecture 5. Parallel Processing (3)
Haonan Wang
CMPE 200 Computer Architecture & Design

## Slide 2: Multi-core CPUs, Multiprocessors, and GPUs
Multi-core CPUs, Multiprocessors
  Individual cores are fine-tuned for high ILP
  Good for Task-level parallelism (TLP)
  However, it is hard to employ hundreds of cores in one system
    Cache coherence, control, power, cost …
For specific tasks, Graphics Processing Unit (GPU) can be an alternative solution
  For tasks with high Data-Level parallelism
  E.g., particle simulation, image/video processing, games, machine learning …
  The usage of GPU is common now
Instruction & Data level parallelism combinations
  SISD: Classical Von Neumann machine
  MISD: NA
  SIMD: GPU
  MIMD: multi-core & multiprocessor

## Slide 3: Isn’t GPU used for graphics processing?
Recent GPUs employ regular ALUs for programmable stages, which can be used for general purpose computing not only for the graphics applications
  GPGPU
  Programming language support: CUDA, OpenCL, …
GPU is efficient
  High performance
    hundreds of TFLOPS (floating point operations per second)
    CPU: hundreds of GFLOPS
  Energy/cost efficient by design
    Used in Top 500 Supercomputers in the world
https://commons.wikimedia.org/wiki/File:The_OpenGL_-_DirectX_graphics_pipeline.png

## Slide 4: GPU Scaling Trends
GTX 980
(Maxwell)
2048
CUDA
Cores
(224 GB/sec)
2014
GP 100
(Pascal)
3584
CUDA
Cores
(720 GB/sec)
2016
GV 100
(Volta)
5120
CUDA
Cores
(900 GB/sec)
2017
GTX 680
(Kepler)
1536
CUDA
Cores
(192 GB/sec)
2012
GTX 480
(Fermi)
448
CUDA
Cores
(139 GB/sec)
2010
GA 100
(Ampere)
8192
CUDA
Cores
(1555 GB/sec)
2020

## Slide 5: Why is GPU so Efficient?
GPU is specialized for compute-intensive, highly data parallel computation (owing to its graphics rendering origin)
  More transistors can be devoted to data processing rather than caching and control
  At peak performance GPU uses order of magnitude less energy per operation than CPU
  Working with suitable applications: high arithmetic intensity (the ratio between arithmetic operations and memory operations), high DLP, not too sensitive to latency
Credit: Dan Negrut, ME964 UW-Madison

## Slide 6: Classical GPGPU Architecture (Nvidia)
Warp Scheduler
Threads
Interconnect
…
…
L1 Caches
SM/Core
L1 Caches
PE
PE
…
L2 Cache
DRAM
Module
Memory Controller
L2 Cache
Memory Controller
L2 Cache
Memory Controller
DRAM
Module
DRAM
Module
Register File
Register File
SM/Core
PE
PE
…
Memory
Partition
W
W
W
W
W
W
warps
Row open:
Activation
Row close:
Restore & Precharge
Memory Array
Row Buffer
Warp contains 32 threads that execute the same instruction with different data - SIMD

## Slide 7: State-Of-The-Art GPU (Ampere)

## Slide 8: Working Philosophy (1): SIMD
GPU Shader
Image taken from the photo "Robin Jeffers at Ton House" (1927) by Edward Weston
0 | 0 | 0 | 0
64 | 64 | 64 | 0
128 | 192 | 192 | 0
192 | 192 | 128 | 64
Individual Pixels
(0 = black, 255 = white)

## Slide 9: Working Philosophy (1): SIMD
GPU Shader
0 | 0 | 0 | 0
64 | 64 | 64 | 0
128 | 192 | 192 | 0
192 | 192 | 128 | 64
Individual Pixels
(0 = black, 255 = white)
Image taken from the photo "Robin Jeffers at Ton House" (1927) by Edward Weston

## Slide 10: Working Philosophy (1): SIMD
0 | 0 | 0 | 0
64 | 64 | 64 | 0
128 | 192 | 192 | 0
192 | 192 | 128 | 64
Individual Pixels
+ Brightness
(0 = black, 255 = white)
0
0
0
0
64
64
64
0
128
192
192
0
192
192
128
64
+ 20 (brightness factor)
20
20
20
20
84
84
84
20
148
212
212
20
212
212
148
84
20 | 20 | 20 | 20
84 | 84 | 84 | 20
148 | 212 | 212 | 20
212 | 212 | 148 | 84
Image taken from the photo "Robin Jeffers at Ton House" (1927) by Edward Weston

## Slide 11: Working Philosophy (2): Hide Latency
W1
W2
W3
Computation
Waiting for Data from GPU Memory
GPU memory hierarchy provide high BW, but usually high latency
 Hide long memory latency with computation from other thread warps

## Slide 12: GPU Program Execution Flow
CPU
PCI-Express
System Memory
GPU
Global Memory
Host
Device
SM
...
Results
Execute a kernel in parallel
Application
Sequential Part
Parallel Part
Kernel with data

## Slide 13: GPU Program Execution Flow
CPU
PCI-Express
System Memory
GPU
Global Memory
Host
Device
SM
...
Results
Execute a kernel in parallel
Application
Sequential Part
Parallel Part
Sequential Part
Parallel Part
Sequential Part
Kernel with data

## Slide 14: CUDA Code Example: Vector Addition
C code
__global__ void vecAddCUDA (float* A, float* B, float* C){ // executed on the GPU
...
int i = threadIdx.x;
C[i] = A[i] + B[i];
}
int main(){ // executed on CPU
...
int numBlocks = 1;
int numThreads = 32;
vecAddCUDA <<<numBlock,numThreads>>>(A,B,C);
}
int main(){ // executed on CPU
...
for (int i=0; i<32; i++)
C[i] = A[i] + B[i];
}
CUDA C code

## Slide 15: Multicore Performance: Amdahl’s Law
Speedup due to enhancement E:
Speedup w/ E = ----------------------
Exec time w/o E
Exec time w/ E
ExTime w/ E = ExTime w/o E  ((1-F) + F/S)
Speedup w/ E = 1 / ((1-F) + F/S)
Suppose that enhancement E accelerates a fraction F (F <1) of the task by a factor S (S>1) and the remainder of the task is unaffected:

## Slide 16
Consider an enhancement that runs 20 times faster but is only usable 25% of the time
Speedup w/ E = 1/(.75 + .25/20) = 1.31
What if its usable only 15% of the time?
Speedup w/ E = 1/(.85 + .15/20) = 1.17
Amdahl’s Law tells us that to achieve linear speedup with 100 cores, none of the original computation can be scalar!
To get a speedup of 90 from 100 cores, the percentage of the original program that could be scalar would have to be 0.1% or less
  Speedup w/ E = 1/(.001 + .999/100) = 90.99
Example 1: Amdahl’s Law
Speedup w/ E = 1 / ((1-F) + F/S)

## Slide 17
Consider summing 10 scalar variables and two 10 by 10 matrices on 10 cores
Speedup w/ E = 1/(.091 + .909/10) = 1/0.1819 = 5.5
What if there are 100 cores?
Speedup w/ E = 1/(.091 + .909/100) = 1/0.10009 = 10.0
What if the matrices are 100 by 100 (or 10,010 adds in total) on 10 cores?
Speedup w/ E = 1/(.001 + .999/10) = 1/0.1009 = 9.9
What if there are 100 cores?
Speedup w/ E = 1/(.001 + .999/100) = 1/0.01099 = 91
Speedup w/ E = 1 / ((1-F) + F/S)
Example 2: Amdahl’s Law

## Slide 18
Consider summing 10 scalar variables and two 10 by 10 matrices on 10 cores
Speedup w/ E = 1/(.091 + .909/10) = 1/0.1819 = 5.5
What if there are 100 cores?
Speedup w/ E = 1/(.091 + .909/100) = 1/0.10009 = 10.0
What if the matrices are 100 by 100 (or 10,010 adds in total) on 10 cores?
Speedup w/ E = 1/(.001 + .999/10) = 1/0.1009 = 9.9
What if there are 100 cores?
Speedup w/ E = 1/(.001 + .999/100) = 1/0.01099 = 91
Speedup w/ E = 1 / ((1-F) + F/S)
Example 2: Amdahl’s Law

## Slide 19: Conclusion Time
What are the ways to do synchronization for multicore?
Barrier sync vs. MPP primitives
What are the key ideas of GPU?
SIMD & hiding latency